## Slide 1: STATICS (ENGINEERING MECHANICS-I)
Beams-Internal Effects
بسم الله الرحمن الرحيم
Notes: This is a title slide.

## Slide 2: Beams-Internal Effects
The design of any structural or mechanical member requires an investigation of both the external loads and reactions acting on the member and the loading acting within the member – in order to be sure the material can resist this loading.
How to determine the Internal Loadings:
  The internal loadings can be determined using the method of sections.
  The idea is to cut an imaginary section through the member so that the internal loadings (of interest) at the section become external on the free body diagram of the section.
  Use equations of equilibrium and find the required internal forces.

## Slide 3
5- 3
ENGINEERING MECHANICS : STATICS

## Slide 4: Internal forces
N: Normal force; V: Shear force; M: Bending moment.
If the member is subjected to a coplanar system of forces, only. N (Normal force), V (shear force) , and M (bending moment) act at the section.
Note: N will induce when applied loading is oblique.

## Slide 5
5- 5
ENGINEERING MECHANICS : STATICS

## Slide 6: Sign Convention
The directions shown for N, V and M are in a positive sense. The easy way to remember this sign convention is to isolate a small segment of the member and note that:
Positive normal force tends to elongate the segment.
Positive shear tends to rotate the segment clockwise.
Positive bending moment tends to bend the segment concave upward, so as to hold water.

## Slide 7: Effect of Bending and Shear

## Slide 8: Shear Force and Bending Moment in a Beam
5- 8
To determine bending moment and shearing force at any point in a beam subjected to concentrated and distributed loads.
Determine reactions at supports by treating whole beam as free-body.
Cut beam at C and draw free-body diagrams for AC and CB. By definition, positive sense for internal force-couple systems are as shown.
From equilibrium considerations, determine M and V or M’ and V’.

## Slide 9: Shear-force and Bending-moment diagrams
The variation of shear-force and bending moments plotted against distance along the beam give the shear-force and bending moment diagrams for the beam.

## Slide 10: Shear Force and Bending Moment Diagrams
5- 10
Variation of shear and bending moment along beam may be plotted.
Determine reactions at supports.
Cut beam at C and consider member AC,
Cut beam at E and consider member EB,
For a beam subjected to concentrated loads, shear force is constant between loading points and bending moment varies linearly.
+
+
+
_

## Slide 11: NOTE
The part of the beam which involves the smaller number of forces, either to the right or to the left of the arbitrary section, usually yields the simpler solution.
Avoid using a transverse section that coincides with the location of a concentrated load or couple, as such this position represents a point of discontinuity in the variation of shear or bending moment.

## Slide 12: Problem-1
Determine the shear and moment values in the simple beam at three sections: 1.5 m, 2.5 m and 4 m from the left support.
1 m
A
1 m
1 m
2 kN/m
2.8 kN.m
1 m
4 kN
B
1 m

## Slide 13: Solution
Reactions:
1 m
1 m
1 m
2 kN/m
2.8 kN.m
1 m
4 kN
B
1 m
A

## Slide 14: SF and BM calculations
2.8 kN.m
1.5
A
2 kN/m
2 m
2.8 kN.m
2.5
A

## Slide 15: SF and BM calculations
A
2 kN/m
1 m
1 m
2.8 kN.m
1 m
4 m
1 m
1 m
2.8 kN.m
1 m
4m
2 kN/m
BM is the same under the point load but SF changes from 0.36 kN to -3.64 kN.
4kN