## Slide 1: Analysis of Frames

## Slide 2: Two force members
A two-force member has forces applied at only two points on the member.
For any two-force member to be in equilibrium:
  The two forces acting on the member must have the same magnitude;
  Act in opposite directions; and
  Have the same line of action

## Slide 3: Multi-force members
A multi-force member has forces (and/or couple moments) applied at more than two points on the member.

## Slide 4: Frames and Machines
Frame or Machine: A structure is called a frame or machine if at least one of its individual members is a multi-force member.
Difference between Frame and Machine: Frames are structures which are designed to support applied loads and are usually fixed in position. Machines are structures which contain moving parts and are designed to transmit forces or couples from input values to output values.
In this course we will study only pin-connected frames.

## Slide 5: Frames and Machines (contd.)
This large crane is a typical example of a frame.
These pliers act as simple machines. Here the applied force on the handle creates a much larger force at the jaws.

## Slide 6: How to solve frame problems
The forces acting on each member of a frame are found by isolating its each member with a free-body diagram and applying the equations of equilibrium.
Free body diagram of a member is drawn by drawing its outlined shape and showing all the forces and/or couple moments that act on it.
The principle of action and reaction must be carefully observed when we represent the forces of interaction on the separate free-body diagrams.

## Slide 7: Analysis of Frames
6 - 7
Frames and machines are structures with at least one multiforce member. Frames are designed to support loads and are usually stationary (i.e. not moving). Machines contain moving parts and are designed to transmit and modify forces.
A free body diagram of the complete frame is used to determine the external forces acting on the frame.
Internal forces are determined by dismembering the frame and creating free-body diagrams for each component.
Forces between connected components are equal, have the same line of action and opposite sense.
Forces on two force members have known lines of action but unknown magnitude and sense.
Forces on multiforce members have unknown magnitude and line of action. They must be represented with two unknown components.
BE: two-force member

## Slide 8
http://web.mst.edu/~bestmech/statics/sa/sa/6_4_2_1.htm