## Slide 1: Exp #1 Glucose
Quantitative determination of glucose in serum or plasma

## Slide 2
Glucose is a major carbohydrate present in the peripheral blood . The oxidation of glucose is the major source of cellular energy in the body. Glucose determinations help to diagnose and treat the diabetes mellitus(D.M).
The blood glucose level is normally maintained within a narrow range under various conditions by hormones ,such as insulin, glucagon, or epinephrine.
Patients with diabetes demonstrate an inability to produce insulin.
Clinical diagnosis should not be made on a single test result.

## Slide 3: Clinical significant:
Elevated glucose associated with:
pancreatitis, pituitary or thyroid dysfunction, renal failure and liver disease
Low glucose associated with:
insulinoma, hypopituitarism , neoplasms, or insulin hypoglycemia

## Slide 4: Principle:
Glucose+O2+H2O Gluconic acid +H2O2
H2O2+4 aminoantipyrine +PHBS quinoneimine dye(red color) +4H2O
The quinoneimine dye has an absorption maximum at 510 nm. The amount of color produced is directly proportional to the glucose content of the sample
GOD
POD

## Slide 5
*GOD=glucose oxidase
*PHBS=p-hydroxybenzene sulfona
*POD=peroxidase
*Specimen:
Serum or plasma or CSF
Free of hemolysis or clot(glycolysis)
Stability: stable at 2-8 ºC for one day.

## Slide 6: Procedure:
1. Assays conditions:
Wavelength……………………..510 nm (490-550)
Cuvette…………………………….1 cm light path
Temperature…………………….37 ºc
2 .Adjust the instrument to zero with distilled water

## Slide 7
3. Pipette into a cuvette
4. Mix and incubate for 10 min at 37ºc
5. Read the absorbance (A).
* The color is stable for at least 30 min

## Slide 8: Calculation
(A)Sample x 100(std conc)= mg/dL
(A)standard
Conversion factor: mg/dL x 0.0555=mmol/L
Normal Range:
Fasting…………………70-105 mg/dL
Or ………………....3.9-5.8 mmol/L

## Slide 9: Limitaions:
The following substances reportedly cause decreased glucose values :
Ascorbic Acid when greater than 5 mg/dL
Hemoglobin when greater than 0.7 g/dL
Bilirubin when greater than 15 mg/dL
Uric Acid when greater than 2.0 mg/dL
Cysteine when greater than 10 mg/dL
others

## Slide 10
Fasting plasma glucose (FPG) versus oral glucose tolerance test (OGTT):
OGTT is performed by serial measurement of plasma glucose before and after a specific amount of glucose is given orally.
Although OGTT is more sensitive than FPG, it is affected by a large number of factors that result in poor reproducibility.
Therefore, an OGTT is rarely necessary for the diagnosis of DM.

## Slide 11
*Whole blood versus plasma glucose:
Most lab instruments measures plasma glucose, the results is more reliable .
It is 10-15% higher than whole blood glucose, since RBC contain less water per unit volume than plasma.
*Capillary versus venous plasma glucose:
There is little difference between them .
in hyperglycemia, capillary plasma glucose may be significantly higher than venous plasma glucose.

## Slide 12
Hemoglobin A1C (glycosylated Hemoglobin):
Whole blood sample used to monitor the degree of the control of blood glucose level during the past 2 months