## Slide 1
Example :
Draw the profiles of outside edge, inside edge, and center line for a two lanes highway of 24 ft. Assume that the cross-section is a known of 2% e= 5%, and 70 mph design speed .
Draw a cross-section for this highway at 70% of the length of runoff for the following cases:
- rotation about center line. - rotation about inside edge. - rotation about outside edge.

## Slide 2
Solution :-
From Table 7-5 For
Two lanes highway
e = 5 %
V = 70 mph
We get
Length of runoff = 150 ft
Length of runout = = 60 ft
Chart: 
| 0 | 60 | 120 | 180 | 270
Outer | -2 | -2 | 0 | 2 | 5
Column2 | 0 | 0 | 0 | 0 | 0
150 ft
5
Runout
2

## Slide 3
Chart: 
| 0 | 60 | 120 | 180 | 270
Outer | -0.24 | -0.24 | 0 | 0.24 | 0.6
Inner | -0.24 | -0.24 | -0.24 | -0.24 | -0.6
Center | 0 | 0 | 0 | 0 | 0
Rotation about Center
Runoff = 150 ft
Runout =60 ft

## Slide 4
Chart: 
| 0 | 60 | 120 | 180 | 270
Outer | -0.24 | -0.24 | 0 | 0.24 | 0.6
Inner | -0.24 | -0.24 | -0.24 | -0.24 | -0.6
Center | 0 | 0 | 0 | 0 | 0
Rotation about Center
Runoff = 150 ft
Runout =60 ft

## Slide 5
Chart: 
| -12 | 0 | 12
Surface | 0.42 | 0 | -0.42
Center | 0 | 0 | 0
Cross Section (Rotation about Center) at 70% of Runoff
12 ft
12 ft
3.5 %
3.5 %

## Slide 6
Chart: 
| 0 | 60 | 120 | 180 | 270
Outer | -0.24 | -0.24 | 0 | 0.24 | 0.6
Inner | -0.24 | -0.24 | -0.24 | -0.24 | -0.24
Center | 0 | 0 | 0 | 0 | 0.36
Rotation about Inner Edge
Runoff = 150 ft
Runout =60 ft
0.7 x 150 = 105 ft

## Slide 7
Chart: 
| -12 | 0 | 12
Surface | 0.84 | 0.3 | -0.24
Center | 0 | 0 | 0
Cross Section (Rotation about Inner) at 70% of Runoff
24 ft
3.5 %

## Slide 8
Chart: 
| 0 | 60 | 120 | 180 | 270
Outer | -0.24 | -0.24 | -0.24 | -0.24 | -0.24
Inner | -0.24 | -0.24 | -0.48 | -0.8 | -1.2
Center | 0 | 0 | -0.24 | -0.4 | -0.6
Rotation about Outer Edge
Runoff = 150 ft
Runout =60 ft

## Slide 9
Chart: 
| -12 | 0 | 12
Surface | -0.24 | -0.84 | -1.44
Center | 0 | 0 | 0
Cross Section (Rotation about Outer) at 70% of Runoff
24 ft
3.5 %