## Slide 1: IHE Cardiology
Eric Poiseau, INRIA
IHE Europe Technical Project Manager

## Slide 2: Primary Sponsors
Physician Associations & Colleges
  Primary: ACC, ESC
  Specialty: ASE, ASNC, HRS, SCAI, CTA
Vendor Participation
  About 20 companies involved in demonstrations in North America and Europe
  46 companies tested Cardiology integration profiles at connect-a-thon

## Slide 3: Profile Roadmap
Year 2004-2006 (Final Text)
  Cath Workflow (Cath)
  Echo Workflow (Echo)
  Retrieve ECG for Display (ECG)
  Evidence Documents (ED) for Cath and Echo
  Displayable Reports (DRPT) <<withdrawn for modifications>>
Year 2006-2007 (Trial Implementation)
  Stress Test Workflow (STRESS)
  Implanted Device Cardiac Observations (IDCO)
  Nuclear Medicine (NM) Cardiology Option
  Cross Enterprise Document Sharing (XDS)
  Cross Enterprise Document Sharing – Imaging (XDS-I)
  Cross Enterprise Document Sharing – Medical Summary (XDS-MS)

## Slide 4: Profile Roadmap
Future
  Finalize Displayable Reports (DRPT)
  Evidence Document Templates
    Stress Measurements
    Nuclear Cardiology Measurements
  Data Harvesting
  Portable Data for Imaging (PDI – DVD Support)
  EP Urgent Implantable Device Cardiac Identification (PDQ-IDC)

## Slide 5: Domain Visibility & Support
ACC Annual Conference
  2005 and 2006 ACC Interoperability Showcase
  Educational Workshops and Session
ESC Annual Conference
  2005 and 2006 ESC Interoperability Showcase
  Educational Workshops and Session
Specialty Hands-On Demonstrations
  ASE 2006
  ASNC 2007 and 2008
  HRS 2007
Additional Conference Representation
  CT Angiography
  SCAI
  Computers in Cardiology
  American College of Cardiology Administrators (ACCA)

## Slide 6: Overview
Cardiology Workflows General
  Cath Workflow
  Echo Workflow
  Stress Workflow
Content Display Requirements
  Stress Echo
  Stress
  Nuclear Cardiology

## Slide 7: The Problem
This is an example of a cardiology workflow.
Workflow is the linchpin to data integrity

## Slide 8: General Workflow

## Slide 9: Overview
Cardiology Workflows General
  Cath Workflow
  Echo Workflow
  Stress Workflow
Content Display Requirements
  Stress Echo
  Stress
  Nuclear Cardiology

## Slide 10: Cath Lab
1
2
3
4
5
6
7
Multiple re-entry of Patient ID
Error prone
Results fragmented across systems
Results inconsistently time-tagged
Custom solutions needed for data sharing
Difficult to manage
Uncoordinated with Hospital Information System
Unidentified patients (emergency)
Un-ordered cath exams
Diagnostic and interventional procedures
Ad hoc scheduling of cath labs
Change of rooms during procedure
8
9
10
11
Notes: Anybody recognize this? Unfortunately it’s frighteningly familiar ! It is a typical cath lab control room. I count at least 7 monitors (there are some more in the lab room). Almost every one is a different system. On each one you need to enter the patient name and ID – the same each time (yeah, right …)

## Slide 11: Use Cases
  Case C1: Patient Registered at ADT and Procedure Ordered at the Order Placer
  Case C2: Patient Registered at ADT and Procedure Ordered at DSS/OF
  Case C3: Patient Registered at ADT and Procedure Not Ordered
  Case C4: Patient Registered at DSS/OF and Procedure Ordered
  Case C5: Patient Not Registered
  Case C6: Patient Updated During Procedure
  Case C7: Change Rooms During Procedure
  Case C8: Cancel Procedure
  Case C9: Post-Procedure Evidence Creation
  Case C10: EP Ablation / Implantation Lab

## Slide 12: Overview
Cardiology Workflows General
  Cath Workflow
  Echo Workflow
  Stress Workflow
Content Display Requirements
  Stress Echo
  Stress
  Nuclear Cardiology

## Slide 13: Use Cases
Case E1: Patient Registered at ADT and Procedure Ordered
Case E2: Intermittently Connected Modality
Case E3: Intermittently Connected Modality with Ad Hoc Procedure, Patient Registered, Scheduled Procedure
Case E4: Intermittently Connected Modality with Ad Hoc Procedure, Patient Registered, Unscheduled Procedure
Case E5: Intermittently Connected Modality with Ad Hoc Procedure, Patient Unregistered, Unscheduled Procedure
Case E6: Stress Echo Staged Protocol
Case E7: Echo Measurements Evidence Creation

## Slide 14: Overview
Cardiology Workflows General
  Cath Workflow
  Echo Workflow
  Stress Workflow
Content Display Requirements
  Stress Echo
  Stress
  Nuclear Cardiology

## Slide 15: So what is Stress Testing?
Uses exercise or medication to increase the work of the heart.
Continuous 12 lead ECG monitoring during study
Looking for changes in ST segments
Used as a screening tool
Or to test effectiveness of therapy
Done in Non-Invasive Lab, and Cardiologist Office

## Slide 16: Stress
Image Intensive…multiple samples of 12 lead ECG during the protocol
Summary report usually one page in length
Physician will do comparisons to previous studies

## Slide 17: Stress Options
Stress Echo
  Began in the early – mid 1990’s
  Observation of wall motion and ejection fractions with the heart under stress
  High specificity for correlating ischemia to functional abnormalities
  Can be done with exercise but mainly chemical
Nuclear Stress
  Most often combined with exercise or chemical stress testing
  Use of radioisotope to detect presence and resolution of ischemic regions of the heart
  Scan immediately post
  Scan 4 hours to 1 day later
  Resolution of ischemic area determines viability of muscle

## Slide 18: Stress Workflow Diagram
Requires that Image Manager / Image Archive and Image Display support images, waveforms and structured reports
Notes: If a Report Creator wishes to participate in this profile, it does not have to support any transactions directly, however it is required to be grouped either with an Acquisition Modality, or with an Image Display in order to be able to Query/Retrieve the images, waveforms, and evidence documents. The Report Creator is expected to be able to transfer some contents of the created or retrieved objects into the reports it creates, and to send those reports in accordance with another Profile.

## Slide 19: Use Cases
Case S1: Cardiac Stress Test, ECG Only
  Limited use with lower sensitivities and specificities
  Screening tool only
Case S2: Cardiac Stress Test with Imaging
  More common use case
    Echocardiography – requires Consistent Time to combine clinical data from Stress Monitor and Echo Modality

## Slide 20: Overview
Cardiology Workflows General
  Cath Workflow
  Echo Workflow
  Stress Workflow
Content Display Requirements
  Stress Echo
  Stress
  Nuclear Cardiology

## Slide 21: Benefit: Stress Echo Viewing Consistency
Notes:   Image Display actors supporting the STRESS ECHO option shall be able to negotiate and accept the JPEG Baseline (Process 1): Default Transfer Syntax for Lossy JPEG 8 Bit Image Compression for Ultrasound Multi-frame images, and shall support the YBR_FULL_422 photometric interpretation.
  The Image Display actor may organize and present multiple images based on Stage and View for clinical comparison. Stage Number (0008,2122), View Number (0008,2128), Stage Code Sequence (0040,000A), and View Code Sequence (0008,2240) are mandated for the stress echo Modality (see section 4.2.3), and may be used by the Image Display Actor to determine the Stage and View of each image unambiguously.

## Slide 22: Agenda
Cardiology Workflows General
  Cath Workflow
  Echo Workflow
  Stress Workflow
Content Display Requirements
  Stress Echo
  Stress
  Nuclear Cardiology

## Slide 23: Nuclear Cardiology
Image formats
  Stress and Rest raw data review
  Stress and Rest processed data
  Gated SPECT data
  Quantitative data
  Screen captures, “snap shots”
Color maps
  Gray scale is default
  Color overlays can be applied

## Slide 24: Perfusion Display
Standard perfusion display
Stress/Rest
  Short axis
  Horizontal long axis
  Vertical long axis

## Slide 25
Perfusion Display - Color
Standard perfusion display
Stress/Rest
  Short axis
  Horizontal long axis
  Vertical long axis
Color map can be overlaid on the image

## Slide 26: Quantitative Display
Output from 3rd party quantitative perfusion software can be displayed

## Slide 27
Quantitative Display
Output from 3rd party quantitative gated software can be displayed

## Slide 28: Screen Captures
Screen captures can be displayed to show important images