## Slide 1
Chapter 13
Notes: <number>

## Slide 2
Inductance is the property of a conductor to oppose a change in current.
The effect of inductance is greatly magnified by winding a coil on a magnetic material.
Summary
Inductance
Common symbols for inductors (coils) are
Air core
Iron core
Ferrite core
Variable
Notes: <number>

## Slide 3
Summary
Self Inductance
Self-inductance is usually just called inductance, symbolized by L.
Self-inductance is a measure of a coil’s ability to establish an induced voltage as a result of a change in its current.
The induced voltage always opposes the change in current, which is basically a statement of Lenz’s law.
The unit of inductance is the henry (H). One henry is the inductance of a coil when a current, changing at a rate of one ampere per second, induces one volt across the coil.
Notes: <number>

## Slide 4
Summary
Self Inductance
The induced voltage is given by the formula
What is the inductance if 37 mV is induced across a coil if the current is changing at a rate of 680 mA/s?
Example
54 mH
Rearranging,
Notes: <number>

## Slide 5
Summary
Factors affecting inductance
Four factors affect the amount of inductance for a coil. The equation for the inductance of a coil is
where
L = inductance in henries
N = number of turns of wire
 = permeability in H/m
l = coil length in meters
Notes: <number>

## Slide 6
Summary
What is the inductance of a 2.0 cm long, 150 turn coil wrapped on an low carbon steel core that is 0.50 cm diameter? The permeability of low carbon steel is 2.5 x104 H/m
Example
22 mH
0.020 m


2
-4
150 t x 2.510 H/m x 7.8510 m
-5
2
Notes: <number>

## Slide 7
Summary
Physical parameters affecting inductance
The inductance given by the equation in the previous slide is for the ideal case. In practice, inductors have winding resistance (RW) and winding capacitance (CW). An equivalent circuit for a practical inductor including these effects is:
Notes: <number>

## Slide 8
Summary
Recall Lenz’s law states,
When the current through a coil changes, an induced voltage is created across the coil that always opposes the change in current.
In a practical circuit, the current can change because of a change in the load as shown in the following circuit example...
Lenz’s law
Notes: <number>

## Slide 9
Summary
Lenz’s law
A basic circuit to demonstrate Lenz’s law is shown.
Initially, the SW is open and there is a small current in the circuit through L and R1.
Notes: <number>

## Slide 10
Summary
SW closes and immediately a voltage appears across L that tends to oppose any change in current.
Initially, the meter reads same current as before the switch was closed.
Lenz’s law
Notes: <number>

## Slide 11
Summary
After a time, the current stabilizes at a higher level (due to I2) as the voltage decays across the coil.
Lenz’s law
Later, the meter reads a higher current because of the load change.
Notes: <number>

## Slide 12
Summary
Practical inductors
Inductors come in a variety of sizes. A few common ones are shown here.
Notes: <number>

## Slide 13
Summary
Series inductors
When inductors are connected in series, the total inductance is the sum of the individual inductors. The general equation for inductors in series is
2.18 mH
Example
If a 1.5 mH inductor is connected in series with an 680 H inductor, the total inductance is
Notes: <number>

## Slide 14
Summary
Parallel inductors
When inductors are connected in parallel, the total inductance is smaller than the smallest one. The general equation for inductors in parallel is
The total inductance of two inductors is
…or you can use the product-over-sum rule.
Notes: <number>

## Slide 15
Summary
Parallel inductors
Example
If a 1.5 mH inductor is connected in parallel with an 680 H inductor, the total inductance is
468 H
Notes: <number>

## Slide 16
Summary
Inductors in dc circuits
When an inductor is connected in series with a resistor and dc source, the current change is exponential.
Notes: <number>

## Slide 17
Summary
Inductors in dc circuits
The same shape curves are seen if a square wave is used for the source.
VS
VL
VR
Notes: <number>

## Slide 18
Summary
Universal exponential curves
Specific values for current and voltage can be read from a universal curve. For an RL circuit, the time constant is
Rising exponential
Falling exponential
Notes: <number>

## Slide 19
Example
In a series RL circuit, when is VR > 2VL?
Summary
Read the rising exponential at the 67% level.
After 1.1 
The curves can give specific information about an RL circuit.
Universal exponential curves
Notes: <number>

## Slide 20
Summary
The universal curves can be applied to general formulas for the current (or voltage) curves for RL circuits. The general current formula is
i =IF + (Ii IF)eRt/L
  IF = final value of current
  Ii = initial value of current
  i = instantaneous value of current
The final current is greater than the initial current when the inductive field is building, or less than the initial current when the field is collapsing.
Universal exponential curves
Notes: <number>

## Slide 21
Summary
Inductive reactance
Inductive reactance is the opposition to ac by an inductor. The equation for inductive reactance is
Example
The reactance of a 33 H inductor when a frequency of 550 kHz is applied is
114 
Notes: <number>

## Slide 22
Summary
Inductive phase shift
When a sine wave is applied to an inductor, there is a phase shift between voltage and current such that voltage always leads the current by 90o.
Notes: <number>

## Slide 23
True Power: Ideally, inductors do not dissipate power. However, a small amount of power is dissipated in winding resistance given by the equation:
Ptrue = (Irms)2RW
Reactive Power: Reactive power is a measure of the rate at which the inductor stores and returns energy. One form of the reactive power equation is:
Pr=VrmsIrms
The unit for reactive power is the VAR.
Power in an inductor
Summary
Notes: <number>

## Slide 24
The quality factor (Q) of a coil is given by the ratio of reactive power to true power.
Q of a coil
For a series circuit, I cancels, leaving
Summary
Notes: <number>

## Slide 25
Inductor
Winding
Induced voltage
Inductance
An electrical device formed by a wire wound around a core having the property of inductance; also known as a coil.
The loops or turns of wire in an inductor.
Voltage produced as a result of a changing magnetic field.
The property of an inductor whereby a change in current causes the inductor to produce a voltage that opposes the change in current.
Key Terms
Notes: <number>

## Slide 26
Henry (H)
RL time constant
Inductive reactance
Quality factor
A fixed time interval set by the L and R values, that determines the time response of a circuit. It equals the ratio of L/R.
The opposition of an inductor to sinusoidal current. The unit is the ohm.
The unit of inductance.
Key Terms
The ratio of reactive power to true power for an inductor.
Notes: <number>

## Slide 27
Quiz
1. Assuming all other factors are the same, the inductance of an inductor will be larger if
a. more turns are added
b. the area is made larger
c. the length is shorter
d. all of the above
Notes: <number>

## Slide 28
Quiz
2. The henry is defined as the inductance of a coil when
a constant current of one amp develops one volt.
one volt is induced due to a change in current of one amp per second.
one amp is induced due to a change in voltage of one volt.
the opposition to current is one ohm.
Notes: <number>

## Slide 29
Quiz
3. The symbol for a ferrite core inductor is
a.
b.
c.
d.
Notes: <number>

## Slide 30
Quiz
4. The symbol for a variable inductor is
a.
b.
c.
d.
Notes: <number>

## Slide 31
Quiz
5. The total inductance of a 270 H inductor connected in series with a 1.2 mH inductor is
a. 220 H
b. 271 H
c. 599 H
d. 1.47 mH
Notes: <number>

## Slide 32
Quiz
6. The total inductance of a 270 H inductor connected in parallel with a 1.2 mH inductor is
a. 220 H
b. 271 H
c. 599 H
d. 1.47 mH
Notes: <number>

## Slide 33
Quiz
7. When an inductor is connected through a series resistor and switch to a dc voltage source, the voltage across the resistor after the switch closes has the shape of
a. a straight line
b. a rising exponential
c. a falling exponential
d. none of the above
Notes: <number>

## Slide 34
Quiz
8. For circuit shown, the time constant is
a. 270 ns
b. 270 s
c. 270 ms
d. 3.70 s
Notes: <number>

## Slide 35
Quiz
9. For circuit shown, assume the period of the square wave is 10 times longer than the time constant. The shape of the voltage across L is
a.
b.
c.
d.
Notes: <number>

## Slide 36
Quiz
10. If a sine wave from a function generator is applied to an inductor, the current will
a. lag voltage by 90o
b. lag voltage by 45o
c. be in phase with the voltage
d. none of the above
Notes: <number>

## Slide 37
Quiz
Answers:
1. d
2. b
3. d
4. c
5. d
6. a
7. b
8. a
9. c
10. a
Notes: <number>