## Slide 1: Lab#1
UTP cables

## Slide 2: Making connections - Tools
Cat5e cable
RJ45 connectors
Cable stripper
Scissors
Crimping tool

## Slide 3: Making connections - Steps
Strip cable end
Untwist wire ends
Arrange wires
Trim wires to size
Attach connector
Check
Crimp
Test

## Slide 4: Step 1 – Strip cable end
Strip 1 – 1½” of insulating sheath
Avoid cutting into conductor insulation

## Slide 5: Step 2 – Untwist wire ends
Sort wires by insulation colors

## Slide 6: Step 3 – Arrange wires
TIA/EIA 568A: GW-G OW-Bl BlW-O BrW-Br
TIA/EIA 568B: OW-O GW-Bl BlW-G BrW-Br

## Slide 7: Step 4 – Trim wires to size
Trim all wires evenly
Leave about ½” of wires exposed

## Slide 8: Step 5 – Attach connector
Maintain wire order, left-to-right, with RJ45 tab facing downward

## Slide 9: Step 6 - Check
Do all wires extend to end?
Is sheath well inside connector?

## Slide 10: Step 7 - Crimp
Squeeze firmly to crimp connecter onto cable end (8P)

## Slide 11: Step 8 – Test
Does the cable work?

## Slide 12: Let’s go to work!