## Slide 1
Microbiology is Fun!

## Slide 2: What is Microbiology?
Micro - too small to be seen with the nacked eye
Bio - life
logy - study of
(The science that studies micro organisms)

## Slide 3: Organisms included in the study of Microbiology
Bacteria
Algae
Fungi
Viruses
Microorganisms - Microbes - Germs

## Slide 4
Microbiology equipment
Microbiology equipment
Microbiology equipment

## Slide 5: Petri dish
A petri dish is a flat dish made of plastic
or glass with a cover that is used to grow
microorgansim

## Slide 6: Incubator
Incubator is a warm cabinet that you can set it's temperature to a proper temperature for
microbs growth.
a good temperature for most bacteria is About 35ºc and agood temprature for most fungi is 25°c.

## Slide 7: Hot air oven
This kind of dry heat sterilization is recomended when it is undesirable that steam make contact with the material to be sterilized. This is true for glasswares – glasspetriplates, Pipettes as well as for substances like oil, powder, etc.

## Slide 8
autoclave sterilizes items by heating them with steam to a very high temperature (121 degrees° C/15 p.si).
The advantage of using an autoclave is that
it can reach temperatures
higher than boiling water alone
, so it can kill not only bacteria
but also bacterial spores, which tend to be resistant
Autoclaves

## Slide 9: Bunsen burner
Bunsen burner is produces
gas flame which used for heating, sterilization (inoculating loop)

## Slide 11: glassware
tube
beaker
flask

## Slide 12
pipette

## Slide 13
The Microscope

## Slide 14
With a binocular microscope, adjust oculars for both eyes!

## Slide 15
Don’t shut one eye while observing under the microscope!

## Slide 16
Always carry with 2 hands
Only use lens paper for cleaning
Do not force knobs
Always store covered

## Slide 17
How to properly carry the microscope

## Slide 18
Eyepiece
Arm
Stage
Coarse Focus
Fine Focus
Base
Body Tube
Revolving Nosepiece
Objective Lens
Stage Clips
Diaphragm
Light

## Slide 19
Place the Slide on the Microscope
Use Stage Clips
Click Nosepiece to the lowest (shortest) setting
Look into the Eyepiece
Use the Coarse Focus

## Slide 20
Follow steps to focus using low power
Click the nosepiece to the longest objective
Do NOT use the Coarse Focusing Knob
Use the Fine Focus Knob to bring the slide