## Slide 1: Lab1 A VISIBLE ABSORPTION SPECTROMETER

## Slide 2
-One of the simplest and most widely used methods to determine concentration of a substance in solution
  -Measures light absorbed by solution at a specific wavelength
Notes: <number>

## Slide 3
-In the analysis, the amount of light radiation absorbed by a sample is measured. The light absorption is directly related to the concentration of the colored compound in the sample.
-The wavelength (λ) of maximum absorption is known for different compounds.

## Slide 4
This method is used to determine concentrations of various chemicals which can give colors either directly or after addition of some other chemicals

## Slide 5
Principles of Spectrophotometer
A spectrophotometer consists of two instruments:
Spectrometer: for producing light of any selected color (wavelength),
Photometer: for measuring the intensity of light.

## Slide 6
The instruments are arranged so that liquid in a cuvette can be placed between the spectrometer beam and the photometer.

## Slide 7
-The amount of light passing through the tube is measured by the photometer.
-The photometer delivers a voltage signal to a display device, normally a galvanometer.
-The signal changes as the amount of light absorbed by the liquid changes.

## Slide 8
The electromagnetic spectrum is a family of waves consisting of, gamma ray, X-rays, ultraviolet, visible light, infra-red, microwaves and radio waves.
Electromagnetic spectrum

## Slide 9
Visible light
-Is only a small portion of the entire electromagnetic spectrum and it includes the colors commonly observed (red, yellow, green, blue and violet).
-The visible spectrum consists of electromagnetic radiation whose wavelengths range from 400 nm to nearly 800 nm

## Slide 10: Visible region wavelength
Color | Wavelength (nm)
Ultraviolet | 400 and under
Violet | 400 - 450
Blue | 450 - 500
Green | 500 - 570
Yellow | 570 - 590
Orange | 590 - 620
Red | 620 - 650
Infrared | 750 & over
Notes: <number>

## Slide 11
100% transmittance means no light is absorbed by the solution so that incident light is 100% transmitted.
100% T = 0A

## Slide 12
The Spectrophotometer Instrument
All spectrophotometer instruments designed to measure the absorption of radiant energy have
the basic components as follows:
1.Light source:
tungsten lamp for visible region.
The intensity of out put of the lamp varies with the wavelength.

## Slide 13
2. Monochromator (filter ):
To isolate a desired wavelength from the source.
3. Transparent container (cuvette):
For the sample and the blank

## Slide 14
4. A radiation detector (phototube):
To convert the radiant energy received to a measurable signal; and a readout device that displays the signal from the detector

## Slide 15
Io I
A = 0.012
 l 
Lamp
Monochromator
Cuvette
Detector
Notes: <number>

## Slide 16
Notification:
-Pyrex glass absorbs no light in the visible region but absorbs almost all the light in the UV region.
-Hence in UV range quartz or silica cuvettes are used

## Slide 17
Procedure:
*The general measurement procedure consists of 5 steps:
1. Prepare samples to make colored compound or discolor compound.
2. Make series of standard solutions of known concentrations.

## Slide 18
3. Set spectrophotometer to Absorption mode and choose the desired wavelength
4. Zeroing machine by adding blank then measure light absorbance of standards then your sample
5. Plot standard curve: Absorbance vs. Concentration or make a calculation

## Slide 19: Rules to handle cuvettes:
- Do not handle lower portion of the cuvette.
- Rinse cuvette with two portion of solution.
- Wipe off any liquid drops with a clean lens paper.
- Insert the cuvette with the index-line facing the front of the instrument.

## Slide 20
*Some Operating Instructions For Spectrophotometer:
1. Ensure 230v.
2. Insert the power cord of the instrument in to a power point.
3. Turn the switch at ‘ON” position.
4- waiting machine to warm up
5-use it when it’s ready
6-select mode(Abs) and adjust wavelenght

## Slide 21
Is the wavelength at which the maximum fraction of light is absorbed by a solution.
Lambda λ max

## Slide 22: How to calculate λ max:
Materials:
Chromium nitrate.
Blank.
Spectrophotometer.
Wavelengths :400- 800 nm.

## Slide 23
Prep for standard chromium nitrate :
Weight 0.476 g of chromium nitrate & dissolve it with 100 ml of distal water
In anew balance machine measure the weight as carat (ct) not gram
So the value will be 4.76ct

## Slide 24
Procedure:
1- Adjust spectrophotometer to zero against blank.
2- Take the readings of chromium nitrate at wavelengths starting from 400 till 800 nm in 50 nm interval (400-450-500-550-........800).

## Slide 25
The interval start with 50,20,10,5 and 2
Finally ,take the reading in one interval .
This is going to be λ max.

## Slide 26: Any Question??