## Slide 1: Lec5: Applying Dynamic Routing Protocols in CISCO Packet Tracer
Notes: <number>

## Slide 3: Configuring Dynamic Routing Protocols
  RIP
  IGRP
  EIGRP
  OSPF
  IS-IS
  BGP
Notes: <number>

## Slide 4
R2
30.0.0.0
20.0.0.0
10.0.0.0
40.0.0.0
50.0.0.0
R1
R3
R4
Configure the following network with different routing protocols

## Slide 5
Router1 (R2)
Router0 (R1)
Router3 (R4)
Router2 (R3)
Notes: <number>

## Slide 6: Configuring R1 Interfaces
Router>enable
Router#configure terminal
Enter configuration commands, one per line. End with CNTL/Z.
Router(config)#hostname R1
R1(config)#interface fastethernet 0/0
R1(config-if)#ip address 10.0.0.1 255.0.0.0
R1(config-if)#no shutdown
%LINK-5-CHANGED: Interface FastEthernet0/0, changed state to up %LINEPROTO-5-UPDOWN: Line protocol on Interface FastEthernet0/0, changed state to up
R1(config-if)#exit
R1(config)#interface serial 0/0/0
R1(config-if)#ip address 20.0.0.1 255.0.0.0
R1(config-if)#clock rate 64000
R1(config-if)#bandwidth 64
R1(config-if)#no shutdown
%LINK-5-CHANGED: Interface Serial0/0/0, changed state to down
R1(config-if)#exit

## Slide 7: Configuring R2 Interfaces
Router>enable
Router#configure terminal
Enter configuration commands, one per line. End with CNTL/Z.
Router(config)#hostname R2
R2(config)#interface serial 0/0
R2(config-if)#ip address 20.0.0.2 255.0.0.0
R2(config-if)#no shutdown
%LINK-5-CHANGED: Interface Serial0/0, changed state to up %LINEPROTO-5-UPDOWN: Line protocol on Interface Serial0/0, changed state to up
R2(config-if)#exit
R2(config)#interface fastethernet 0/0
R2(config-if)#ip address 30.0.0.1 255.0.0.0
R2(config-if)#no shutdown
%LINK-5-CHANGED: Interface FastEthernet0/0, changed state to up
R2(config-if)#exit
%LINEPROTO-5-UPDOWN: Line protocol on Interface FastEthernet0/0, changed state to up

## Slide 8: Configuring R3 Interfaces
Router>enable
Router#configure terminal
Enter configuration commands, one per line. End with CNTL/Z.
Router(config)#hostname R3
R3(config)#interface fastethernet 0/0
R3(config-if)#ip address 30.0.0.2 255.0.0.0
R3(config-if)#no shutdown
%LINK-5-CHANGED: Interface FastEthernet0/0, changed state to up %LINEPROTO-5-UPDOWN: Line protocol on Interface FastEthernet0/0, changed state to up
R3(config-if)#interface serial 0/0
R3(config-if)#ip address 40.0.0.1 255.0.0.0
R3(config-if)#clock rate 64000
R3(config-if)#bandwidth 64
R3(config-if)#no shutdown
%LINK-5-CHANGED: Interface Serial0/0, changed state to down
R3(config-if)#exit %LINK-5-CHANGED: Interface Serial0/0, changed state to up %LINEPROTO-5-UPDOWN: Line protocol on Interface Serial0/0, changed state to up

## Slide 9: Configuring R4 Interfaces
Router>enable
Router#configure terminal
Enter configuration commands, one per line. End with CNTL/Z.
Router(config)#hostname R4
R3(config)#interface fastethernet 0/0
R3(config-if)#ip address 50.0.0.1 255.0.0.0
R3(config-if)#no shutdown
%LINK-5-CHANGED: Interface FastEthernet0/0, changed state to up %LINEPROTO-5-UPDOWN: Line protocol on Interface FastEthernet0/0, changed state to up
R3(config-if)#interface serial 0/0
R3(config-if)#ip address 40.0.0.2 255.0.0.0
R3(config-if)#clock rate 64000
R3(config-if)#bandwidth 64
R3(config-if)#no shutdown
%LINK-5-CHANGED: Interface Serial0/0, changed state to down
R3(config-if)#exit %LINK-5-CHANGED: Interface Serial0/0, changed state to up %LINEPROTO-5-UPDOWN: Line protocol on Interface Serial0/0, changed state to up

## Slide 10: Applying Dynamic Routing Protocols on R1,R2,R3,R4

## Slide 11: RIP
How to configure router R1 with RIP protocol?
R2
R3
R4
R1
30.0.0.0
20.0.0.0
10.0.0.0
40.0.0.0
50.0.0.0
R1>enable
R1#configure terminal
R1(config)#router rip
R1(config-router)#network 10.0.0.0
R1(config-router)#network 20.0.0.0
R1(config-router)#exit

## Slide 12: IGRP
How to configure router R2 with IGRP protocol?
R2
R2
R3
R1
30.0.0.0
20.0.0.0
10.0.0.0
40.0.0.0
50.0.0.0
R2>enable
R2#configure terminal
R2(config)#router rip
R2(config)#router igrp 100
R2(config-router)#network 20.0.0.0
R2(config-router)#network 30.0.0.0
R2(config-router)#exit
100 is Autonoms System (AS) number

## Slide 13: EIGRP
How to configure router R3 with EIGRP protocol?
R2
R3
R4
R1
30.0.0.0
20.0.0.0
10.0.0.0
40.0.0.0
50.0.0.0
R3>enable
R3#configure terminal
R3(config)#router eigrp 1
R3(config-router)#network 30.0.0.0
R3(config-router)#network 40.0.0.0
R3(config-router)#exit

## Slide 14: OSPF
Router(config)# router ospf process_ID
Router(config-router)# network IP_address wildcard_mask area area_#
The process_ID Used to differentiate between OSPF processes running on the same router.
Your router might be a boundary router between two OSPF autonomous systems, and to differentiate them on your router, you will give them unique process IDs.
Note that these numbers do not need to match between different routers so they have nothing to do with autonomous system numbers.

## Slide 15: OSPF
How to configure router R2 with OSPF protocol?
R2
R3
R4
R1
30.0.0.0
20.0.0.0
40.0.0.0
R2>enable
R2#configure terminal
R2(config)#router ospf 2
R2(config-router)#network 20.0.0.0 0.255.255.255 area 0
R2(config-router)#network 30.0.0.0 0.255.255.255 area 0
R2(config-router)#exit

## Slide 16: Different Routing Commands
Commands | Descriptions
Router(config)#router rip | Enables RIP as a routing protocol
Router(config-router)#network w.x.y.z | w.x.y.z is the network number of the directly connected network you want to advertise.
Router(config)#no router rip | Turns off the RIP routing process
Router(config-router)#no network w.x.y.z | Removes network w.x.y.z from the RIP routing process.
Router(config-router)#version 2 | RIP will now send and receive RIPv2 packets globally.
Router(config-router)#version 1 | RIP will now send and receive RIPv1 packets only
Router(config-router)#no auto-summary | RIPv2 summarizes networks at the classful boundary. This command turns autosummarization off.
Router(config-router)#passive-interface s0/0/0 | RIP updates will not be sent out this interface.
Router(config-router)#no ip split-horizon | Turns off split horizon (on by default).
Router(config-router)#ip split-horizon | Re-enables split horizon
Router(config-router)#timers basic 30 90 180 270 360 | Changes timers in RIP: 30 = Update timer (in seconds) 90 = Invalid timer (in seconds) 180 = Hold-down timer (in seconds) 270 = Flush timer (in seconds) 360 = Sleep time (in milliseconds)
Router#debug ip rip | Displays all RIP activity in real time
Router#show ip rip database | Displays contents of the RIP database

## Slide 17
Notes: <number>