## Slide 1: Lab3 Atomic-absorption spectroscopy

## Slide 2
AAS is a technique for determining the
concentration of a particular metal
element (e.g.Fe, Cu, Al, Pb, Ca, Zn)in a
sample ( water, medicine, food) .
- It can be used to analyze the Conc. of over 70 different metals in a solution.
Introduction

## Slide 3
Atomic-absorption (AA) spectroscopy uses the absorption of light to measure the concentration of gas-phase atoms.
Since samples are usually liquids or solids, the analyte atoms must be vaporized or atomized in a flame.

## Slide 4
*Steps:
The steps are involved turning a liquid sample into an atomic gas:
*Desolvation:
the liquid solvent is evaporated, and the dry sample remains.
*Vaporisation or Volatilization:
the solid sample vaporises to a gas.

## Slide 6
1-Hollow Cathode Lamp:
The light that is focused into the flame is produced by it. The type of hollow cathode tube depends on the metal being analyzed. For analyzing the concentration of copper, a copper cathode tube would be used.
AAS parts:

## Slide 7
2- Monochromator:
Which is set to isolate the radiation at the specified wavelength and travels into the detector.

## Slide 8
3- Detector:
-Photo multiplier tube.
-Extremely sensitive
-Can detect single photons
-Measures the intensity of the beam of light.
When some of the light is absorbed by metal, the beam's intensity is reduced. The detector records that reduction as absorption. That absorption is shown on output device by the data system

## Slide 10
Principle:
Sample solutions are usually aspirated and entering to the flame excitation by heat of flame absorb light from hallow cathode lamb to go from ground state E˳ to higher energy level E1monochromator detector measuring the reduction of intensity of light refer to conc. of sample.
Each Element have specific E that will absorb a specific wavelength of light .

## Slide 11
Schematic of an atomic-absorption