## Slide 1: http://www.youtube.com/watch?v=ZmqqRPISg0g&feature=player_detailpage
The polymerase chain reaction (PCR)

## Slide 2
The polymerase chain reaction (PCR) is a scientific technique in, molecular biology to amplify a single or a few copies of a piece of DNA across several orders of magnitude, generating thousands to millions of copies of a particular DNA sequence.
Developed in 1983 by Kary Mullis

## Slide 3: PCR Principles And Procedure
PCR is used to amplify a specific region of a DNA strand (the DNA target).
A basic PCR set up requires several components and reagents. These components include:
DNA template that contains the DNA region (target) to be amplified.
Two primers that are complementary to the 3' (three prime) ends of each of the sense and anti-sense strand of the DNA target.
Taq polymerase or another DNA polymerase with a temperature optimum at around 70 °C.

## Slide 4
Deoxynucleoside triphosphates (dNTPs; nucleotides containing triphosphate groups), the building-blocks from which the DNA polymerase synthesizes a new DNA strand.
Buffer solution, providing a suitable chemical environment for optimum activity and stability of the DNA polymerase.
Divalent cations, magnesium or manganese ions; generally Mg2+ is used, but Mn2+ can be utilized for PCR-mediated DNA mutagenesis, as higher Mn2+ concentration increases the error rate during DNA synthesis
Monovalent cation potassium ions.

## Slide 5
Procedure
PCR consists of a series of 20-40 repeated temperature cycles, with each cycle consisting of 2-3 discrete temperature steps.
The cycling is often preceded by a single temperature step (called hold) at a high temperature (>90°C),
The temperatures used and the length of time they are applied in each cycle depend on a variety of parameters.

## Slide 6
Initialization step:
Temperature 94–96 °C,
Time required 1–9 minutes.
It is only required for DNA polymerases that require heat activation by hot-start PCR.
Denaturation step:
First regular cycling event
Temperature 94–98 °C
Time required 20–30 seconds.
It causes melting of the DNA template by disrupting the hydrogen bonds, yielding single-stranded DNA molecules.

## Slide 7
Annealing step:
Temperature 50–65 °C
Time required 20–40 seconds
allowing annealing/binding of the primers to the single-stranded DNA template.
The polymerase binds to the primer-template hybrid and begins DNA synthesis.

## Slide 8
Extension/elongation step:
Temperature 72 °C (depending on the DNA polymerase used)
Taq polymerase has its optimum activity temperature at 75–80 °C,
DNA polymerase synthesizes a new DNA strand complementary to the DNA template strand by adding dNTPs

## Slide 9
The extension time depends both on the DNA polymerase used and on the length of the DNA fragment to be amplified
Under optimum conditions a thousand bases per minute can be amplified, if there are no limitations due to limiting substrates or reagents