## Slide 1
Nuclear Pharmacy
Lab #1
DANGER Radiation risk
DANGER Radiation risk
DANGER Radiation risk
DANGER Radiation risk

## Slide 3: What is Nuclear Pharmacy?
The development of nuclear pharmacy as a specialty area followed the development of nuclear medicine as a recognized specialty by the American Medical Association in the early 1970's.

## Slide 4: What is Nuclear Pharmacy?
Nuclear Medicine
A specialty of medicine and medical imaging that uses radiopharmaceuticals in the diagnosis and treatment of diseases.

## Slide 5: What is Nuclear Pharmacy?
Nuclear Pharmacy
A specialty area of pharmacy practice dedicated to the compounding and dispensing radiopharmaceuticals for use in nuclear medicine procedures.
Notes: radiopharmaceuticals page 79 def

## Slide 6: What are the applications of Radiopharmacy?
Diagnostic
  The radiopharmaceutical accumulated in an organ of interest emit gamma radiation which are used for imaging of the organs with the help of an external imaging device called gamma camera.
Treatment
  They are radiolabeled molecules designed to deliver therapeutic doses of ionizing radiation to specific diseased sites.
Research
Notes: Diagnostic
  Barium swallow – examination of upper GI tract
  Non-imaging diagnostics
    Radioactive Isotope labelling for tracing
      i.e. More specific tests for thyroid function, renal function and vitamin adsorption.
Research
  Pharmacological
    Drug delivery – i.e. brain perfusions and examining whether or not drugs cross blood brain barrier.
Curative & Palliative
  Radiotherapy
    Brachytherapy – The introduction of a Radionuclide into a localised area of tissue, i.e. a tumour. The radiation destroys cells within the vicinity.
    Iodine-131 – A radioactive isotope used to treat Hyperthyroidism. Once injected the isotope concentrates within certain tissues. Has the advantage of not requiring invasive surgery or anaesthesia. – Who makes the drug?
  Palliative treatment - refers to the management of symptoms when the underlying disease is untreatable or terminal. Radiotherapy may aid in prolonging the life of dying patients.

## Slide 7: The Nuclear Pharmacist Role
Order, receipt, storage and inventory control of radioactive drugs (radiopharmaceuticals)
Preparation of radiopharmaceuticals
Functional checks of instruments
Determination of radiopharmaceutical quality and purity
Filling of prescription orders

## Slide 8: The Nuclear Pharmacist Role
Packaging, labeling of radiopharmaceuticals
Communicating radiopharmaceutical-related information to others
Assuring that patients receive proper preparation
Participation in clinical trials

## Slide 9: Employment Opportunities
Nuclear Pharmacists work in a wide variety of settings:
Nuclear pharmacies
Hospitals
Academia
Industry
Government and private research institutes

## Slide 10: Training
Nuclear pharmacists can receive training by attending a nuclear pharmacy program in various schools of pharmacy and practice experience through a nuclear pharmacy. The colleges listed below offer nuclear pharmacy programs
University of Arkansas | Mercer University | University of Oklahoma
Butler University | University of New Mexico | Purdue University
Duquesne University | State University of New York at Buffalo | Medical University of South Carolina
Massachusetts College of Pharmacy | Ohio State University | Temple University University of Utah

## Slide 11: Certification
Upon successful completion of a nuclear pharmacist training program, nuclear pharmacists can be certified through an examination offered by the Board of Pharmaceutical Specialties (BPS).
Such nuclear pharmacists are then designated as Board Certified Nuclear Pharmacists (BCNP). For more information

## Slide 12: Design of a Nuclear Pharmacy
Protection of personnel from radiation hazard.
  Control of personnel radiation exposure is performed with approved personal dosimeters, which are regularly checked and their readings recorded.
Avoidance of contamination of work area.
Radiation detection instruments.
Clean air.
Disposal of radioactive waste.

## Slide 13
Dispensing Area
Counting Lab
Compounding Area
Offices
Corridor
Conceptual design of a nuclear pharmacy unit
Should be equipped with workbenches made of stainless steel or wood covered with laminated plastic
The floor should be made of removable tiles or covered with rubber matting so it can be replaced with new ones in case of spillage

## Slide 14: Operation of a Nuclear Pharmacy
Receiving of radioactive materials
Preparation of radiopharmaceuticals
Quality control tests of radiopharmaceuticals
Storage
Dispensing
Radioactive waste disposal
Infectious waste disposal

## Slide 15: Receiving radioactive materials
Delivered directly to nuclear medicine department or nuclear pharmacy (short half-lives)
Packages should be monitored within 3 hr if delivered during normal hours
Packages should be monitored within 3 hr from the beginning of the next working day if delivered after working hours

## Slide 16: Preparation of radiopharmaceuticals
Only trained people should be responsible for and participate in the preparation
Aseptic technique
Lead barrier shields
Syringe shields
Leaded gloves, aprons, and eye glasses should be worn
Quantity
Notes: Aseptic techniques
Personnel should appropriately apply aseptic techniques throughout the handling of
radiopharmaceuticals for injection, including the radiolabelling of kits. This implies the use of
special clothing, sterile gloves, sterile vials, sterile syringes, sterile needles and sterile
diluents, and that the work is done in a well-planned and expedient way.

## Slide 17: Radiation shielding
Alpha and beta radiations are readily shielded because of their limited range of penetration.
Radiation | Protection
Alpha particles | Piece of paper Mono-energetic and have a range of a few centimeters in air
Beta radiation | Aluminum Glass Transparent plastic materials
Gamma radiation | Lead Tungsten

## Slide 19: Quality Control Tests of Radiopharmaceuticals
Before despising for humans
Colloidal and macro-aggregated preparation should be checked for particle size.
Workstations and their environment should regularly be monitored with respect to microbiological quality.

## Slide 20: Storage
Should be properly stored to prevent degradation by light or temperature
Must be stored in lead containers or behind lead shields

## Slide 21: Dispensing
Starts with a prescription
Prescription should contain
  Patients name
  Identification no.
  Age
  Date time
  Physician signature

## Slide 22: Radioactive waste disposal
Syringes, vials containing residual activities, needles, contaminated papers, liquid waste
According to guideline
  Decay in storage
  Release into a sewerage system
  Transfer to an authorized recipient (disposable facility)
  Others (incineration and atmospheric release of radioactive gases)

## Slide 23: Radioactive waste disposal
Radionuclides with have lives less than 120 days usually are disposed of by this method
Radio active should be stored separately according the similar half lives
For soluble radioactive materials in water
Disposed quantity should not exceed the limits of the maximum permitted concentrations (MPCs)
Flow rate of water
Number of radionuclide
For long-lived radionuclide
They bury or incinerate at approved sites and facilities

## Slide 24: Infectious waste disposal
Body fluids tissue
Incinerated or chemically treated, steamed or dry sterilized
Should be stored in puncture resistant, leak resistant bags or containers
Should be labeled with international biohazard symbol
Storage period

## Slide 25: Thank You

## Slide 26: Quality control tests of radiopharmaceuticals
Visual Inspection of Product
Visual inspection of the compounded radiopharmaceutical shall be conducted to ensure the absence of foreign matter and also to establish product identity by confirming that
a liquid product is a solution, a colloid, or a suspension
a solid product has defined properties that identify it.
Assessment of Radioactivity
-The amount of radioactivity in each compounded radiopharmaceutical should be verified and documented prior to dispensing, using a proper standardized radionuclide (dose) calibrator.