## Slide 1
313
PHT
LAB#1

## Slide 2
☠ Lab coat & marker.
☠ No eating, drinking,
☠ Benches disinfection.
☠ Inoculating loop sterilization.
☠ Aseptic technique.
☠ Discarded cultures & infectious materials.
☠ Broken or spilled living cultures.
☠ Microscope.
☠ At the end of each lab check:
    Gas tap is turned off.
    Water tap is closed properly.
    Microscope lamp is turned off.
☠ Finally wash your hands thoroughly.
Microbiology laboratory safety protocoal
Notes: <number>

## Slide 3
Discard cultures and other infectious materials:
Petri dishes→ Plastic bag → Autoclave.
Test tube cultures → wire basket → Autoclave.
Used pipettes → Jar containing a disinfectant → Plastic bag → Autoclave
Used slides, covers → Jar containing a disinfectant
Broken glass → swept in a dustpan → container for broken glass.
NEVER place contaminated material in waste basket.
Notes: <number>

## Slide 4
Broken or spilled living cultures:
Clothing → Autoclave plastic bag → Autoclave.
Flood the area with a disinfectant ( or paper towels are placed over the spills).
After 20- 30min→ wipe up & discard the waste in autoclavable dustpan→ Autoclave.
Notes: <number>

## Slide 5: Staining of Bacteria
<number>
Types of staining technique:-
Simple staining
(use of a single stain)
Differential staining
(use of two contrasting stain)
For visualization of morphological
shape & arrangement.
Identification
Visualization
of structure
Gram
stain
Acid fast
stain
Spore
stain
Capsule
stain

## Slide 6: Flaming of Loop
<number>

## Slide 7: Smearing out of the sample
<number>

## Slide 8: Smear Fixation
<number>

## Slide 9
<number>
Principle of Differential Stains
* Application of the primary stain.
  * Decolourization.
  *Application of the counter-stain.

## Slide 10: Gram’s Stain
<number>

## Slide 11: G-ve bacilli
<number>
Gm+ve cocci

## Slide 12: Gram Stain
<number>
It is the most important differential stain used in bacteriology because it classified bacteria into two major groups:
Gram positive:
Appears violet after Gram’s stain
b) Gram negative:
Appears red after Gram’s stain

## Slide 13: Gram Stain
<number>
Materials:-
    Cultures of Staphylococci, Candida, Bacillus, gram –ve bacteria.
    Crystal violet (primary stain)
    Gram’s iodine (mordant)
    Acetone-alcohol (decolorizing agent)
    Safranin (counter stain)

## Slide 14: Gram Staining Technique
<number>

## Slide 15: Gram Stain [single]
<number>
Procedure:
s
CV
iodine
30-60 sec
2 min
10 sec
safranin
30 sec

## Slide 16
<number>
Gram +ve
S.aureus
Gram –ve
E.coli
Step 1: Crystal Violet
Step 2: Gram’s Iodine
Step 3: Decolorization
(Aceton-Alcohol)
Step 4: Safranin Red

## Slide 17: Results:
<number>
Shape: Cocci
Arrangement: clusters
Colour: Violet
Gram’s reaction: Gram’s +ve
Name of microorganism: Staphylococcus aureus (S. aureus)

## Slide 18: Results:
<number>
Shape: Oval
Arrangement: Single
Colour: Violet
Gram’s reaction: Gram’s +ve
Name of microorganism:
Candida albicans (C. albicans)

## Slide 19: Results:
<number>
Shape: Bacilli
Arrangement: Chains
Colour: Violet
Gram’s reaction: Gram +ve
Name of microorganism:
Bacillus subtilis (B. subtilis)

## Slide 20: Results:
<number>
Shape: Rods
Arrangement: Single
Colour: red
Gram’s reaction: Gram -ve
Name of microorganism:
Gram –ve bacilli

## Slide 21: Culture Media
The culture media is an artificial preparation contains the essential element and nutrient in a proper concentration needed by the microorganism to grow.
It may be:-
    Liquid (broth)
    Solid (containing agar)
    Semisolid (containing low conc of agar)

## Slide 22: Culture Media
Most common ingredients:-
Essential elements and nutrients.
Solidifying agents.

## Slide 23: Types of culture media:
Simple media
Enriched media
Selective media
Indicator media
Selective and indicator media
Notes: <number>

## Slide 24: Isolation of Pure Colonies of Microorganism “Streak Plate Method”
In natural environments, bacteria & other m.o exist in mixed population.
“Streak Plate Technique”
The individual cells are separated from each other by certain distance on the surface of the agar.
After incubation, each single deposited cell divide many times and finally form visible mass of growth “COLONY”.

## Slide 25: The streak Plate Method
The culture prepared from a single type of colony is regarded as a pure culture.
The streak Plate Method is used for:
  Checking the purity of a bacterial culture.
  Isolating individual species from a mixture culture.

## Slide 26: The streak Plate Method
Objective:-
for isolation of individual species of a mixed broth culture.
Materials:-
  Nutrient agar plate.
  Mixed broth culture of Serratia marcescens and staph. aureus.

## Slide 27: The streak Plate Method
Procedure:
S & S
Aseptic technique
Invert the plate and
Incubate for 24h at 37℃
Drop of the culture
Flame & Cool
Flame & Cool
Flame & Cool

## Slide 28
The streak Plate Method

## Slide 29
The streak Plate Method

## Slide 30: Antibiotic Sensitivity Testing
Antibiotic sensitivity testing is used to determine the susceptibility of the microorganism to various antimicrobial agents.
Notes: <number>

## Slide 31
Sensitivity testing techniques:
  Disc Diffusion Method.
  Serial Dilution Method (Minimum inhibitory concentration).
Notes: <number>

## Slide 32: Disc Diffusion Method
The effectiveness of an antibiotic in this technique is based on the size of the zone of inhibition that surrounds a disc that has been impregnated with a specific concentration of the agent.
Advantages:
  Rapid
  Accurate
  Inexpensive
Notes: <number>

## Slide 33: Disc Diffusion method
Materials:
  Cultures of
  Staph. aureus,
  E. coli
  Pseudomonas aeruginosa
  Filter paper disc
  Antibiotic solutions (Vancomycin, Augmentin, Ceftazidime, Azactam)
  20 ml melted nutrient agar
  Petri-dish
  Sterile 1ml pipette
Notes: <number>

## Slide 34: Procedure
45°c
0.1ml
m.o
inoculate
Aug
Az
Van
Cef
Az
24 h
at 37°c
incubate
Don’t invert
Notes: <number>

## Slide 35: Results:
Measure the diameter of each inhibition zone
The diameter of the
inhibition zones are directly proportional to the
susceptibility of the
microorganism to the antibiotics
(sensitive, intermediate, resistant).

## Slide 36: Results
Cef
Az
Van
Aug
Notes: <number>

## Slide 37
<number>
Thank you