## Slide 1: Polymerase Chain Reaction (PCR)
By: Sahar AlSubaie

## Slide 2: PCR:
PCR is a technique for amplifying DNA sequences in vitro.

## Slide 3: PCR properties:
Rapid & easy.
Sensitive.
Robust.
Widespread applications.

## Slide 4: Basic requirements for PCR reaction:
DNA sequence of target region
Primers
Taq polymerase (Thermo-stable DNA polymerase)
dNTPs
DNA thermal cycler

## Slide 5: Basic requirements for PCR reaction:

## Slide 6: Standard PCR reaction:
DNA template (target) to be amplified. 1-5uL.
Two primers (forward and reverse).
Master mix.

## Slide 7: Master mix consist of :
1-2ul Taq polymerase. (optimum temperature at around 70C.)
1-2.5ul dNTPs.
4-7ul Buffer solution
1-2ul Divalent cations (Mg2+)
1-2ul Monovalent cation (k+1)

## Slide 8: PCR cycling steps:
Denaturation
Annealing
Extension

## Slide 9: Denaturation:
Double stranded DNA are separated to form single stranded DNA.
Temperature: 93-95C°.

## Slide 10: Annealing:
Primers bind to their complementary sequences.
Temperature: 50-70C° (depending on the melting temperature of the expected duplex).

## Slide 11: Extension:
DNA polymerase binds to the annealed primers and extends DNA at the 3’ end of the chain.
Temperature: 72C°

## Slide 12: PCR cycling steps:

## Slide 13: Standard PCR method:
Prepare mix containing primers, dNTP’s, buffer, Taq polymerase and water sufficient for all reaction tubes.
Aliquot appropriate volume to each tube.
Add DNA to each tube using a new tip for each sample.

## Slide 14: Standard PCR method:
Load tubes on PCR machine.
Cover the plate.
N.B If PCR machine does not have heated lid, 1 drop of mineral oil should be added to each tube before loading then start the program.

## Slide 15: Properties of Polymerase:
Taq polymerase originally isolated from Thermus aquaticus.
Heat stable (half life of about 30 min at 95C°).
Taq DNA polymerase has no proof-reading function in 3’ to 5’ direction.
Primer extension occurs at up to 100 bases/sec.
Plateau is eventually reached.

## Slide 16: Trouble Shooting:
Possible reasons | Problem
Primers annealing? | No product
Primers annealing elsewhere in genome? | Product of incorrect size
Contamination? Several annealing sites? | Several Products formed

## Slide 17: PCR Rxn inhibitors:
protinase K: digest polymerase
phenol: denature the polymerase.
EDTA: chelates Mg+2

## Slide 18: Advantages of PCR:
Uses less patient DNA.
Result obtained more quickly about 3hr for PCR.
No need to use radioactive material for PCR.
Precise in determining sizes of alleles.
Can be used to detect point mutations.

## Slide 19: Disadvantages of PCR:
Target DNA sequence must be known.
Errors made by Taq polymerase.
Size limitations particularly in GC rich triplet repeats.

## Slide 20: PCR Based Technologies:
Multiplex PCR
QF-PCR
RT-PCR