## Slide 1
Fluorometric determination of riboflavin
Lab 5

## Slide 2
Fluorescence is a kind of a luminescence, which is the emission of photons from electronically excited states.
Fluorescence occurs when the electron is transferred from a lower energy state into an "excited" higher energy state to form fluorescence.
Fluorescence

## Slide 3
The electron will remain in this state for 10⁻⁸ sec. then the electron returns to the lower energy state and it releases the energy in form of fluorescence.

## Slide 5
-In ultraviolet absorption spectroscopy when molecule absorbs UV radiation at one wavelength and its immediately re-emission, usually in a longer wavelength.
-Some molecules fluoresce naturally and others can be modified to make fluorescent compounds.
Fluorescence

## Slide 6
excitation
fluorescence
First excited state with four vibrational energy levels
Ground state with four Vibrational energy levels

## Slide 7
Fluorescent compounds have two characteristic spectra:
*an excitation spectrum (the wavelength and amount of light absorbed) and an emission spectrum (the wavelength and amount of light emitted).
These spectra are often referred as a compound's
fluorescence signature or fingerprint.
-No two compounds have the same fluorescence
signature. This principle makes fluorometry a
highly specific analytical technique.

## Slide 8
*What is fluorometery?
Fluorometry is the measurement of
fluorescence.
It’s measured by a fluorometer or
fluorimeter.
,

## Slide 9
A fluorometer involves using a beam of light, usually ultraviolet light.
A fluorometer generates the wavelength of light required to excite the analyte of interest.
it selectively transmits the wavelength of light emitted, then it measures the intensity of the emitted light.
The emitted light is proportional to the concentration of the analyte being measured .

## Slide 10
Fluorescence compounds:
1- aromatic and heterocyclic compounds.
2- compounds with multiple conjugated groups.
3- compounds containing electron donating groups as OH, NH2 ,OCH3...
4- poly cyclic compounds like vit K, purines, nucleosides, vit A .

## Slide 11
5- NADH fluorescence.
6- non fluorescence compounds when converts to fluorescent derivatives like:
Steroids
Metals by chelating.
Antibodies.

## Slide 12: Fluorescence spectra
Fluorescence is used primarily for quantitative
analysis in ppm (part per millions) .
F=Kфp₀ (2.3 abc)
Where F is fluorescence intensity
K instrument constant
Ф is the quantum efficiency
p₀ intensity of excitation
a molar absorptive, b cell path, c molar concentration,so F=K.c

## Slide 13
Advantages of fluorometer:
- Very specific
- Very sensitive.
- Wide Concentration Range
- Simplicity and Speed
- Low Cost

## Slide 14
Disadvantages:
*The fluorescence is very sensitive to environmental changes which include PH, temperature, solvent contamination and UV light used for excitation can make photochemical change

## Slide 15
Clinical uses of instrument
Uses to measure fluorescence for qualitative and quantitative analysis
Used to measure any substance that exists in small conc. for example: vitamins from blood sample.

## Slide 17: Instrumentation
1-Light Source:
The lamp or light source provides the energy that excites the compound by emitting light.
Light sources include xenon lamps, high pressure mercury vapor lamps.

## Slide 18
2-Excitation Filter /monochromator:
The excitation filter is used to screen out the wavelengths of unabsorbed light by the compound being measured.

## Slide 19
3-Sample Cell/Cuvette:
*the cuvette material must allow the
compound's absorption and
emission light energy to pass through.
*the size of cuvette affects the measurement.
The greater the pathlength (or diameter) of
the cell, the lower the concentration that can
be read.
Cuvettes are made from borosilicate or
quartz glass.

## Slide 20
4-Emission Filter(monochromator ):
Stray light emitted from the sample.

## Slide 21
5-Light Detector:
The light detector is most often a photomultiplier tube, so photodiodes are increasingly being used.
The light passing through the emission filter is detected by the photomultiplier or photodiode.
The light intensity, which is directly proportional (linear) to the compound's concentration, is registered as a digital readout.

## Slide 22
Schemating drawing

## Slide 23: Precautions
-pH
-Cleanliness of glassware.
-High standards of experimental technologist
are necessary to prevent quenching.
-Temperature.
-Cuvette Size (Pathlength)

## Slide 24: Riboflavin Experiment:
Riboflavin (vitamin B2) is strongly
fluorescent in 5% acetic acid solution.

## Slide 25: Chemical and solutions required
1- 5 % Acetic acid:
The addition of a few drops of glacial acetic acid to the solution will insure an acid pH and help to stabilize it.
2- Riboflavin stock solution .
3- Riboflavin standards solution 10( ppm)
4- Unknown.

## Slide 26: Preparation of standards
 | Blank | Std .1 | Std.2 | Std.3 | Std.4 | Std.5
Riboflavin stoc.std(10 ppm) | ............. | 0.2 ml | 0.4 ml | 0.6 ml | 0.8 | 1 ml
5% acetic acid |  | 9.8 ml | 9.6 ml | 9.4 ml | 9.4 ml | 9 ml

## Slide 27: Procedure
1- switch on the machine.
2- install the excitation and emission filtered in their holders.
3- start lamp (UV) by pressing 3-4 sec. the start switch and release it.
4- leave to warm up ,15 mins.
5- open the door of the instrument which acts as sample holder.

## Slide 28
6- adjust the range select or at x1 (excitation filter) for less conc. sample (ppm) and the higher range for higher conc. sample.
7- Put reagent blank cuvette in the sample holder, close the door and with the help of blank knob set read out to zero.
8- Remove reagent blank and insert the std. highest conc. And with help of attenuator knob set the read out to 100 and record this reading.

## Slide 29
9- Check twice for zeroing and 100 by inserting appropriate samples . If this not ok select higher range .
10- Take the reading for other std. and given unknown .

## Slide 30
 | blank | Std. 1 | std 2 | std 3 | std 4 | std 5
Conc. In ppm volume | 0 | 0.2 | 0.4 | 0.6 | 0.8 | 1.0
reading | 0 | 15.5 | 24. 7 | 52.9 | 92.4 | 100

## Slide 31
11- plot the graph and from the graph find out the conc. of unknown.
F
0
1
5
CONC.