## Slide 1: Radionuclide Production
Lab # 6

## Slide 2: Production of Radionuclide
Naturaly-occuring radionuclide are long-lived.
All radionuclides commonly administered to patients in nuclear medicine are artificially produced
Most are produced by cyclotrons, nuclear reactors, or radionuclide generators
The type of radionuclide produced in a cyclotron or a reactor depends on
  The irradiating particle
  Its energy
  The target nuclei

## Slide 3: Production of Radionuclide
Very short-lived radionuclides are available only in the institutions that have the cyclotron or reactor facilities; they cannot be supplied to remote institutions or hospitals because they decay rapidly.
For remote facilities there is a secondary source of radionuclides, particularly short-lived ones, which is called a radionuclide generator

## Slide 4: Making unstable isotopse
We have to change the ratio of neutrons (N) to protons (Z) to get outside the band of stability

## Slide 5: Nulcear bombardment
Hit nucleus of stable atoms with sub-nuclear particles: neutrons, protons, alpha particles etc.
Main methods of performing this bombardment
Inserting target in a nuclear reactor - fine for longer-lived radionuclide as some time is needed for processing and shipment
Using a charged-particle accelerator called a 'cyclotron' – needed locally for short-lived isotopes (T1/2 ~ 1 to 100 min).
We can also use longer-lived isotopes from a nuclear reactor that decay to a short-lived radioisotope in a portable 'generator'

## Slide 6: Common Radionuclides

## Slide 7: Cyclotrons-Produced Radionuclide
Charged particles such as protons, deuterons, a particles, 3He particles are accelerated in circular paths under vacuum by means of an electromagnetic field.
When targets of stable elements are irradiated by placing them in the external beam of the accelerated particles or in the internal beam at a given radius in a cyclotron, the accelerated particles irradiate the target nuclei and nuclear reactions take place.

## Slide 8: Cyclotrons-Produced Radionuclide
111Cd
12-MeV protons
An example of a simple cyclotron-produced radionuclide is 111In, which is produced by irradiating 111Cd with 12-MeV protons in a cyclotron.

## Slide 9: Cyclotrons-Produced Radionuclide
Since we are using proton bombardment we change the element and typically lie below the line of stability. Thus decay is typically by positron emission.
  Most cyclotron-produced radionuclides are neutron poor and therefore decay by positron emission or electron capture
Cyclotrons can be located locally, thus allowing for short lived isotopes.
Cylcotrons are very expensive to buy and operate.

## Slide 12: Nuclear Reactors
A nuclear reactor is constructed with fuel rods made of fissile materials such as enriched 235U
These fuel nuclei undergo spontaneous fission with extremely low probability.
Fission is defined as the breakup of a heavy nucleus into two fragments of approximately equal mass, accompanied by the emission of two to three neutrons with mean energies of about 1.5 MeV.
Neutrons emitted in each fission can cause further fission of other fissionable nuclei in the fuel rod provided the right conditions exist.

## Slide 13: Nuclear Reactors
This obviously will initiate a chain reaction, ultimately leading to a possible meltdown situation in the reactor.
This chain reaction must be controlled
To control a selfsustained chain reaction, excess neutrons (more than one) are removed by positioning cadmium rods in the fuel core (cadmium has a high probability of absorbing a thermal neutron).

## Slide 15: Generators
Why?
The use of short-lived radionuclides has grown considerably, because larger dosages of these radionuclides can be administered to the patient with only minimal radiation dose and produce excellent image quality.
This increasing appreciation of short-lived radionuclides has led to the development of radionuclide generators that serve as convenient sources of their production.

## Slide 16: Principles of a Generator
A generator is constructed on the principle of the decay-growth relationship between a long-lived parent radionuclide and its short-lived daughter radionuclide.
The chemical property of the daughter nuclide must be distinctly different from that of the parent nuclide so that the former can be readily separated

## Slide 17: Principles of a Generator
In a generator, basically a long-lived parent nuclide is allowed to decay to its short-lived daughter nuclide and the latter is then chemically separated.

## Slide 18: The importance of radionuclide generators lies in the fact that they are
Easily transportable
Serve as sources of short-lived radionuclides in institutions far from the site of a cyclotron or reactor facility

## Slide 19: History
The first commercial radionuclide generator was the 132Te (t1/2=78 hr)–132I (t1/2=2.3 hr) in the early 1960s.
Since then, a number of other generator systems have been developed and tried for routine use in nuclear medicine.
Only a few of these generators are of importance in nuclear medicine.
  They are the 99Mo–99mTc, 113Sn–113m In, 82Sr–82Rb, and 68Ge–68Ga systems.

## Slide 20: Structure and Mechanism
consists of a glass or plastic column fitted at the bottom with a fritted disk.
The column is filled with adsorbent material such as cation- or anion-exchange resin, alumina, and zirconia, on which the parent nuclide is adsorbed.
The daughter radionuclide grows as a result of the decay of the parent until either a transient or a secular equilibrium is reached within several half-lives of the daughter

## Slide 21: Structure and Mechanism
Because there are differences in chemical properties, the daughter activity is eluted in a carrierfree state with an appropriate solvent leaving the parent on the column.
After elution, the daughter activity starts to grow again in the column until an equilibrium is reached in the manner mentioned above; the elution of activity can be made repeatedly.

## Slide 22: Generator Activity Levels

## Slide 24
The daughter activity grown by the decay of the parent is separated chemically from the parent.
The eluent in vial A is drawn through the column and the daughter nuclide is collected in vial B under vacuum.
Typical generator system

## Slide 25
The vial containing the eluant is first inverted onto needle A, and
another evacuated vial is inverted onto the other needle B.

## Slide 26
The vacuum in the vial on needle B draws the eluant through the
column and elutes the daughter nuclide, leaving the parent
nuclide on the column.

## Slide 27: Generator produced radionuclide
Technetium-99m has been the most important radionuclide used in nuclear medicine
Short half-life (6 hours) makes it impractical to store even a weekly supply
The mother isotope in 99Mo, which is reactor produced.
Supply problem overcome by obtaining parent Mo-99, which has a longer half-life (67 hours) and continually produces Tc-99m
99Mo can be produced in a reactor or from fission products, but it cannot be produced in a cyclotron (99Mo is a beta emitter, requiring the addition of neutrons, not protons).

## Slide 28: Thank You