## Slide 1: Lec 2: Protocols

## Slide 2: What is protocol?
A protocol is a set of rules that governs the communications between computers on a network.
Functions of protocols:
  Addressing
  Data Packet Format
  Segmentation (Splitting long messages into small pieces)
  Embedding control information
  Detecting Errors
  Controlling data flow
  Controlling connection

## Slide 3: What is protocol stack?
A protocol stack is a complete set of network protocol layers that work together smoothly to provide networking capabilities such as accessing network resources & exchanging information.
It is called a stack because it is typically designed as a hierarchy of layers, each supporting the one above it and using those below it.
Example of protocol stack: TCP/IP

## Slide 4: What is TCP/IP?
is the suite of communications protocols that is used to connect hosts on the Internet and on most other computer networks as well.
It is also referred to as the TCP/IP protocol suite and the Internet protocol suite.

## Slide 5: Protocol Classification
By Routing Capabilities:
  Routable Protocols
  Non-routable Protocols
By Method Orientation:
  Connection oriented
  Connectionless
By Layer Level Tasks:
  Tasks on the Application Level
  Tasks on the Transport Level
  Tasks on the Network Level

## Slide 6: By Routing Capabilities:
Routable Protocols
  A communications protocol that contains a network address (IP Address) as well as a device address (MAC Address).
  Allows packets to be forwarded from one network to another.
  Used in both LAN or WAN
  Example: IP, IPX.
Non-routable Protocols
  A communications protocol that contains only a device address (MAC address) and not a network address (IP address).
  Does not incorporate an addressing scheme for sending data from one network to another
  Used only in LAN
  Example: NetBIOS

## Slide 7: By Method Orientation
Connection-oriented
  Establishes a secure connection between the sender and the receiver before exchanging data then close the connection after exchanging data.
  Advantage: Reliable (Because it guarantee the data arrival)
  Disadvantage: Slow data arrival
  Example: TCP (Transmission Control Protocol)
Connectionless
  Data is exchanged without prior arrangement or connection establishment.
  The sender transmits data to the receiver without ensuring that the recipient is available and ready to receive the data.
  Advantage: Fast data arrival
  Disadvantage: Not-reliable (Does not guarantee data arrival)
  Example: IP (Internet Protocol) - UDP (User Datagram Protocol)

## Slide 8: By Layer Level Tasks
Tasks on the application level (Application layer, Presentation layer, Session layer)
  Insure connection between user applications & the network server & exchange data between them.
  Example:
    File Transfer Protocol (FTP) allow transferring data between the sender & the receiver.
    Server Message Block (SMB)
    Simple Network Management Protocol (SNMP)

## Slide 9: By Layer Level Tasks
Tasks on the transport level (Transport Layer)
  Insure the security & the continuity of data transfer without any mistakes & is responsible for maintaining the quality & the accuracy of the exchanged information between devices.
  Examples:
    Transmission Control Protocol (TCP)
    User Data Protocol (UDP)

## Slide 10: By Layer Level Tasks
Tasks on the network level (Data link layer – Network layer):
  Include tasks performed by data link layer & network layer.
  It routes messages
  Assign address to messages
  Establish path between the sender & the receiver.
  Example:
    IPX Protocol: It is a connectionless unreliable routable network protocol
    IPX corresponds to IP protocol from the TCP/IP suite which is responsible for addressing & routing data.

## Slide 11: Protocols used in Network Management
Simple Network Management Protocol (SNMP)
  It is a protocol for managing networks & controlling them to get the best network performance & generating statistical reports about network hardware & maintaining the network security.
  Functions:
    Performance management
    Network setup management
    Error detection management
    Network security management
    Account management on the network

## Slide 12: Protocols used in Network Management
Common Management Information Protocol (CMIP)
  Monitoring & controlling (ISO) standards on the network, referred to as (C_MIP)
    (C.MOT) Cmip Over TCP/IP
    A copy from (C.MIP) that works on the TCP/IP networks
    (C.MOL) Cmip Over IEEE 802 (Ethernet, Token ring)
    A copy from (C_MIP) works on network with the same bandwidth.(ex: Eithrnet, Token Ring)

## Slide 13: Protocols used in Network Management
Distributed Management Environment (DME)
  A protocol for managing & controlling networks defined by open source systems & it is not widely used.
Transmission Control Protocol/ Internet Protocol (TCP/IP)
  Suite of protocols that allow networks & deferent kind of network devices to be connected to each other.
  It has becomes the standard protocol that is used to guarantee the compatibility between different kind of devices.
  Supported by LAN & WAN networks.

## Slide 14: Protocols used in Network Management
  A Transmission Control Protocol (TCP)
    It is a connection oriented transport protocol used with the group of (TCP/IP) protocols.
    Monitors the size of the information sent over the network.
    (Reliable) Ensure data arrival in the correct format to the intended recipient.
  4. B Internet Protocol (IP)
  A protocol that receives data packets from UDP or TCP protocol & adds to the header an IP address

## Slide 15: Protocols used in Network Management
  C User Datagram Protocol (UDP)
  A connection-less transport protocol that is one of the core protocols of the Internet protocol suite & alternative to the TCP.
  Usable to send large amount of data in short time.
  Example: Live broadcasting of video conferencing

## Slide 16: Protocols used in Network Management
  D Internet Control Management Protocol (ICMP)
  One of the TCP/IP protocols for sending & controlling error messages.
  Example: Router uses this protocol to inform the sender that the receiver is not available.
  E Address Resolution Protocol (ARP)
  One of the TCP/IP protocols used to get the MAC address (physical address) from the IP address (logical address).
  This protocol works by sending the IP address in the network & the work station that has that IP address responds by sending its physical address.

## Slide 17: Protocols used in Network Management
  F Reverse Address Resolution Protocol
  It is one of the TCP/IP suite protocols used to get the IP address (logical address) from the MAC address (physical address)
  G Dynamic Host Configuration Protocol (DHCP)
  It is one of the TCP/IP protocols automatically assign IP addresses users who join the TCP/IP network so that no need to manually assign IP addresses.
  Used in ISDN routers & in MODEM router that allow users to connect to the Internet.

## Slide 18: Protocols used in Network Management
Internet Packet eXchange (IPX)
It is one of the Netware operating system protocol works exactly as IP address in the TCP/IP.
It contain the network address and allow messages to be routed into specified network but it does not guarantee the completeness in the message arrival.
  Netware: Group of operating systems from (NOVELL) that help other operating systems such as: Windows, Macintosh, DOS, OS12

## Slide 19: Summary