## Slide 1: The OSI Model and the TCP/IP Protocol Suite
Outline:
  Protocol Layers
  OSI Model
  TCP/IP Model
  Addressing

## Slide 2: OBJECTIVES
To discuss the OSI model and its layer architecture and to show the interface between the layers.
To briefly discuss the functions of each layer in the OSI model.
To introduce the TCP/IP protocol suite and compare its layers with the ones in the OSI model.
To show the functionality of each layer in the TCP/IP protocol with some examples.
To discuss the addressing mechanism used in some layers of the TCP/IP protocol suite for the delivery of a message from the source to the destination.

## Slide 3: Computer Network Components
    Computer with NIC (PCs, laptops, handhelds)
    routers & switches (IP router, Ethernet switch)
    Links” Transmission media” (wired, wireless)
    protocols (IP,TCP,CSMA/CD,CSMA/CA)
    applications (network services) i.e. Network Operating System (NOS)
    humans and service agents

## Slide 4: Protocol “Layers”
Networks are complex!
many “pieces”:
  hosts
  routers
  links of various media
  applications
  protocols
  hardware, software
Question:
Is there any hope of organizing structure of network?
Or at least our discussion of networks?

## Slide 5: Organization of air travel
a series of steps
ticket (purchase)
baggage (check)
gates (load)
runway takeoff
airplane routing
ticket (complain)
baggage (claim)
gates (unload)
runway landing
airplane routing
airplane routing

## Slide 6: Layering of airline functionality
Layers: each layer implements a service
  via its own internal-layer actions
  relying on services provided by layer below
ticket (purchase)
baggage (check)
gates (load)
runway (takeoff)
airplane routing
departure
airport
arrival
airport
intermediate air-traffic
control centers
airplane routing
airplane routing
ticket (complain)
baggage (claim
gates (unload)
runway (land)
airplane routing
ticket
baggage
gate
takeoff/landing
airplane routing

## Slide 7: Why layering?
Dealing with complex systems:
explicit structure allows identification, relationship of complex system’s pieces
  layered reference model for discussion
modularization eases maintenance, updating of system
  change of implementation of layer’s service transparent to rest of system
  e.g., change in gate procedure doesn’t affect rest of system

## Slide 8: What’s a protocol?
human protocols:
“what’s the time?”
“I have a question”
introductions
… specific msgs sent
… specific actions taken when msgs received, or other events
network protocols:
machines rather than humans
all communication activity in Internet governed by protocols
protocols define format, order
of msgs sent and received among
network entities,
and actions taken on msg transmission
, receipt

## Slide 9: What’s a protocol?
a human protocol and a computer network protocol:
Q: Other human protocols?
Hi
Hi
Got the
time?
2:00
TCP connection
request
TCP connection
response
Get http://www.awl.com/kurose-ross
<file>
time

## Slide 10: PROTOCOL LAYERS
We discussed that a protocol is required when two entities need to communicate.
When communication is not simple, we may divide the complex task of communication into several layers.
Let us use a scenario in communication in which the role of protocol layering may be better understood.
We use two examples. In the first example, communication is so simple that it can occur in only one layer.

## Slide 11: Example 1
Assume Maria and Ann are neighbors with a lot of common ideas. However, Maria speaks only Spanish, and Ann speaks only English.
Since both have learned the sign language in their childhood, they enjoy meeting in a cafe a couple of days per week and exchange their ideas using signs.
Occasionally, they also use a bilingual dictionary. Communication is face to face and Happens in one layer as shown in Figure.

## Slide 12: Example 2
Now assume that Ann has to move to another town because of her job. Before she moves, the two meet for the last time in the same cafe.
Although both are sad, Maria surprises Ann when she opens a packet that contains two small machines.
  The first machine can scan and transform a letter in English to a secret code or vice versa.
  The other machine can scan and translate a letter in Spanish to the same secret code or vice versa.
Ann takes the first machine; Maria keeps the second one.
The two friends can still communicate using the secret code, as shown in Figure.

## Slide 13: PROTOCOL LAYERS
Network activity involves sending data from one computer to another. This complex process can be broken into discrete, sequential tasks. The sending computer must:
  Recognize the data.
  Divide the data into manageable chunks.
  Add information to each chunk of data to determine the location of the data and to identify the receiver.
  Add timing and error-checking information.
  Put the data on the network and send it on its way.
In this case, we may need several protocols, one for each layer.

## Slide 14: THE OSI MODEL
In 1978, the International Organization for Standardization (ISO) released a set of specifications that described network architecture for connecting dissimilar devices.
Established in 1947, the International Standards Organization (ISO) is a multinational body dedicated to worldwide agreement on international standards.
Almost three-fourths of countries in the world are represented in the ISO.
An ISO standard that covers all aspects of network communications is the Open Systems Interconnection (OSI) model.

## Slide 15
ISO is the organization;
OSI is the model.
Note

## Slide 16: Topics Discussed in the Section
Layers in the OSI Model
Layered Architecture
Layer-to-layer Communication
Encapsulation

## Slide 17: OSI Model Layers
The OSI reference model architecture divides network communication into seven layers.
Each layer covers different network activities, equipment, or protocols.
Layering specifies different functions and services as data moves from one computer through the network cabling to another computer.

## Slide 18: OSI Model Layers
Each layer provides some service or action that prepares the data for delivery over the network to another computer.
The lowest layers—1 and 2—define the network's physical media and related tasks, such as putting data bits onto the network interface cards (NICs) and cable.
The highest layers define how applications access communication services.
The higher the layer, the more complex its task.

## Slide 19: OSI Model Layers
Also, the OSI reference model defines how each layer communicates and works with the layers immediately above and below it.
The layers are separated from each other by boundaries called interfaces.
The interface defines the services offered by the lower networking layer to the upper one and further defines how those services will be accessed.
All requests are passed from one layer, through the interface, to the next layer.
Each layer builds upon the standards and activities of the layer below it.
Each layer provides services to the next-higher layer and shields the upper layer from the details of how the services below it are actually implemented.

## Slide 20
OSI layers

## Slide 21: OSI Model Layers
With the exception of the lowest layer in the OSI networking model, no layer can pass information directly to its counterpart on another computer. Instead, information on the sending computer must be passed down through each successive layer until it reaches the physical layer.
The information then moves across the networking cable to the receiving computer and up that computer's networking layers until it arrives at the corresponding layer.

## Slide 22: OSI Model Layers
But, we can visualize that each layer has a direct communication with its associated layer on the other computer. This provides a logical, or virtual, communication between peer layers

## Slide 23
An exchange using the OSI model ( Encapsulation)

## Slide 24: Encapsulation
Before data is passed from one layer to another, it is broken down into packets, or units of information, which are transmitted as a whole from one device to another on a network.
At the sender, each layer adds additional formatting or addressing to the packet, which is needed for the packet to be successfully transmitted across the network.
At the receiving end, the packet passes through the layers in reverse order. Each layer reads the information on the packet, strips it away, and passes the packet up to the next layer.
When the packet is finally passed up to the application layer, the packet is in its original form, which is readable by the receiver.

## Slide 25: Encapsulation
source
application
transport
network
link
physical
Ht
Hn
M
segment
Ht
datagram
destination
application
transport
network
link
physical
Ht
Hn
Hl
M
Ht
Hn
M
Ht
M
M
network
link
physical
link
physical
Ht
Hn
Hl
M
Ht
Hn
M
Ht
Hn
M
Ht
Hn
Hl
M
router
switch
message
M
Ht
M
Hn
frame

## Slide 26: TCP/IP Model
The TCP/IP protocol suite was developed prior to the OSI model.
Therefore, the layers in the TCP/IP protocol suite do not match exactly with those in the OSI model.
The original TCP/IP protocol suite was defined as four layers. Today, however, TCP/IP is thought of as a five-layer model.
Application
Troubleshooting, file sharing, internet
Transport
Flow control, error control
Internet
Network Access
IP addressing and routing of network traffic
Interface with the physical network

## Slide 27: Comparison between OSI and TCP/IP
IOS Model
Application
Presentation
Session
Transport
Network
Data Link
Physical
TCP/IP Model
Application
Transport
Internet
Network Access

## Slide 28: LAYERS IN THE OSI MODEL
In this section we briefly describe the functions of each layer in the OSI model.

## Slide 29
A private internet

## Slide 30: Physical layer
The physical layer coordinates the functions required to transmit a bit stream over a physical medium.
It defines the procedures and functions that physical devices and interfaces have to perform for transmission occur.
The physical layer is concerned with the following:
  Physical characteristics of interfaces and media:
  Representation of the bits
  Data rate, the number of bits sent each second.
  Line configuration, Point to point or multipoint configuration.
  Physical topology
  Transmission Mode : Simplex, half duplex or full duplex

## Slide 31
The physical layer is responsible for moving individual bits from one
(node) to the next.
Note

## Slide 32
Communication at the physical layer

## Slide 33
The unit of communication at the physical layer is a bit.
Note

## Slide 34: Link Layer: Introduction
Some terminology:
hosts and routers are nodes
communication channels that connect adjacent nodes along communication path are links
  wired links
  wireless links
  LANs
layer-2 packet is a frame, encapsulates datagram
data-link layer has responsibility of
transferring datagram from one node
to adjacent node over a link

## Slide 35: Link layer: context
datagram transferred by different link protocols over different links:
  e.g., Ethernet on first link, frame relay on intermediate links, 802.11 on last link
each link protocol provides different services
  e.g., may or may not provide rdt over link
transportation analogy
trip from Princeton to Lausanne
  limo: Princeton to JFK
  plane: JFK to Geneva
  train: Geneva to Lausanne
tourist = datagram
transport segment = communication link
transportation mode = link layer protocol
travel agent = routing algorithm

## Slide 36: Link Layer Services
framing, link access:
  encapsulate datagram into frame, adding header, trailer
  channel access if shared medium
  “MAC” addresses used in frame headers to identify source, dest
    different from IP address!

## Slide 37: Link Layer Services (more)
flow control:
  pacing between adjacent sending and receiving nodes
error detection:
  errors caused by signal attenuation, noise.
  receiver detects presence of errors:
    signals sender for retransmission or drops frame
error correction:
  receiver identifies and corrects bit error(s) without resorting to retransmission
half-duplex and full-duplex
  with half duplex, nodes at both ends of link can transmit, but not at same time

## Slide 38: Where is the link layer implemented?
in each and every host
link layer implemented in “adaptor” (aka network interface card NIC)
controller
physical
transmission
cpu
memory
host
bus
(e.g., PCI)
network adapter
card
host schematic
application
transport
network
link
link
physical

## Slide 39: Data Link Layer
The data link layer transforms the physical layer, a raw transmission facility, to a reliable link ( it make the physical layer appear error-free to the upper layer)
it responsible for node-to-node delivery.
The Data Link layer is concerned with the following:
  Framing.
  Physical addressing, each node has its unique address.
  Flow Control.
  Access Control.
  Error control, normally achieved through a trailer to the end of the frame.

## Slide 40
Communication at the data link layer

## Slide 41
The unit of communication at the data link layer is a frame.
Note

## Slide 42: Network layer
transport segment from sending to receiving host
on sending side encapsulates segments into data grams.
on receiving side, delivers segments to transport layer.
network layer protocols in every host, router
router examines header fields in all IP data grams passing through it
application
transport
network
data link
physical
application
transport
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical

## Slide 43: Two Key Network-Layer Functions
forwarding: move packets from router’s input to appropriate router output
routing: determine route taken by packets from source to dest.
  routing algorithms
analogy:
routing: process of planning trip from source to dest
forwarding: process of getting through single interchange

## Slide 44: Network Layer
Is responsible for the source-to-destination delivery of a packet possible across multiple networks.
Functions:
  Logical addressing.
  Routing, It determines which path the data should take based on network conditions, priority of service, and other factors.

## Slide 46
The unit of communication at the network layer is a datagram (Packet).
Note

## Slide 47: Transport Layer
The transport layer is responsible for process-to-process delivery of the entire message.
Makes sure that the data arrives without errors, in the proper sequence and in a reliable condition.
Functions:
  Port addressing, The network layer gets each packet to the correct computer; the transport layer gets the entire message to the correct process on that computer.
  Segmentation and reassembly: a message is divided into transmittable segments, each having a sequence number
  Connection control: The transport layer can be either connectionless or connection-oriented.
  Flow control
  Error control
Notes:     A connectionless transport layer treats each segment as an independent packet and delivers it to the transport layer at the destination machine.
    A connection-oriented transport layer makes a connection with the transport layer at the destination machine first before delivering the packets. After all the data are transferred, the connection is terminated.

## Slide 48
Communication at transport layer

## Slide 49
The unit of communication at the transport layer is a segment, user datagram, or a packet, depending on the specific protocol used in this layer.
Note