## Slide 1: Lec 5: SNMP Network Management

## Slide 2: What is protocol?
TCP/IP network management model:
  Management station
  Management agent
  Management information base
  Network management protocol

## Slide 3: Management Station
Is a stand-alone device
A set of management applications for data analysis, fault recovery
An interface by which network manager monitors and controls the network
A database of information extracted from the MIBs of all the managed entities in the network

## Slide 4: Management Station
Performs the monitoring function by retrieving the value of MIB objects
Cause an action to take place at an agent
Changes the configuration settings at an agent by modifying the value of specific variables

## Slide 5: Management Agent
Equipped on key platforms
  Hosts, bridges, routers, and hubs
Managed from a management station
Responds to requests for information
  Action from the management station
  Asynchronously provides the management with important but unsolicited information

## Slide 6: Management Information Base
Object
  Represented the managed resources in the network
  Is a data variable that represents one aspect of managed agent
MIB
  The collection of objects
  Functions as a collection of access points at the agent for the management station
    Objects are standardized across systems of a particular class
      Used for the management of routers

## Slide 7: Network Management Protocol
Linked the management station and agents
Simple Network Management Protocol (SNMP)
  Used for the management of TCP/IP networks
  Key capabilities
    Get
      Enables the management station to retrieve the value of objects at the agent
    Set
      Enables the management station to set the value of objects at the agent
    Trap
      Enables an agent to notify the management station of significant event

## Slide 8: Network Management Protocol Architecture
Designed to be an application-level protocol that is part of the TCP/IP protocol suite
  Operates over UDP
Management station
  Manager process
Controls access to a central MIB at the management station
Provides an interface to the network manager
Achieves network management by using SNMP
  Implemented on top of UDP. IP, and the relevant network-dependent protocols
Managed devices
  Agent
    Implements SNMP, UDP, IP
    Interprets the SNMP messages and controls the agent’s MIB

## Slide 9: Configuration of SNMP

## Slide 10: Network Management Example
A management application of NMS calls for the service of the management process
The management process calls the SNMP manager
The SNMP manager constructs a request packet and sends it to SNMP agent
The SNMP agent passes the packet to the agent process
The agent process accesses the values of the requested variable and passes it to the SNMP agent

## Slide 11: Network Management Example
The SNMP agent constructs the response packet
And sent it to the SNMP manager
The SNMP manager receives the response packet and passes it to management process the management process.
The management process either passes the
requested values to the application program that displays it, perhaps using a Graphical User Interface (GUI), or stores it in memory for later retrieval.

## Slide 12: SNMP Protocol
SNMP management station
  getRequest
  getNextRequest
  setRequest
SNMP agent
  GetResponse
    The form of acknowledged message by the agent
    Passed up to the management application
  Trap
Issues by agent to response to an event that effects the MIB and the underlying managed resources

## Slide 13: The Role of SNMP

## Slide 14: Trap Directed Polling
If the number of managed agents is large, and if each agent maintains a large number of objects
  Management station becomes impractical regularly to poll all agents for all object data
At initialization time, and at infrequent intervals
  Management station poll all of the agents for some key information
  Interface characteristics
  Baseline performance statistics
    Packet count

## Slide 15: Trap Directed Polling
Once baseline is established
  Management station refrains from polling
  Each agent notifies the management station of any unusual event – traps
    Agent crashes and is rebooted
    Link fails
    Overload condition as defined by the packet load crosses some threshold

## Slide 16: Trap Directed Polling
Management station may choose to take some action
  Is alerted to an exception condition
  May directly poll to the agent reporting the event and to some nearby agents to diagnose any problem
  Gain more specific information about the exception condition
Results in substantial savings of network capacity and agent processing time

## Slide 17: Overhead of Network Management System
The number of CPU cycles
  Management application program
  SNMP protocol
    Constructs a request packet
    the number of control bytes supplied by the protocol stack layers
  Large storage for management stations and management agents
  The amount of traffic generated by network management packets