## Slide 1
Packetizing
Error Detection
07/30/26
<number>

## Slide 2: The Data Link Layer
Data link layer is responsible for carrying a packet ( called frame) from one hop to the next hop.
Specific responsibilities of the data link layer include framing, addressing, flow control, error control, and media access control.
07/30/26
<number>

## Slide 3
07/30/26
<number>

## Slide 4: How Networks Send Data
To send data over a network, the data is broken down into small, manageable packets , each wrapped with the essential information needed to get it from its source to the correct destination .
In the sender, data is disassembled in small chunks.
Then it reassemble in the proper order when it reaches its destination.
07/30/26
<number>

## Slide 5: The Function of Packets in Network Communications
Networks cannot operate if computers put large amounts of data on the cable at the same time.
07/30/26
<number>
Notes: As you see in the figure, a computer sending large amounts of data causes other computers to wait (increasing the frustration of the other users) while the data is being moved. This is not called "sharing"; it is called "monopolizing the network.“
In order for many users at once to transmit data quickly and easily across the network, the data must be broken into small, manageable chunks. This way, users each get their share of access to the network. These chunks are called packets, or frames
<number>

## Slide 6: The Function of Packets in Network Communications
There are two reasons why putting large chunks of data on the cable at one time slows down the network:
  Large amounts of data sent as one large unit tie up the network and make timely interaction and communications impossible because one computer is flooding the cable with data.
  The impact of retransmitting large units of data further multiplies network traffic.
These effects are minimized when the large data units are reformatted into smaller packages for better management of error correction in transmission.
07/30/26
<number>
Notes: This way, only a small section of data is affected, and, therefore, only a small amount of data must be retransmitted, making it relatively easy to recover
from the error.
.
<number>

## Slide 7: Components of Packets
  Packets contents are based on the protocol used , but they basically contain:
  Source address
  Destination address
  Data to be sent ( files & messages)
  Other information like:
    Giving instructions to the network on how to send data
    Telling the receiving computer how to collect and arrange packets.
    Checking data from errors (determine the need to resend the data)
07/30/26
<number>

## Slide 8
error-checking component
07/30/26
<number>

## Slide 9
07/30/26
<number>

## Slide 10: Accuracy of the Transmitted Data
Data can be corrupted during transmission.
For reliable communication, errors must be detected and corrected.
07/30/26
<number>

## Slide 11: Single-Bit Error
  In a single-bit error, only one bit in the data unit has changed. (0 → 1 or 1 → 0)
07/30/26
<number>

## Slide 12: Burst Error
Two or more bits in the data unit have changed
Burst error does not necessarily mean that the errors occur in consecutive bits
Corrupted Bits = 4 bits
07/30/26
<number>

## Slide 13: Error Detection
Error detection uses the concept of redundancy, which means adding extra (redundant) bits for detecting errors at the destination
07/30/26
<number>
Notes: Redundancy is achieved through various coding schemes. The sender adds redundant
bits through a process that creates a relationship between the redundant bits and the
actual data bits. The receiver checks the relationships between the two sets of bits to
detect or correct the errors
<number>

## Slide 14: Error Detection Methods
07/30/26
<number>
Three types of redundancy checks:

## Slide 15: Parity Check
The most common and least expensive
a parity bit (extra bit)is added to every data unit so that the total number of 1’s is even or odd.
Simple parity check can detect single bit errors.
It can detect burst errors only if the total number of errors in each data unit is odd.
07/30/26
<number>

## Slide 16: Even/odd parity
Computers can sometimes make errors when they transmit data.
Even/odd parity:
is basic method for detecting if an odd number of bits has been switched by accident.
    Odd parity:
      The number of 1-bit must add up to an odd number
    Even parity:
      The number of 1-bit must add up to an even number
07/30/26
<number>

## Slide 17: Even/odd parity
The computer knows which parity it is using
If it uses an even parity:
  If the number of of 1-bit add up to an odd number then it knows there was an error:
If it uses an odd:
  If the number of of 1-bit add up to an even number then it knows there was an error:
However, If an even number of 1-bit is flipped the parity will still be the same. But an error occurs
  The even/parity can’t this detect this error.
07/30/26
<number>

## Slide 18: Even/odd parity
It is useful when an odd number of 1-bits is flipped.
Suppose we have an 7-bit binary word (7-digits).
  If you need to change the parity you need to add 1 (parity bit) to the binary word.
  You now have 8 digit word.
  However, the computer knows that the added bit is a parity bit and therefore ignore it.
07/30/26
<number>

## Slide 19: Example (1)
Suppose you receive a binary bit word “0101” and you know you are using an odd parity.
Is the binary word errored?
The answer is yes:
    There are 2 1-bit, which is an even number
    We are using an odd parity
    So there must have an error.
07/30/26
<number>

## Slide 20
A single bit is appended to each data chunk
  makes the number of 1 bits even/odd
Example: even parity
  1000000(1)
  1111101(0)
  1001001(1)
Example: odd parity
  1000000(0)
  1111101(1)
  1001001(0)
07/30/26
<number>

## Slide 21: Parity Checking
Assume we are using even parity with 7-bit ASCII.
The letter V in 7-bit ASCII is encoded as 0110101.
How will the letter V be transmitted?
  Because there are four 1s (an even number), parity is set to zero.
  This would be transmitted as: 01101010.
If we are using an odd parity:
  The letter V will be transmitted as 01101011
07/30/26
<number>

## Slide 22: Exercise 1
Suppose you are using an odd parity. What should the binary word “1010” look like after you add the parity bit?
Answer:
  There is an even number of 1-bits.
  So we need to add another 1-bit
  Our new word will look like “10101”.
07/30/26
<number>

## Slide 23: Exercise 2
Suppose you are using an even parity. What should the binary word “1010” look like after you add a parity bit?
Answer:
  There is an even number of 1’s.
  So we need to add another 0
  Our new word will look like “10100”.
07/30/26
<number>

## Slide 24: Parity Check
07/30/26
<number>
0 | 0 | 1 | 0 | 1 | 0 | 1 | 1
0 | 0 | 1 | 0 | 1 | 0 | 1 | 1
Sender
Receiver
0 | 0 | 1 | 0 | 1 | 0 | 1
Data
Data + Redundancy Bits
The Medium
0 | 0 | 1 | 0 | 1 | 0 | 1
Even?
Yes , Drop parity bit & accept data
No
Reject Data
Calculate Parity bit
Count bits
Notes: <number>

## Slide 25: Cyclic Redundancy Check (CRC)
07/30/26
<number>
Used for error checking
Unlike the parity check which is based on addition, CRC is based on binary division.
Before sending data ,some calculation are done on the data packets to generate a CRC number
The CRC is calculated so the packet ( data + CRC ) becomes exactly divisible by a predetermined number.
When data is received , the packet is divided by the number.

## Slide 26: Cyclic Redundancy Check (CRC)
If the reminder “0” : data is correct
If the reminder “1” : data has a problem and need to be sent again.
CRC Can detect single bit & burst errors.
07/30/26
<number>

## Slide 27: Checksum
Uses a process known as checksum to generate an error-detection character appended to the data.
This calculation is applied in both the sender side and the receiver side
  A match between receiver checksum and transmitted checksum indicates good data.
  A mismatch indicates an error has occurred.
Capable of detecting single or burst errors.
It is simple to implement in either hardware or software.
07/30/26
<number>

## Slide 28
Multiple Access Methods

## Slide 30: Multiple Access Methods
When nodes or stations are connected and use a common link (cable or air) , called a multipoint or broadcast link, we need a multiple-access protocol to coordinate access to the link.
It is a set of rules that defines how a stations puts data onto the link and takes data from the link .

## Slide 31: Multiple Access Methods
Many formal protocols have been devised to handle access to a shared links. We categorize them into three groups.

## Slide 32: CONTROLLED ACCESS
In controlled access, the stations consult one another to find which station has the right to send.
A station cannot send unless it has been authorized by other stations.
Two methods:
Polling Access Method
Token Passing Access Method
Notes: In these access methods, no contention and no collision take place.
<number>

## Slide 33: 1 Polling Access Method
In this access method, one station is designated as the primary device and the others are secondary stations.
All access to the network is controlled by the primary station.
The primary queries (polls) each of the secondary stations in turn, if it has information to be transmitted.
Only when it is polled does the secondary have access to the communication channel.

## Slide 34: 2 Token-Passing Access Method
In this access method, a special type of packet, called a token, circulates around a cable ring from station to station .
When any station on the ring needs to send data across the network, it must wait for a free token.
When a free token is detected, the station will take control of it if the station has data to send.

## Slide 35: Random Access Methods
In random access or contention methods, no station is superior to another station and none is assigned the control over another (i.e. each station has the right to the medium without being controlled by any other station).
It is named contention method because stations on the network contend, or compete, for an opportunity to send data.
Methods:
  Carrier-Sense Multiple Access With Collision Detection
  Carrier-Sense Multiple Access With Collision Avoidance

## Slide 36: Carrier-Sense Multiple Access
In this way of methods, each station first listen to the cable (or check the state of the cable ) before sending.
When the station "senses" that the cable is free ( that there is no traffic on the cable) it can send a frame.
Once the station has transmitted frame on the cable, no other station can transmit data until the original data has reached its destination and the cable is free again.

## Slide 37: Collisions
Even though each station listens for network traffic before it attempts to transmit, an access conflict -collision- will happen if more than one station tries to send at the same time.
When a collision happened, the frames will be either destroyed or modified
The collisions occur because it takes time for signals to propagate through the link.
Two specialized methods of collision management have been developed to improve performance: Collision Detection (CD) and Collision Avoidance (CA).

## Slide 39: Carrier-Sense Multiple Access With Collision Detection
The carrier-sense multiple access with collision detection (CSMA/CD) adds a procedure to handle a collision.
In this method, a station monitors the medium after it sends a frame to see if the transmission was successful. If so, the station is finished. If, however, there is a collision, the frame is sent again.
In the case of collision, the two stations involved stop transmitting for a random period of time and then attempt to retransmit.
Each station determines its own waiting period; this reduces the chance that the computers will once again transmit simultaneously.

## Slide 40: Carrier-Sense Multiple Access With Collision Avoidance
The Carrier-Sense Multiple Access With Collision Avoidance (CSMA/CA) differs from the previous method in that there is no collision.
Each station signals its intent to transmit before it actually transmits data.

## Slide 41: CHANNELIZATION
Channelization is a multiple-access method in which the available bandwidth of a link is shared in time, frequency, or through code, between different stations.
Used for wireless communications.
Methods:
  Frequency division Multiple Access
  Time division Multiple Access
  Code division Multiple Access

## Slide 42: Frequency-Division Multiple Access
In frequency-division multiple access (FDMA), the available bandwidth is divided into frequency bands.
Each station is allocated a band to send its data. In other words, each band is reserved for a specific station, and it belongs to the station all the time.

## Slide 43: Time-division Multiple Access
In time-division multiple access (TDMA), the stations share the bandwidth of the channel in time.
Each station is allocated a time slot during which it can send data.
Each station transmits its data in is assigned time slot.

## Slide 44: Code-Division Multiple Access
In the code-division multiple access (CDMA), each station assigned a code that used to send its data.
Several transmitters can send information simultaneously over a single communication channel.
CDMA differs from FDMA because only one channel occupies the entire bandwidth of the link.
It differs from TDMA because all stations can send data simultaneously; there is no timesharing.
Notes: <number>