## Slide 1: Ethernet and Token Ring LAN Networks

## Slide 2: Local Area Network
local area network (LAN) is a computer network that is designed for a limited geographic area such as a building or a campus.
Although a LAN can be used as an isolated network, most LANs today are also linked to a wide area network (WAN) or the Internet.
A computer connected via a LAN to the Internet needs all the 5 layers of the TCP/IP model.
The three upper layers are common to all LANs.
The LANs differ in the 2 lower layers.

## Slide 3: IEEE Project 802
In 1985, the Computer Society of the IEEE started a project, called Project 802, to set standards to enable intercommunication among equipment from a variety of manufacturers.
Project 802 does not seek to replace any part of the OSI or the TCP/IP model.
Instead, it is a way of specifying functions of the physical layer and the data link layer of major LAN protocols.
The IEEE has subdivided the data link layer into two sublayers:
  logical link control (LLC) and media access control (MAC).

## Slide 4: IEEE Project 802 cont.
IEEE has also created several physical layer standards for different LAN protocols.
Flow control and error control duties are collected into the LLC sublayer.
MAC sublayer governs the operation of access method.
Framing is handled in both the LLC sublayer and the MAC sublayer.
The LLC sublayer is the same for all LANs.
The LANs differ in their MAC sublayer and in their physical layer.

## Slide 6: LANs
The LAN market has seen several technologies such as Ethernet, Token Ring, Token Bus, FDDI, and ATM LAN.
Some of these technologies survived for a while, but Ethernet is by far the dominant technology.

## Slide 7: Ethernet

## Slide 8: Ethernet
Ethernet is the most popular LAN.
Ethernet use CSMA/CD as an access method.
Traditional Ethernet is designed to operate at 10 Mbps.
For a higher data rate, Fast Ethernet is designed to operate at 100 Mbps.
For an even higher data rate, Gigabit Ethernet is designed to operate at 1000 Mbps.
There are four different implementations for baseband (digital), Traditional Ethernet :
  10 Base 5
  10 Base 2
  10 Base-T
  10 Base-FL

## Slide 9: The Ethernet Frame Format
The Ethernet frame include the following fields:
Description | Frame field
Marks the start of the frame | Preamble
The origin and destination physical addresses | Destination and source addresses
Used to identify the network layer protocol | Type
The data encapsulated from the upper layer protocol. | Data
Error-checking field to determine if the frame arrived without being corrupted | Cyclical redundancy check (CRC)

## Slide 10: 10 Base5: Thick Ethernet
It is sometimes called thick Ethernet, or Thicknet.
This Ethernet LAN makes use of thick coaxial cable.
It uses a bus topology with an external transceiver (transmitter/receiver) connected via a tap to the thick coaxial cable.
The transceiver is responsible for transmitting, receiving, and detecting collisions.
The maximum length of the coaxial cable must not exceed 500 m.
Can support as many as 100 nodes (stations, repeaters, and so on) per backbone segment.

## Slide 11
Transceiver cables or drop cable that connects the transceiver to the NIC.

## Slide 12: 10Base2: Thin Ethernet
It is called thin Ethernet, or Cheapernet.
The size of the coaxial cable is much thinner and more flexible than the 10Base5.
It also uses a bus topology applied as a daisy chain.
In this Ethernet, the transceiver is normally part of the network interface card (NIC), which is installed inside the station.
Note that the collision here occurs in the thin coaxial cable.
This implementation is more cost effective than 10Base5 because thin coaxial cable is less expensive than thick coaxial.
The length of each segment cannot exceed 200 m.
Can support up to 30 nodes per backbone segment.

## Slide 14: 10BaseT
It uses twisted-pair cable to connect computers.
It use a physical star topology, but internally they use a bus signaling system like other Ethernet configurations.
The stations are connected to a hub via two pairs of twisted cable, one pair is used to receive data and one pair is used to transmit data.
Any collision here happens in the hub.
The maximum length of a 10BaseT segment is 100m.
Can support up to 1024 nodes.

## Slide 16: 10Base-F
10 Base-F uses a star topology to connect stations to a hub.
The stations are connected to the hub using two fiber-optic cables.
The segment length is 2,000 m.

## Slide 17: Token Ring

## Slide 18: Token Ring
The Token Ring architecture was developed in the mid-1980s by IBM.
Token Ring specifications are governed by the IEEE 802.5 standards.
It use the token-passing access method.
It can be implemented with a physical ring, or can be a logical ring with a physical star topology.
The logical ring represents the token's path between computers. The actual physical ring of cable is in the hub.

## Slide 19: Token Ring
A Token Ring network includes the following features:
  Star-wired ring topology
  Token-passing access method
  Shielded and unshielded twisted-pair cabling
  Transfer rates of 4 and 16 Mbps
  Baseband transmission

## Slide 20: Token Ring
In a pure token-passing network ( with ring topology), a computer that fails, stops the token from continuing. This in turn brings down the network.
In the logical ring , a hub is designed to detect a failed NIC, and to disconnect from it.
This procedure bypasses the failed computer so that the token can continue on.
Therefore, a faulty computer or connection will not affect the rest of the Token Ring network.

## Slide 21: Token Ring
The hub in the Token Ring networks does not function like a shared Ethernet hub.
The Token Ring method is more deterministic and ensures that all users get regular turns at transmitting their data.
With Ethernet, all users compete to get onto the network.

## Slide 22: Token Ring Frame Formats
The Token Ring frame include the following fields:

## Slide 23
Description | Frame field
Indicates start of the frame | Start delimiter
Indicates the frame's priority and whether it is a token or a data frame | Access control
Contains either Media Access Control information for all computers or "end station" information for only one computer | Frame control
The address of receiver | Destination address
The address of source | Source address
Contains the data being sent | Information, or data
Contains CRC error-checking information | Frame check sequence
Indicates the end of the frame | End delimiter
Tells whether the frame was recognized, copied, or whether the destination address was available | Frame status

## Slide 24: Monitoring the System
The first computer to come online is assigned by the Token Ring system to monitor network activity.
The monitoring computer makes sure that frames are being delivered and received correctly. It does this by checking for frames that have circulated the ring more than once and ensuring that only one token is on the network at a time.
Also the process of monitoring called beaconing. The active monitor sends out a beacon announcement every seven seconds. The beacon is passed from computer to computer throughout the entire ring.

## Slide 25: Cont.
If a station does not receive an expected announcement from its upstream neighbor, it attempts to notify the network of the lack of contact.
It sends a message that includes its address, the address of the neighbor that did not announce, and the type of beacon.
From this information, the ring attempts to diagnose the problem and make a repair without disrupting the entire network.
If it is unable to complete the reconfiguration automatically, manual intervention is required.