## Slide 1: Lec7: SNMP Management Information

## Slide 2: Outline
Introduction
Structure of Management Information
Practical Issues
Summary

## Slide 3: SNMP Management Structure

## Slide 4: Introduction
In order to retrieve or change values stored within a managed device with SNMP
  information must be kept by the managed device
  information must be kept in a standard way
Information in a managed object is kept in a MIB (Management Information Base)

## Slide 5: Introduction (cont.)
Each Resource to be managed is represented by an Object.
The MIB is a structured collection of such objects.
For SNMP, the MIB is, in essence a database structure in form of a tree.
Each system (workstation, server, router, bridge etc.) in a network or internetwork maintains a MIB that reflects the status of the managed resources at that system.
A network management entity can monitor the resources at that system by reading the values of objects in the MIB and may control the resources at that system by modifying those vales.

## Slide 7: SNMP
defines the format of packets exchanged between a manager and an agent. It reads and changes the status (values) of objects (variables) in SNMP packets.

## Slide 8: Structure of Management Information Base
SMI (RFC 1155) defines the general framework within which a MIB can be defined and constructed.
    identifies data types, and specifies how resources within the MIB are represented and named.
    Encourages simplicity and extensibility within the MIB.
    Stores simple data: scalars and two-dimensional arrays of scalars
One example of a scalar object could be an ip Address and that for a Tabular object could be a table of user information
Each object has an associated identifier of the Abstract Syntax Notation One (ASN.1) type Object Identifier (OID)
When an SNMP manager requests an object, it sends the OID to the SNMP agent

## Slide 9: SNMP MANAGEMENT INFORMATION BASE
SMI Object Tree
All managed objects in the SNMP environment are arranged in a hierarchical or tree structure.
Any node with children is a Subtree
Otherwise a leaf node.
mib – 2 (1)
enterprises (1)
system(1)
ip(4)
icmp(5)
at(3)
udp(7)
egp(8)
transmission(10)
interfaces(2)
tcp(6)
snmp(11)
e.g. OID for internet is 1.3.6.1, directory is 1.3.6.1.1 and for tcpConnTable is 1.3.6.1.2.1.6.13 that is;
iso org dod internet mgmt mib-2 tcp tcpConnTable
Manufacturers of networking equipment can add product specific objects to the hierarchy; under enterprises.
tcpConnTable(13)

## Slide 10
SNMP MANAGEMENT INFORMATION BASE
Defining Objects – ASN.1 allowed Object Syntax
Universal Types
  INTEGER
  OCTETSTRING
  NULL
  OBJECT IDENTIFIER
  SEQUENCE
  SEQUENCE-OF
Application-wide Types
  Networkaddress
  Ipaddress
  Counter
  Gauge
  Timeticks
  Opaque
Each object within an SNMP MIB is defined in a formal way.
Definition specifies the data type of the object, its allowed value ranges, and its relationship to other objects in the MIB.
ASN.1 includes a number of predefined universal types and a grammar for defining new types that are derived from the existing ones.

## Slide 11
SNMP MANAGEMENT INFORMATION BASE
A Management Information base consists of a set of Objects
Each object has a type and a value
SNMP Managed Objects are defined using macro
Object definition levels are;
    Macro definition, macro instance, and macro instance value.
Macro used for SNMP MIBs was initially defined in RFC 1155 (SMI), and later expanded in RFC 1212 (Concise MIB definitions)
RFC 1155 is used for defining MOs in MIB-I
RFC 1212 is used for defining MOs in MIB-II which is implemented in most SNMP agents today.
Defining Objects – Cont’d

## Slide 12
SNMP MANAGEMENT INFORMATION BASE
Defining Objects – Cont’d
OBJECT-TYPE
  String that describes the MIB object.
  Object IDentifier (OID).
SYNTAX
  Defines what kind of info is stored in the MIB object. “datatype”
ACCESS
  read-only, write-only, read-write, not accessible.
STATUS
  Implementation support required. Either mandatory, optional, or deprecated
DESCRIPTION
  Textual description describing this particular managed object. Reason why the MIB object exists.
Unique OID that defines this object
Object Definition Example
tcpMaxConn OBJECT-TYPE
  SYNTAX INTEGER
    ACCESS read-only
    STATUS mandatory
    DESCRIPTION
      “The limit on the total number of TCP connections the entity can support.”
    ::= {tcp 4}
MIB Object definition is mainly composed of:
    Syntax, Access and Status

## Slide 13
SNMP MIB structure only supports a simple 2-dimensional table with scalar-valued entries
The definition of tables involves the use of the sequence and sequence-of ASN.1 types and the IndexPart of the OBEJECT-TYPE macro.
For example: the tcpconnTable seen earlier has OID 1.3.6.1.2.1.6.13 that contains information about TCP connections, may contain: state, local address, local port, remote address, remote port e.t.c
In particular, definition involves use of:
    Sequence of
    Sequence
SNMP MANAGEMENT INFORMATION BASE
Defining Tables

## Slide 14: Table Definition
SEQUENCE OF TcpConnEntry
  ASN.1 constructs SEQUENCE OF consists of one or more elements, all of the same type
  Each element is a row of the table
  A table consists of zero or more rows
SEQUENCE
  ASN.1 constructs SEQUENCE consists of a fixed no. of elements, possibly of more than one type
  Each row of the table contains elements of type
    INTEGER, IpAddress, INTEGER (..65535), IpAddress, INTEGER

## Slide 15
SNMP MANAGEMENT INFORMATION BASE
Defining Tables – Cont’d
xxxxTable
xxxxEntry
Element-1
Element-2
Element-3
Element-n
SEQUENCE OF
SEQUENCE
Elements can only be scalar objects. Nesting tables not supported.
IndexPart used to distinguish each row in the table.

## Slide 16
SNMP MANAGEMENT INFORMATION BASE
Defining Tables – MIB II Specification of TCP connection table (RFC 1213)

## Slide 17
SNMP MANAGEMENT INFORMATION BASE
Defining Tables – Instance of a TCP connection table

## Slide 18
SNMP MANAGEMENT INFORMATION BASE
MIB-II (RFC 1213) defines the second version of the MIB; the first version, MIB-I is in RFC 1156.
MIB-II is a superset of MIB-I with some additional objects and groups.
Every device that supports SNMP must also support MIB-II
Some criteria for object inclusion in MIB II include:
    Only essential objects,
    Weak Control Objects,
    Evidence of current use and utility,
    Unlimited number of Objects,
    No derived objects,
    e.t.c
MIB II

## Slide 19
SNMP MANAGEMENT INFORMATION BASE
MIB II Object Groups

## Slide 20: Results
We can compare the task of network management to the task of writing a program.
❏ Both tasks need rules. In network management this is handled by SMI. ❏ Both tasks need variable declarations. In network management this is handled by MIB. ❏ Both tasks have actions performed by statements. In network management this is handled by SNMP.

## Slide 21: References
Chu-Sing Yang, Chapter 5: SNMP Management Information, Department of Electrical Engineering National Cheng Kung University
Rashid Mijumbi, SNMP MANAGEMENT INFORMATION BASE
Chapter 21:Network Management:SNMP