## Slide 1: Lec8: SNMP v1

## Slide 2: Outlines
• SNMPv1 does not formally define a functional model
– What was the functional model?
– Deals with the user oriented requirements: (configuration, fault, performance, security, and accounting)
– The functions are actually built in the community based access policy of the SNMP administrative model

## Slide 3: SNMP Structure
Each SNMP message contains a protocol data unit (PDU).
These SNMP PDUs are used for communication between SNMP managers and SNMP agents.
The SNMP Version 1 architecture defines the following types of PDUs that flow between SNMP managers and SNMP agents:
  GETREQUEST
  GETNEXTREQUEST
  SETREQUEST
  GETRESPONSE PDU
  TRAP PDU

## Slide 4: SNMP v1 PDUs:
GETREQUEST: PDU Sent by the SNMP manager to retrieve one or more requested MIB variables specified in the PDU.
GETNEXTREQUEST: PDU Sent by the SNMP manager to retrieve the next MIB variable that is specified in the PDU. You can have multiple requests in the PDU. This PDU is primarily used by the SNMP manager to walk through the SNMP agent MIB.
SETREQUEST : PDU Sent by the SNMP manager to set one or more MIB variables specified in the PDU with the value specified in the PDU.
GETRESPONSE PDU: Sent by the SNMP agent in response to a GETREQUEST, GETNEXTREQUEST, or SETREQUEST PDU.
TRAP PDU: message sent by the SNMP agent to notify the SNMP manager about a significant event that occurred in the agent.

## Slide 5: The Message format of the SNMP PDUs (GETREQUEST, GETNEXTREQUEST, SETREQUEST, GETRESPONSE )
Version: The version of the SNMP message.
Community name : A string of the name of the community from where the PDU originated. This value can be up to 255 characters in length.
PDU type: The type of PDU contained by the SNMP message. PDU type can be one of the following: GETREQUEST – GETNEXTREQUEST – SETREQUEST - GETRESPONSE
Request ID: A unique number that is used to distinguish between different requests and to associate them with the corresponding response.
Error status: Used to indicate that an error occurred while the agent was processing a request.
Error index: Used to provide additional information about the error by identifying which variable in the list caused an error.
Variable binding list: grouping of number of operations in a single message: e.g., one request to get all values and one response listing all values
Version | Community name | PDU type | Request ID | Error status | Error index | Variable binding list

## Slide 6: The Message format of the SNMP PDUs (TrapPDU)
Version: The version of the SNMP message.
Community name : A string of the name of the community from where the PDU originated. This value can be up to 255 characters in length.
PDU type: The type of PDU contained by the SNMP message; in this case, a trap PDU.
Enterprise object identifier: The unique identifier of the SNMP agent that is sending the trap. This value can be up to 255 characters in length.
Network address: The default IP address of the SNMP agent that is sending the trap.
Trap type: The type of trap PDU being sent. The following trap values can be defined: Authentication failure – Coldstart – EgpNeighborLoss - Enterprise-specific – Linkdown – Linkup - Warmstart
Specific trap type: A user-defined value for an enterprise-specific trap.
Time stamp: The system up time, in 1/1000 second, for the system generating the trap.
Variable binding list: grouping of number of operations in a single message: e.g., one request to get all values and one response listing all values
Version | Community name | PDU type | Enterprise object identifier | Network address | Trap type | Specific trap type | Time stamp | Variable binding list

## Slide 7: General Message Format for all PDUs
3 different versions:
SNMPv1, SNMPv2, SNMPv3
SNMP message format is defined using ASN.1, encoded for transmission over UDP
Message ::= SEQUENCE { version INTEGER {version-1(0)}, community OCTET STRING, data PDUs }
Version | Community name | PDU type | Variable binding list

## Slide 8: General Message Format for all PDUs
Message ::= SEQUENCE { version INTEGER {version-1(0)}, community OCTET STRING, data PDUs }
PDUs::= CHOICE { get-request [0] IMPLICIT PDU, get-next-request [1] IMPLICIT PDU, get-response [2] IMPLICIT PDU, set-request [3] IMPLICIT PDU, trap [4] IMPLICIT Trap-PDU
}
Version | Community name | PDU type | Variable binding list

## Slide 9: The Message format of the SNMP PDUs (GETREQUEST, GETNEXTREQUEST, SETREQUEST, GETRESPONSE )
PDU ::= SEQUENCE { request-id INTEGER, error-status INTEGER { noError (0), tooBig (1), noSuchName(2), badValue (3), readOnly (4), genErr (5) }, error-index INTEGER, variable-bindings VarBindList }
Version | Community name | PDU type | Request ID | Error status | Error index | Variable binding list

## Slide 10: Message Format-variable bindings
name
value
var-bind 1
name
value
var-bind 2
name
value
var-bind n
. . .
VarBindList ::= SEQUENCE OF VarBind
VarBind ::= SEQUENCE { name ObjectName, value ObjectSyntax }
ObjectName ::= OBJECT IDENTIFIER
ObjectSyntax ::= CHOICE { simple SimpleSyntax, application-wide ApplicationSyntax }

## Slide 11: Message Format-variable bindings
SimpleSyntax ::= CHOICE { number INTEGER, string OCTET STRING, object OBJECT IDENTIFIER, empty NULL }
ApplicationSyntax::= CHOICE { address NetworkAddress, counter Counter, gauge Gauge, ticks TimeTicks, arbitrary Opaque }
NetworkAddress::= CHOICE { internet IpAddress }

## Slide 12: Message Format-Trap PDU
Trap-PDU ::= SEQUENCE { enterprise OBJECT IDENTIFIER, agent-addr NetworkAddress, generic-trap INTEGER { coldStart (0), warmStart (1), linkDown (2), linkUp (3), authenticationFailure(4), egpNeighborLoss (5), enterpriseSpecific (6) }, specific-trap INTEGER, time-stamp TimeTicks, variable-bindings VarBindList }
Pertain to the system generating
the trap (sysObjectID)
-IP address of the objetc
Elapsed time since last re-initialization
Specific code to identify the
trap cause…
Version | Community name | PDU type | Enterprise object identifier | Network address | Trap type | Specific trap type | Time stamp | Variable binding list

## Slide 13: SNMP Operations
An SNMP entity (manager or agent) performs the following to transmit a PDU
  Construct a PDU using ASN.1
  Pass PDU to Authentication Service (AS) along with source and distention transport addresses and community name
    AS returns a PDU that is encrypted (if encryption is supported)
  The Protocol entity then constructs an SNMP message by adding the version field and the community name to the PDU
  Message is encoded using BER and it is passed to the transport service
An SNMP entity (manager or agent) performs the following upon reception of an SNMP message
  The receiver performs basic syntax check, message is discarded in case of error
  Verifies the version number--message discarded if there is mismatch
    Authentication (if supported): if message does not authenticate, generate trap and discard message.
  Finally, using the community name, the access policy is selected and PDU is processed

## Slide 14: GetRequest PDU
Sender includes the following fields:
  PDU Type
  request-id
  Variable-bindings
    A list of object instances whose values are requested
SNMP dictates that a scalar object is identified by its OBJECT-IDENTIFIER concatenated with 0
  e.g., sysDescr.0: distinguishes between the object type and an instance of the object
sysServices (7)
sysLocation (6)
sysDescr (1)
system
(mib-2 1)
sysObjectId
(2)
sysUpTime (3)
sysName (5)
sysContact (4)

## Slide 15: GetRequest PDU
GetRequest (sysDescr.0)
GetResponse (sysDescr .0= "SunOS" )
GetRequest (sysObjectID.0)
GetResponse ( sysObjectID.0=enterprises.11.2.3.10.1.2 )
GetRequest (sysUpTime.0)
GetResponse (sysUpTime.0=2247349530)
GetRequest (sysContact.0)
GetResponse (sysContact.0=" ")
GetRequest (sysName.0)
GetResponse (sysName.0="noc1 ")
GetRequest (sysLocation.0)
GetResponse (sysLocation.0=" ")
GetRequest (sysServices.0)
GetResponse (sysServices.0=72)
Manager
Process
Agent
Process
.0 indicates that the scalar value
should be retrieved (scalar objects only)
The manager could have used only one message to obtain the values of all objects under system group: using “variable binding list”
Notes: A managed object should implement the system group. The manager by detecting the object, it will poll the new object to learn the values of objects in the system group

## Slide 16: GetRequest PDU
Get Request is atomic
  Either all values (of all variables provided in the binding list) retrieved or none
error message is generated if at least one of the variables could not be found/returned; error-status:
  noSuchName
  tooBig
  genErr
error-index: indicate the problem object (i.e., variable in binding list that caused the problem)
With SNMP, only leaf objects in the MIB can be retrieved
  e.g. it is not possible to retrieve an entire row of a table by simply accessing the Entry Object (e.g., ipRouteEntry)
   the management stations has to include each object instance (in the row) in the binding list
    By including the complete object identifier and respecting the rule of indexing!

## Slide 17: GetRequest PDU
GetRequest (ipRouteDest.9.1.2.3, ipRouteMetric1.9.1.2.3, ipRouteNextHop. 9.1.2.3 )
ipRouteDest ipRouteMetric1 ipRouteNextHop
9.1.2.3 3 99.0.0.3
10.0.0.51 5 89.1.1.42
10.0.0.99 5 89.1.1.42
Index of table

## Slide 18: GetNextRequest PDU
PDU format:
  same as GetReqest
Difference:
  each variable in the binding list refers to an object instance next in the order
GetNextRequest (sysDescr.0)  return the value of the object instance of sysObjectId
Advantages:
  Allows a network manager to discover a MIB structure dynamically
  Efficient way for searching through tables whose entries are unknown
sysServices (7)
sysLocation (6)
sysDescr (1)
system
(mib-2 1)
sysObjectId
(2)
sysUpTime (3)
sysName (5)
sysContact (4)

## Slide 19: GetNextRequest PDU
Error message: no object next
to sysServices
GetRequest (sysDescr.0)
GetResponse (sysDescr .0= "SunOS" )
GetNextRequest (sysDescr.0)
GetResponse ( sysObjectID.0=enterprises.11.2.3.10.1.2 )
Get-Next-Request Operation for System Group
Manager
Process
Agent
Process
GetNextRequest (sysObjectID.0)
GetResponse (sysUpTime.0=2247349530)
GetNextRequest (sysUpTime.0)
GetResponse (sysContact.0=" ")
GetNextRequest (sysContact.0)
GetResponse (sysName.0="noc1 ")
GetNextRequest (sysName.0)
GetResponse (sysLocation.0=" ")
GetNextRequest (sysLocation.0)
GetResponse (sysServices.0=72)
GetNextRequest (sysServices.0)
GetResponse (noSuchName)

## Slide 20: Generalized Case
A sample MIB that contains both scalar values and aggregate objects
Retrieving scalar as well as aggregate objects using get-request and get-next-request
T
Z
A
B
1.1
E
2.1
3.1
1.2
2.2
3.2

## Slide 21: Generalized Case
T.E.1.1
T.E.2.1
T.E.3.1
T.E.1.2
T.E.2.2
T.E.3.2
E
T
Z
A
B
GetRequest ( A )
GetResponse ( A )
GetRequest ( B )
GetResponse ( B )
GetRequest (T.E.1.1)
GetResponse ( T.E.1.1 )
GetRequest (T.E.1.2)
GetResponse ( T.E.1.2 )
GetRequest (T.E.2.1)
GetResponse ( T.E.2.1 )
GetRequest (T.E.2.2)
GetResponse ( T.E.2.2 )
GetRequest (T.E.3.1 )
GetResponse ( T.E.3.1 )
GetRequest (T.E.3.2 )
GetResponse ( T.E.3.2 )
GetRequest (Z )
GetResponse ( Z )
Manager
Process
Agent
Process

## Slide 22: Generalized Case
Observations:
1)- we need to know all the elements in the MIB, including the # of columns and rows in a table
2)- a MIB is traversed from top to bottom (i.e., from left to right in the tree structure)
3)- data in tables is retrieved by traversing all instances of a columnar object
NOTES:
1)- dynamic table: # rows may not be known to manager
  A request to T.E.1.3 results in error message
3)- GetNextRequest could avoid this!
4)- A convention is required for the definition of the next object in a MIB
 SNMP uses lexicographic convention
T.E.1.1
T.E.2.1
T.E.3.1
T.E.1.2
T.E.2.2
T.E.3.2
E
T
Z
A
B

## Slide 23: Lexicographic Ordring- example
3
9
1
2
18
1
5
2
6
2
10
9
21
4
start
end
MIB example of lexicographic ordering

## Slide 24: GetNextRequest PDU
T.E.1.1 is next
object to scalar B
T.E.1.1
T.E.2.1
T.E.3.1
T.E.1.2
T.E.2.2
T.E.3.2
E
T
Z
A
B
GetRequest ( A )
GetResponse ( A )
GetNextRequest ( A )
GetResponse ( B )
GetNextRequest ( B )
GetResponse ( T.E.1.1 )
GetNextRequest (T.E.1.1 )
GetResponse ( T.E.1.2 )
GetNextRequest (T.E.1.2 )
GetResponse ( T.E.2.1 )
GetNextRequest (T.E.2.1 )
GetResponse ( T.E.2.2 )
GetNextRequest (T.E.2.2 )
GetResponse ( T.E.3.1 )
GetNextRequest (T.E.3.1 )
GetResponse ( T.E.3.2 )
GetNextRequest (T.E.3.2 )
GetResponse ( Z )
GetNextRequest ( Z )
GetResponse ( noSuchName )
Manager
Process
Agent
Process

## Slide 25: GetNextRequest PDU
Advantages of Get-Next-Request
1)- no need to know the object ID of the next entity to retrieve its value
2)- issues with dynamic table resolved
3)- allows NMS to discover the structure of a MIB view dynamically
4)- provides an efficient mechanism for searching a table whose entries are unknown
GetRequest ( A )
GetResponse ( A )
GetNextRequest ( A )
GetResponse ( B )
GetNextRequest ( B )
GetResponse ( T.E.1.1 )
GetNextRequest (T.E.1.1 )
GetResponse ( T.E.1.2 )
GetNextRequest (T.E.1.2 )
GetResponse ( T.E.2.1 )
GetNextRequest (T.E.2.1 )
GetResponse ( T.E.2.2 )
GetNextRequest (T.E.2.2 )
GetResponse ( T.E.3.1 )
GetNextRequest (T.E.3.1 )
GetResponse ( T.E.3.2 )
GetNextRequest (T.E.3.2 )
GetResponse ( Z )
GetNextRequest ( Z )
GetResponse ( noSuchName )
Manager
Process
Agent
Process

## Slide 26: Lexicographic Ordring- example
ipRouteDest ipRouteMetric1 ipRouteNextHop
9.1.2.3 3 99.0.0.3
10.0.0.51 5 89.1.1.42
10.0.0.99 5 89.1.1.42
ipRouteTable
1.3.6.1.2.1.4.21
ipRouteEntry
1.3.6.1.2.1.4.21.1 = x
ipRouteDest
x.1
ipRouteMetric1
x.3
ipRouteNextHop
x.7
ipRouteDest.9.1.2.3
x.1.9.1.2.3
ipRouteDest.10.0.0.51
x.1.10.0.0.51
ipRouteDest.10.0.0.99
x.1.10.0.0.99
ipRouteMetric1.9.1.2.3
x.3.9.1.2.3
ipRouteMetric1.10.0.0.51
x.3.10.0.0.51
ipRouteMetric1.10.0.0.99
x.3.10.0.0.99
ipRouteNextHop.9.1.2.3
x.7.9.1.2.3
ipRouteNextHop.10.0.0.51
x.7.10.0.0.51
ipRouteNextHop.10.0.0.99
x.7.10.0.0.99
Index of table

## Slide 27: Accessing Table Values
Retrieving the entire table w/out knowing its contents or number of rows:
GetNextRequest (ipRouteDest, ipRouteMetric1, ipRouteNextHop)
 The agent will respond with the values from the first row
GetResponse ((ipRouteDest.9.1.2.3 = 9.1.2.3),
(ipRouteMetric1.9.1.2.3 = 3),
(ipRouteNextHop.9.1.2.3 = 99.0.0.3))
 The MS stores this info and retrieves the second row
ipRouteDest ipRouteMetric1 ipRouteNextHop
9.1.2.3 3 99.0.0.3
10.0.0.51 5 89.1.1.42
10.0.0.99 5 89.1.1.42

## Slide 28: Accessing Table Values
GetNextRequest (ipRouteDest.9.1.2.3, ipRouteMetric1.9.1.2.3,
ipRouteNextHop.9.1.2.3)
-------------------------------------------
GetResponse ((ipRouteDest.10.0.0.51 = 10.0.0.51),
(ipRouteMetric1.10.0.0.51 = 5),
(ipRouteNextHop.10.0.0.51 = 89.1.1.42))
---------------------------------------------------------------------
GetNextRequest (ipRouteDest.10.0.0.51, ipRouteMetric1.10.0.0.51,
ipRouteNextHop.10.0.0.51)
-------------------------------------------
GetResponse ((ipRouteDest.10.0.0.99 = 10.0.0.99),
(ipRouteMetric1.10.0.0.99 = 5),
(ipRouteNextHop.10.0.0.99 = 89.1.1.42))
ipRouteDest ipRouteMetric1 ipRouteNextHop
9.1.2.3 3 99.0.0.3
10.0.0.51 5 89.1.1.42
10.0.0.99 5 89.1.1.42

## Slide 29: Accessing Table Values
What happens next!, When does the MS stop?
GetNextRequest (ipRouteDest.10.0.0.99, ipRouteMetric1.10.0.0.99,
ipRouteNextHop.10.0.0.99)
-------------------------------------------
GetResponse ((ipRouteMetric1.9.1.2.3 = 3),
(ipRouteNextHop.9.1.2.3 = 99.0.0.3),
(ipNetToMediaIfIndex.1.3 = 1))
ipRouteDest ipRouteMetric1 ipRouteNextHop
9.1.2.3 3 99.0.0.3
10.0.0.51 5 89.1.1.42
10.0.0.99 5 89.1.1.42
Object names in the list in the response does not match those in the request
 MS knows it has reached the end of the table

## Slide 30: SetRequest-PDU
Write a value rather than reading a variable
The operation is atomic:
  either all variables in binding list are updated or none
Procedure receive-SetRequest:
begin
if object not available for set then
issue getresponse (noSuchName, index)
else if inconsistent object value then
issue getresponse (badValue, index)
else if generated PDU too big then
issue getresponse (tooBig)
else if value not settable for some other reason then
issue getresponse (genErr, index)
else issue getresponse (variable bindings)
end;

## Slide 31: SetRequest-PDU-example
Updating the value of ipRouteMetric1 metric of the first row:
SetRequest (ipRouteMetric1.9.1.2.3 = 9)
GetResponse (ipRouteMetric1.9.1.2.3 = 9)
Adding a row to the table -- a MS issues a command:
SetRequest ((ipRouteDest.11.3.3.12 = 11.3.3.12),
(ipRouteMetric1.11.3.3.12 = 9),
(ipRouteNextHop.11.3.3.12 = 91.0.0.5))
ipRouteDest ipRouteMetric1 ipRouteNextHop
9.1.2.3 3 99.0.0.3
10.0.0.51 5 89.1.1.42
10.0.0.99 5 89.1.1.42
Index of the new
object instance in
the table
But this is currently
unknown for the agent!

## Slide 32: SetRequest-PDU-example
Three ways for the agent to handle the request:
1)- reject the operation with error-status = noSuchName
2)- recognize the operation (as creation of a new row) and check whether the operation can be accepted (i.e., all values are correct, no syntax error, etc..)
2.1)- if NO, then return error-status = badValue
2.2)- if YES, then new row is created and
GetResponse ((ipRouteDest.11.3.3.12 = 11.3.3.12),
(ipRouteMetric1.11.3.3.12 = 9),
(ipRouteNextHop.11.3.3.12 = 91.0.0.5))
Adding a row to the table -- a MS issues a command:
SetRequest ((ipRouteDest.11.3.3.12 = 11.3.3.12),
(ipRouteMetric1.11.3.3.12 = 9),
(ipRouteNextHop.11.3.3.12 = 91.0.0.5))
If only this argument is passed,
then the agent may accept or not;
if it accepts to create the row,
then the other objects are assigned
default values

## Slide 33: SetRequest-PDU-example
Row Deletion:
SetRequest (ipRouteMetric1.7.3.5.3 = invalid)
GetResponse (ipRouteMetric1. 7.3.5.3 = invalid)
Some other tables may/may not allow any operation to be done on its columnar objects – check RFCs for more details
Performing an action:
SNMP can read and set values of objects. SNMP can also issue commands to perform certain actions: example, a device may have a flag “reBoot”, if it is set by the manager, then the device will reboot.

## Slide 34: Polling Frequency
Few traps exist in the standard!
  Thus most of the management information is gathered by means of polls (GetRequest, GetNextRequest)
If polling is done un-frequently
  A management station may have outdated view of the network (e.g., congestion might happen and the NM may not be alerted)
If polling is done frequently
  The control messages overhead will be high and degrade the performance
Polling frequency requires some policy definition
  e.g., size of the network (i.e., #agents a MS can handle)

## Slide 35: Polling Frequency
Assumption: assume the MS can handle only one agent at a time (i.e., when polling an agent, a MS does no other work until it is done)
A poll may involve a single get/response transaction or multiple such transactions
The maximum number of agents a MS can handle, considering that it is engaged full time in polling is:
N  (T/)
N: number of agents
T: desired polling interval
: average time required to perform a single poll
T

Agent 1
Agent 2
Agent 1
Agent N

## Slide 36: Polling Frequency
 depends on multiple factors:
  Processing time to generate a request at the MS
  Network delay from MS to agent
  Processing time at the agent to interpret the received message
  Processing time at the agent to generate response
  Network delay from agent to manager
  Processing time at the manager to interpret the message
  Number of request/response transactions to obtain all desired info.
Example
  Devices on a LAN; each device is to be polled every 15 minutes
  Processing times = 50ms;
  Network delay = 1ms (no network congestion)
  N  (1560/) = 4,500
  Where  = 50 + 1+ 50+ 50+ 1+ 50 = 202 ms

## Slide 37: Some Limitations of SNMPv1
SNMP may not be suitable for the mgmt of truly large networks because of the performance limitations of polling
SNMP is not well suited for retrieving large volumes of data, such as an entire routing table
SNMP traps are unacknowledged & may not be delivered
SNMP provides only trivial authentication
  i.e. it is suitable for monitoring rather than control
SNMP does not support explicit actions
  i.e., an action is taken by changing a parameter or setting an object value (indirectly)
SNMP does not support manager-to-manager communications
Many of these problems are addressed in SNMPv2!

## Slide 38: References
Reference: by Behzad Akbari Fall 2011, “SNMPv1 Communication and Functional Models”