## Slide 1
Chapter 2
Notes: <number>

## Slide 2
The Bohr atom is a tool for visualizing atomic structure.
The nucleus is positively charged and has the protons and neutrons.
The atomic number is the number of protons and determines the particular element.
In the neutral atom, the number of electrons is equal to the number of protons.
Electrons are negatively charged and in discrete shells.
Notes: <number>

## Slide 3
The outer shell is called the valence shell. Electrons in this shell are involved in chemical reactions and in metals they account for electrical and thermal conductivity.
A neutral Si atom is shown. There are 4 electrons in the valence shell.
Question:
Is Si a conductor, insulator, or semiconductor?
Semiconductor
Notes: <number>

## Slide 4
There is a force (F) between charges. Like charges repel; unlike charges attract.
The force is directly proportional to charge.
The force is inversely proportional to square of distance (for point sources).
Notes: <number>

## Slide 5
Work is done as a charge is moved in the electric field from one potential to another.
Voltage is the work per charge done against the electric field.
Voltage (V) is the energy (W) per charge (Q); it is responsible for establishing current.
Notes: <number>

## Slide 6
Definition of voltage
One volt is the potential difference (voltage) between two points when one joule of energy is used to move one coulomb of charge from one point to the other.
Notes: <number>

## Slide 7: Example
Find the potential difference between 2 points in electrical system if 60J of energy are expended by a charge of 20C between these two points
Solution
V=W/Q= 60J/20C= 3V

## Slide 8: Example
Determine the energy expended moving a charge of 50 μC through a potential difference of 6V
Sol.
W= QV
= (50x10-6C)(6V)= 300x10-6J
= 300 μJ

## Slide 9
Voltage is responsible for establishing
This is a Cu-Zn battery, such as you might construct in a chemistry class. The chemical reaction occurs when there is an external path for the electrons.
Voltage
current. Voltage sources include generators, solar cells, and batteries to name a few.
Notes: <number>

## Slide 10
Batteries
Batteries do not store charge – they store chemical energy that can be converted to current when an external path is provided to allow the chemical reaction to proceed.
Rather than saying “charging” a battery, it is more accurate to say “reversing the chemical reaction” in a battery.

## Slide 11
Current (I) is the amount of charge (Q) that flows past a point in a unit of time (t).
One ampere is a number of electrons having a total charge of 1 C move through a given cross section in 1 s.
Question:
0.4 A
What is the current if 2 C passes a point in 5 s?
Notes: <number>

## Slide 12
Resistance is the opposition to current.
One ohm (1 ) is the resistance if one ampere (1 A) is in a material when one volt (1 V) is applied.
Conductance is the reciprocal of resistance.
Components designed to have a specific amount of resistance are called resistors.
Notes: <number>

## Slide 13
Question
What is the resistance and tolerance of each of the four-band resistors?
5.1 k± 5%
k± 5%
47  ± 10%
1.0  ± 5%
Notes: <number>

## Slide 14
Variable resistors include the potentiometer and rheostat. A potentiometer can be connected as a rheostat.
The center terminal is connected to the wiper
Notes: <number>

## Slide 15
A basic circuit consists of
a voltage source, 2) a path and 3) a load.
An example of a basic circuit is the flashlight, which has each of these.
Notes: <number>

## Slide 16
An important multipurpose instrument is the DMM, which can measure voltage, current, and resistance. Many include other measurement options.
Notes: <number>

## Slide 17
Ampere
AWG
Charge
Circuit
The unit of electrical current
(American Wire Gauge) A standardization based on wire diameter
An electrical property of matter that exists because of an excess or a deficiency of electrons. Charge can be either + or .
An interconnection of electronic components designed to produce a desired result. A basic circuit consists of a source, a load, and an interconnecting path.
Selected Key Terms
Notes: <number>

## Slide 18
Conductance
Coulomb
Current
Electron
Ground
Ohm ()
The ability of a circuit to allow current. The unit is the siemans (S).
The unit of electrical charge.
The rate of flow of electrical charge.
A basic particle of electrical charge in matter. The electron possesses a negative charge.
Selected Key Terms
The common or reference point in a circuit.
The unit of resistance.
Notes: <number>

## Slide 19
Potentiometer
Resistance
Rheostat
Siemens
Volt
Voltage
A three-terminal variable resistor.
The opposition to current. The unit is the ohm ().
A two-terminal variable resistor.
Selected Key Terms
The unit of conductance
The unit of voltage or electromotive force.
The amount of energy per charge available to move electrons from one point to another in an electric circuit.
Notes: <number>

## Slide 20
Quiz
1. The atomic number is the number of
a. protons in the nucleus
b. neutrons in the nucleus
c. protons plus neutrons in the nucleus
d. electrons in the outer shell
Notes: <number>

## Slide 21
Quiz
2. Valence electrons are
a. in the outer shell
b. involved in chemical reactions
c. relatively loosely bound
d. all of the above
Notes: <number>

## Slide 22
Quiz
3. The atomic particle responsible for electrical current in solid metallic conductors is the
a. proton
b. electron
c. neutron
d. all of the above
Notes: <number>

## Slide 23
Quiz
4. The symbol for charge is
a. C
b. 
c. Q
d. W
Notes: <number>

## Slide 24
Quiz
5. The definition for voltage is
a.
b.
c.
d.
Notes: <number>

## Slide 25
Quiz
6. A battery stores
a. electrons
b. protons
c. ions
d. chemical energy
Notes: <number>

## Slide 26
Quiz
7. The unit of conductance is the
a. ohm
b. coulomb
c. siemens
d. ampere
Notes: <number>

## Slide 27
Quiz
Answers:
1. a
2. d
3. b
4. c
5. c
6. d
7. c
8. b
9. b
10. b
Notes: <number>