## Slide 2: HEMODYNAMIC MONITER

## Slide 3: Definition
  Hemodynamic:
  is a term to describe intravascular pressure, oxygenation, and blood flow occurring within the cardiovascular system.
  Hemodynamic monitoring :
  Using invasive technology to provide quantitative information about vascular capacity, blood volume, pump effectiveness and tissue perfusion.
  It is an essential part of critical care nursing.

## Slide 4: Indications:
- Continuous, real-time blood pressure monitoring
- Planned pharmacologic or mechanical cardiovascular manipulation
- Repeated blood sampling
- Determination of volume responsiveness from systolic pressure or pulse -pressure variation
- Supplementary diagnostic information from the arterial waveform
-Failure of indirect arterial blood pressure measurement

## Slide 5: Types of Hemodynamic Monitoring
Noninvasive Hemodynamic Monitoring
- Noninvasive BP
- Heart Rate, pulses
- Mental Status
- Skin Temperature
-Capillary Refill
- Urine Output
- Pulse Oxymetry
Invasive Hemodynamic Monitoring
CVP, ARTERIAL LINE , PAC -

## Slide 6
Central line & Arterial line

## Slide 7
Outline :
1- Central line :
- Definition
- Purpose
- COMMON CENTRAL LINE INSERTION SITES
- TYPES OF CENTRAL LINE
a- Central venous pressure:
- What is CVP.
- Used.
- Site of insertion
- Causes of increase & decrease CVP
- Nursing management
- METHODS OF CVP MONITORING
- Measuring central venous pressure
- complications

## Slide 8
Cont…
2- Arterial line :
- Definition
- Purpose
- THE ARTERIAL WAVEFORM
b- Arterial Pressure ( AP ):
- Arterial line procedure
- Complication
- REMOVAL OF ARTERIAL LINE

## Slide 9
WHAT IS A CENTRAL LINE:
It is a catheter that provides venous access via the superior vena cava or right atrium.
Purpose :
Permits administration of medication & nutritional support that should not be given via a peripheral route or when standard peripheral route cannot be used .

## Slide 10
COMMON CENTRAL LINE INSERTION SITES:
1- Right internal jugular
2- Left internal jugular
3- Right subclavian
4- Left subclavian
5- Femoral

## Slide 11
6- Or peripherally inserted central catheters (PICC) which are inserted via the antecubital veins in the arm and is advanced into the central veins

## Slide 12
TYPES OF CENTRAL LINE:
1- SINGLE LUMEN
2- TRIPLE LUMEN
3- QUADRUPLE LUMEN

## Slide 13
Central venous pressure ( CVP)
What is CVP :
IS THE PRESSURE WITHIN THE SUPERIOR VENA CAVA OR THE RIGHT ATRIUM to provide information about the body volume status & right ventricular function.
Normal CVP= 0 - 8 mmHg or 3-8 cm H2O
- If less than 0 mean Hypovolemia
- If more than 8 mean Hypervolemia

## Slide 14
CVP READINGS ARE USED:
1- TO SERVE AS A GUIDE TO FLUID BALANCE IN CRITICALLY ILL PATIENTS
2- TO ESTIMATE THE CIRCULATING BLOOD VOLUME
3- TO ASSIST IN MONITORING CIRCULATORY FAILURE

## Slide 15
Site of insertion ;
1- Subclavian vein ( RT/LT)
2- Internal jugular vein
3- Femoral vein

## Slide 16
Causes of increase CVP;
- Hypervolemia
- Right ventricular failure
- Pericarditis
- Cardiac tamponade
Causes of decrease CVP;
- Hypovolemia
- Shock
- Venodilation

## Slide 17
Nursing management :
Before the insertion;
1- Prepare for equipment
During the insertion;
1- Explain procedure to the pt
2- Prepare the site of insertion ( cleaning & shaving)
3- Assist the doctor during insertion
4-Perform continuous assessment of the pt cardiac & respiratory status
After the insertion;
1- Begin the IV infusion
2- Assess integrity of the skin at the site of insertion
3- Cover site of insertion with sterile gauze
4- Prepare pt for x-ray
5- Measurement CVP

## Slide 18
METHODS OF CVP MONITORING:
There are two methods of CVP monitoring
1- Manometer system:
Enables intermittent readings and is less accurate than the transducer system

## Slide 19
2- Transducer system:
Enables continuous readings which are displayed on a monitor.

## Slide 20
Measuring central venous pressure
1- The CVC will be attached to intravenous fluid within a pressure bag. Ensure that the pressure bag is inflated up to 300mmHg.

## Slide 21
2- Catheters differ between manufacturers, however, the white or proximal lumen is suitable for measuring CVP.

## Slide 22
3- Place the patient flat in a supine position if possible.

## Slide 23
4- Tape the transducer to the phlebostaticaxis or as near to the right atrium as possible.

## Slide 24
5- Turn the tap off to the patient and open to the air by removing the cap from the three-way port opening the system to the atmosphere.

## Slide 25
6- Press the zero button on the monitor and wait while calibration occurs .

## Slide 26
7- When 'zeroed' is displayed on the monitor, replace the cap on the three-way tap and turn the tap on to the patient.

## Slide 27
8- Observe the CVP trace on the monitor.

## Slide 28
9- Documentation include :
a- Date & time of insertion catheter.
b- Type & location of the catheter , including NO. of the lumens.
c- Care & maintain procedure performance .
d- Appearance of insertion site .
e- Problem noted such as resistance to flushing
f- client tolerance to procedure

## Slide 29
Complications of CVP :
1- Hemorrhage
2- Catheter occlusion
3- Infection
4- Air embolism
5- Catheter displacement
6- Cardiac arrhythmias
7- Pneumothorax
8- Hemothorax
9- Hemo-pneumothorax

## Slide 30
WHAT IS AN ARTERIAL LINE?
AN ARTERIAL LINE IS A CANNULA USUALLY POSITIONED IN A PERIPHERAL ARTERY
SUCH AS
- Radial artery
- Brachial artery
- Dorsalis pedis artery
- Femoral artery
Purpose :
1- Facilitate monitoring of hemodynamic status by providing information about ABP readings.
2- Obtain hemodynamic data necessary for regulating vasoactive medication & fluid administration.

## Slide 31
THE ARTERIAL WAVEFORM
The arterial waveform reflects the pressure generated in the arteries following ventricular contraction and can be described as having:-
- Anacrotic notch
- Peak systolic pressure
- Dicrotic notch
- Diastolic pressure

## Slide 32
Arterial Pressure ( AP ):
The pressure of the circulating blood on the arteries
.

## Slide 33
COMPLICATIONS:
1- HYPOVOLAEMIA
2- ACCIDENTAL INTR-ARTERIAL INJECTION OF DRUGS
3- LOCAL DAMAGE TO ARTERY

## Slide 34
Pulmonary artery catheter

## Slide 35
Outline :
1- Definition.
2- Purpose .
3- Indication.
4- Contraindication .
5- Insertion site .
6- Lumen type .
7- Assessment.
8- Equipment
9- procedure
10- Normal values of commonly measured parameters.
11- Complication.

## Slide 36
Pulmonary artery catheter
- Pulmonary artery catheter (PAC) is also know as Swan Ganz catheterization .
- A light flexible balloon-tipped tube that is introduced into the pulmonary artery (the artery from the right ventricle of the heart to the lungs.)

## Slide 37
Purpose :
1- Facilitate monitoring of hemodynamic status , providing information a bout right & left side intracardiac pressure , cardiac output , mixed oxygen saturation.
2- Obtain hemodynamic data necessary for regulating vasoactive medication and fluid administration .

## Slide 38
Indication :
1- Assessment and management of shock states.
2- Assessment of pulmonary edema (cardiogenic vs ARDS) .
3- Optimization of cardiac index in cardiogenic shock.
4- Evaluation and drug titration for severe pulmonary hypertension .
5- Diagnostic evaluation of left-to-right cardiac shunts.
6- May aid to optimize peri-operative clinical status in high-risk surgical candidates

## Slide 39
Contraindication :
1- Uncontrolled ventricular or atrial dysrhythmias.
2- Right ventricular mural thrombus.
3- Cardiac arrest .
4- Respiratory arrest.
5- Cyanotic congenital heart disease.
6- Ventricular masses or other structural abnormalities

## Slide 40
Insertion site :
Catheterization of the right side of the heart and pulmonary artery via;
1- Right internal jugular vein
2- Subclavian vein

## Slide 41
Type of lumen :
PAC has 4-5 lumens:
1- Temperature thermistor located proximal to balloon to measure pulmonary artery blood temperature
2- Proximal port located 30 cm from tip for CVP monitoring, fluid and drug administration
3- Distal port at catheter tip for PAP monitoring
4- +/- Variable infusion port (VIP) for fluid and drug administration
5- Balloon at catheter tip

## Slide 42
Normal values of commonly measured parameters are as follows:
- Pulmonary artery systolic pressure: 20-30mmHg
- Pulmonary artery mean pressure: 9-17mmHg
- Pulmonary artery diastolic pressure: 5-15mmHg
- Pulmonary capillary wedge pressure: 8-12mmHg
- Right atrial pressure: 2-6mmHg
- Cardiac index: 2.5-4 L/min/m2
- Cardiac output (CO) L/min

## Slide 43
Complication :
1- Accidental puncture of adjacent arteries
2- Bleeding
3- Neuropathy
4- Air embolism
5- Pneumothorax
6- Dysrhythmias
a- Premature ventricular and atrial contractions
b- Ventricular tachycardia or fibrillation

## Slide 44
CONT….
7- Thromboembolism
8- Mechanical, catheter knots
9- Pulmonary Infarction
10- Infection, Endocarditis
11- Endocardial damage, cardiac valve injury
12- Pulmonary Artery Rupture

## Slide 46
References
- Cole E (2007) Measuring central venous pressure.Nursing Standard. 22 (7) 40-42
- Hamilton H(2006a) Complications associated with venous access devices: part one. Nursing Standard.20, 26, 43-50.
- Hamilton H(2006b) Complications associated with venous access devices: part two. Nursing Standard.20, 27, 59-65.
- Jevon P, Ewens B (Eds)(2007) Monitoring the Critically Ill Patient.Second edition. Blackwell Science, Oxford.