## Slide 1
Electronics

## Slide 2: Evaluation and assessment
Assignments 5%
Seminars/oral 5%
Quizzes 5%
Mid term 15%
Practical/lab 30%
Final 40%

## Slide 3: Semiconductor Devices

## Slide 4: Classification of Materials
Materials may be classified depend on its energy band structure into :-
Insulators
Semiconductors
Metals

## Slide 5: 1- Insulators
It is a very poor conductor of electricity .
The forbidden band which separates the valance band and conduction band is very large ( order of 6 )
The energy which can be supplied to an electron from an applied field is too small to carry the practice from the filled valance band to vacant conduction band
Example : Wood , Glass

## Slide 6
Insulation
Valance band
Forbidden band
Conduction band

## Slide 7: 2- Metals
It is an excellent conductor of electricity .
The filled valance band and the empty conduction band overlap each other with no forbidden energy band.
Under the influence of an applied electric field, the electron acquire additional energy and move in to higher energy states.
Example : Copper , Silver, Aluminum.

## Slide 8
Metals
Valance band
Conduction band

## Slide 9: 3-semiconductors
The conductivity of semiconductors lies in between the insulators and metal.
The forbidden energy band is relatively small ( order of 1ev)
Example : Silicon, Germanium

## Slide 10
Insulation
Valance band
Forbidden band
Conduction band
Eg=1ev

## Slide 11: Properties of semiconductors
The resistivity of a semiconductor is less than an insulator but more than a conductor
Insulator semiconductor metals
conductivity

## Slide 12
2. Semiconductors have –ve temperature coefficient of resistance. For example the resistance of semiconductor decreases with the increase in temperature.
3. When a suitable metallic impurity is added to semiconductor its current conducting property change.

## Slide 13: Classification of semiconductors
The semiconductors may be classified based on its constructure into:-
Intrinsic semiconductors
Extrinsic semiconductors

## Slide 14: 1- Intrinsic semiconductor
The semiconductor is pure.
At room temperature, electrons and holes are created due to thermal energy.
The conduction through the semiconductor is due to both electrons and holes.
The total current inside the semiconductor is the sum of currents due to free electrons and holes.
Example : Germanium and Silicon

## Slide 15: 2- Extrinsic semiconductor
The conductivity of an intrinsic semiconductor can be increased by adding certain impurity atoms to the crystal.
The amount of impurity added extremely small,
1 atom of impurity for 10e6 intrinsic atom
conduction through the semiconductor is due to both electrons and holes.
The total current inside the semiconductor is the sum of currents due to free electrons and holes.
Example : Germanium and Silicon

## Slide 16
Depending upon the type of impurity atoms added, the extrinsic semiconductor can be classified into:-
1- N-type semiconductor
2- P-type semiconductor

## Slide 17: N-type semiconductor
When an intrinsic semiconductor is doped with pentavalent elements such as
Phosphors the resulting conductor is a N-type semiconductor.
The Ge atom or the Si atom is having only 4 valence electrons. The pentavalent atoms form four covalent bond with four parent Ge or Si atom leaving one electron free for conductance.
Since the impurity atoms donates an electron for conductance, it is called donor impurity or N-type impurity.

## Slide 18
P
Ge
Ge
Ge
Ge
N-type semiconductor

## Slide 19: P-type semiconductor
When an intrinsic semiconductor is doped with trivalent elements such as
Boron the resulting conductor is a P-type semiconductor.
The Ge atom or the Si atom is having only 4 valence electrons. The boron atom form three covalent bond with three parent Ge or Si atom the fourth bond constitutes a hole.
Since the trivalent impurity which creates holes which can accept electrons it is known as acceptors or P-type.

## Slide 20
B
Ge
Ge
Ge
Ge
P-type semiconductor

## Slide 21: Formation of PN-Junction
In a piece of semiconductor material, if one half is P-type and another half is N-type, a PN-Junction is formed.
Since N-type has high concentration of free electrons and P-type material has high concentration of free hole.
At the Junction, the free electrons move across the junction from N-type to P-type. The donor ions become positive.

## Slide 22: Formation of PN-Junction-cont
The positive charge is built on the N-side of the junction. The free electrons that cross the junction combines with the holes creating a negative charge on the p-side of the junction.
Exchange of mobile carriers occurs mainly in a narrow region around the junction. This region is called as the depletion layer.
Net negative charge on the P-side prevents further diffusion of electrons in to the P-type

## Slide 23: Formation of PN-Junction-cont
Similarly, the net positive charge on the N-side repels the hole crossing from P-side to N-side.
This potential difference is a barrier is set up near the junction which prevent further movement of charge carriers is electrons and holes.

## Slide 24
+
+
+
+
-
-
-
-
-
+
-
+
-
+
-
+
+
-
+
-
+
-
+
-
+
-
+
-
-
+
-
+
Exposed ionised Acceptors
Exposed ionised Donors

## Slide 25
The magnitude of the contact potential varies with doping levels and temperature. Its 0.3 V for germanium and 0.70 V for silicon