## Slide 1
CHAPTER ONE
Fits and Tolerances
1
CHAPTER ONE : Fits and Tolerances
CONTENTS

## Slide 2: Why tolerances and fits are required?
Due to the inevitable inaccuracy of manufacturing methods, a part
cannot be made precisely to a given dimension, the difference between maximum and minimum limits of size of a part is the tolerance.
Tolerance is the total amount that a specific dimension is permitted to vary.
There is no such thing as an "exact size". Tolerance is key to interchangeable parts.
When two parts are to be assembled, the relation resulting from the difference between their sizes before assembly is called a fit.
CHAPTER ONE : Fits and Tolerances

## Slide 3: Examples of Interchangeable Manufacture
Bottle caps
Rims
Tires
CHAPTER ONE : Fits and Tolerances

## Slide 4: Advantages For Interchangeable Manufacture
Replacement: One such part can freely replace another, without any custom fitting (such as filling).
Easy to Assembly: This interchangeability allows easy assembly of new devices
Repairing: Easier repair of existing devices.
Minimizing time and cost: Minimizing both the time and skill required of the person doing the assembly or repair.
Rapid Manufacturing: Machine tool enables the components to be manufactured more rapidly

## Slide 5: How to decide tolerance?
  Functional requirements of mating parts
  Cost of production
  Available manufacturing process
    Choose as coarse tolerance as possible without compromising functional requirements.
    Proper balance between cost and quality of parts.
CHAPTER ONE : Fits and Tolerances

## Slide 6
1.1 Dimensional Tolerances Some of the dimensional tolerances terms are defined as following:
1. Dimension
2. Size (It is a number expressed in a particular unit in the measurement of length)
3. Actual size (of a part) (the measured size of the finished part after machining)
4. Basic size (the theoretical size used as a starting point for the application of tolerances)
CHAPTER ONE : Fits and Tolerances

## Slide 7
5. Design size (The ideal size for each component (shaft and hole) based upon a selected fit)
6. Limits of size (the maximum and minimum sizes shown by the tolerance dimension)
7. Maximum limit of size (Is the maximum size permitted for the part)
8. Minimum limit of size (it is the minimum size permitted for the part limit of size)
9. Maximum material limit (is the condition of a part when it contains the most amount of material. The MMC of an external feature (such as a shaft) is the upper limit. The MMC of an internal feature(such as a hole) is the lower limit)
10. Minimum material limit (is the condition of a part when it contains the least amount of material possible. The LMC of an external feature is the lower limit of the part. The LMC of an internal feature is the upper limit of the part.)
11. Tolerance (Tolerance is the difference between maximum limit of size and minimum limit of size)
CHAPTER ONE : Fits and Tolerances
Notes: http://homepages.cae.wisc.edu/~me232/tolerance_info/limits_fits.pdf (design size VS basic size)

## Slide 8
12. Zero line (it represents the basic size)
13. Upper deviation (It is the algebraic difference between minimum limit of size and its corresponding basic size)
14. Lower deviation (It is the algebraic difference between minimum limit of size and its corresponding basic size)
15. Tolerance zone (a region representing the difference between the upper and the lower limits)
16. Unilateral tolerance (In this method of presenting the limits, variation is allowed only on one side of the zero line)
17. Bilateral tolerance (Here the limits variation is allowed on either sides of the zero line)
18. Shaft (it refers to any external feature of a part, including any non cylindrical features as well)
19. Hole (the term used for any internal feature of a part including any non cylindrical as well)
CHAPTER ONE : Fits and Tolerances

## Slide 9
CHAPTER ONE : Fits and Tolerances
Notes: https://www.youtube.com/watch?v=KiXHABfRHfQ

## Slide 10
The Tolerance is 0.001” for the Hole as well as for the Shaft
CHAPTER ONE : Fits and Tolerances

## Slide 11
CHAPTER ONE : Fits and Tolerances

## Slide 12
Unilateral tolerance
Bilateral tolerance
Zero line
CHAPTER ONE : Fits and Tolerances

## Slide 13
CHAPTER ONE : Fits and Tolerances

## Slide 14: Calculate the maximum and minimum possible dimension for A
+0.01
-0.01
+0.01
-0.01
CHAPTER ONE : Fits and Tolerances

## Slide 15
20. Basic shaft (the shaft chosen as a basis for the shaft basis system of fit)
21. Basic hole (the hole chosen as a basis for the hole basis system of fit)
22. Fit (Fit is the relationship that exists between two mating parts, a hole and shaft with respect to their dimensional difference )
23. Basic size of a fit (common value of the basic size of the two parts of a fit)
CHAPTER ONE : Fits and Tolerances

## Slide 16
24. Clearance fit
25. Interference fit
26. Transition fit
CHAPTER ONE : Fits and Tolerances
Shaft
Hole
Clearance fit
Shaft
Hole
Tolerance Zone of Hole
Tolerance Zone of Shaft

## Slide 17
27. Minimum clearance
28. Maximum clearance
29. Minimum interference
CHAPTER ONE : Fits and Tolerances

## Slide 18
30. Maximum interference
31. Shaft-basis system of fits
32. Hole-basis system of fits
CHAPTER ONE : Fits and Tolerances
Figure 1.3: Basic hole and shaft system

## Slide 19: 31 - Basic Shaft System of fits
In this system the size of the shaft remains the same and the hole size is varied to get the required fit. Maximum shaft size is taken as the basic size, an allowance is assigned, and tolerances are applied on both sides of and away from this allowance.
CHAPTER ONE : Fits and Tolerances

## Slide 20: 32 - Basic Hole System of fits
In this system the size of the hole remains the same and shaft size is varied to get the required fit. Minimum hole is taken as the basic size, an allowance is assigned, and tolerances are applied on both sides of and away from this allowance.
CHAPTER ONE : Fits and Tolerances

## Slide 21
Or Zero deviation line
CHAPTER ONE : Fits and Tolerances

## Slide 22
CHAPTER ONE : Fits and Tolerances
Notes: https://en.wikipedia.org/wiki/Engineering_tolerance

## Slide 23: Some definitions
Basic Size: is the size from which limits or deviations are assigned. Basic sizes, usually diameters, should be selected from a table of preferred sizes.
Deviation: is the difference between the basic size and the hole or shaft size.
Upper Deviation: is the difference between the basic size and the permitted maximum size of the part.
Lower Deviation: is the difference between the basic size and the minimum permitted size of the part.
CHAPTER ONE : Fits and Tolerances
Notes: https://en.wikipedia.org/wiki/Engineering_tolerance
http://bukbazzar.blogspot.com/2015/04/limits-and-fits.html

## Slide 24: Some Definitions
Fundamental Deviation: is the deviation closest to the basic size. This is identical to the upper deviation for shafts and the lower deviation for holes in a clearance fit.
Tolerance: is the difference between the permitted minimum and maximum sizes of a part.
CHAPTER ONE : Fits and Tolerances

## Slide 25: Some Definitions
The hole-basis system of preferred fits is a system in which the basic diameter is the minimum size of the hole. For the generally preferred hole-basis system, the fundamental deviation is specified by the upper-case letter.
The shaft-basis system of preferred fits is a system in which the basic diameter is the maximum size of the shaft. The fundamental deviation is given by the lowercase letter.
CHAPTER ONE : Fits and Tolerances

## Slide 26: Some Definitions
An interference fit results in an interference between two mating parts under all tolerance conditions.
A clearance fit results in a clearance between the two mating parts under all tolerance conditions.
A transition fit results in either a clearance or an interference condition between two assembled parts.
CHAPTER ONE : Fits and Tolerances

## Slide 27
CHAPTER ONE : Fits and Tolerances

## Slide 28
1.2 Symbols for Tolerances and Deviation and Symbols for Fits:
Tolerance values (The tolerance value is a function of the basic size and is indicated by a number called the grade. )
2. Tolerance zone position
The position of the tolerance zone with respect to the zero line, is indicated by a letter symbol, a capital letter for holes and a small letter The tolerance size thus defined by its basic value followed by a symbol composed of a letter and a number. It is established by a combination of the fundamental deviation indicated by a letter and the IT grade number. In the dimension 50H8, the H8 specifies the tolerance zone.
Example for shaft: 45 g7
International Tolerance Grade (IT)
CHAPTER ONE : Fits and Tolerances
Notes: https://books.google.com.sa/books?id=iwcMo9neBRMC&pg=PA144&lpg=PA144&dq=fundamental+deviation+selection+fits&source=bl&ots=67sTVnD757&sig=rR2GRTtSKmuvsYzCwapuA5_9LGM&hl=en&sa=X&redir_esc=y#v=onepage&q=fundamental%20deviation%20selection%20fits&f=false

## Slide 29
1.2 Symbols for Tolerances and Deviation and Symbols for Fits:
3.A fit (A fit is indicated by the basic size common to both components, followed by symbol corresponding to each component, the hole being quoted first)
CHAPTER ONE : Fits and Tolerances
https://books.google.com.sa/books?id=2ck0AwAAQBAJ&pg=SA6-PA13&lpg=SA6-PA13&dq=fundamental+deviation+selection+fits+IT&source=bl&ots=ZO-M0zNqbP&sig=ofRGWezbxKzJe9uW9zwxVZRZPdk&hl=en&sa=X&redir_esc=y#v=onepage&q=fundamental%20deviation%20selection%20fits%20IT&f=false
Example: 45 H8 g7
Possibly 45 H8 – g7
Or 45 H8/g7
Notes: http://www.engineeringessentials.com/ege/tol/tol_page9.htm

## Slide 30
1.3: Grades of tolerances:
CHAPTER ONE : Fits and Tolerances
Eighteen grades of tolerances are provided IT01, IT0 and IT1 to IT16 The Table 1.1 gives the possible degrees of precision or grade of tolerance, achieved with different machine tools.
Notes: http://www.engineersedge.com/international_tol.htm

## Slide 31
CHAPTER ONE : Fits and Tolerances
Tolerance grade | Intended for | Applicable to components or machines
I T 01 | Gauges | Slip blocks, Reference gauges
I T 0 |  | 
I T 1 |  | 
I T 2 |  | High quality gauges
I T 3 |  | 
I T 4 |  | 
I T 5 | Fits | Ball bearing
I T 6 |  | Grinding, Honing
I T 7 |  | Broaching
I T 8 |  | Center lathe turning
I T 9 |  | Worn automatic lathe
I T 10 |  | Milling
I T 11 |  | Drilling, Rough turning
I T 12 | Not for fits | Light press work
I T 13 |  | Press work
I T 14 |  | Die casting
I T 15 |  | Stamping
I T 16 |  | Sand casting
Table 1.1: degree of precision or grade of tolerance

## Slide 32: Representation of Tolerance 2) Number or Grade IT01, IT0, IT1,….IT16
Tolerance Grade defines range of dimensions (dimensional variation)
There are manufacturing constraints on tolerance grade chosen
International Tolerance Grade Selection
CHAPTER ONE : Fits and Tolerances

## Slide 33
CHAPTER ONE : Fits and Tolerances

## Slide 34: Example
CHAPTER ONE : Fits and Tolerances
Notes: For both hole and the shaft only unilateral tolerances are selected bcz these are presented as basic hole and shaft for which lower and upper deviation respectively are zero.

## Slide 35: Metric Preferred Hole Based System of fit
CHAPTER ONE : Fits and Tolerances
Notes: http://www.moorepants.info/jkm/courses/eng4/lectures/lecture14.html#slide-17

## Slide 36: Metric Preferred shaft Based System of fit
CHAPTER ONE : Fits and Tolerances
Notes: http://www.moorepants.info/jkm/courses/eng4/lectures/lecture14.html#slide-17

## Slide 37
CHAPTER ONE : Fits and Tolerances
Figure 1.5: Position of the various tolerance zones for a given diameter in the ISO system
Holes
Shafts
Notes: ISO Method to Determine Tolerance
Procedure
Basic size selection
Determine the preferred fit
International Grade
Determine tolerances

## Slide 38
CHAPTER ONE : Fits and Tolerances
Notes: https://books.google.com.sa/books?id=iwcMo9neBRMC&pg=PA144&lpg=PA144&dq=fundamental+deviation+selection+fits&source=bl&ots=67sTVnD757&sig=rR2GRTtSKmuvsYzCwapuA5_9LGM&hl=en&sa=X&redir_esc=y#v=onepage&q=fundamental%20deviation%20selection%20fits&f=false

## Slide 39: Table for fundamental deviations for shafts
Notes: https://books.google.com.sa/books?id=2ck0AwAAQBAJ&pg=SA6-PA13&lpg=SA6-PA13&dq=fundamental+deviation+selection+fits+IT&source=bl&ots=ZO-M0zNqbP&sig=ofRGWezbxKzJe9uW9zwxVZRZPdk&hl=en&sa=X&redir_esc=y#v=onepage&q=fundamental%20deviation%20selection%20fits%20IT&f=false

## Slide 40: Table for fundamental deviations for shafts
CHAPTER ONE : Fits and Tolerances
Notes: https://books.google.com.sa/books?id=2ck0AwAAQBAJ&pg=SA6-PA13&lpg=SA6-PA13&dq=fundamental+deviation+selection+fits+IT&source=bl&ots=ZO-M0zNqbP&sig=ofRGWezbxKzJe9uW9zwxVZRZPdk&hl=en&sa=X&redir_esc=y#v=onepage&q=fundamental%20deviation%20selection%20fits%20IT&f=false

## Slide 41: Table for fundamental deviations for holes
Notes: https://books.google.com.sa/books?id=2ck0AwAAQBAJ&pg=SA6-PA13&lpg=SA6-PA13&dq=fundamental+deviation+selection+fits+IT&source=bl&ots=ZO-M0zNqbP&sig=ofRGWezbxKzJe9uW9zwxVZRZPdk&hl=en&sa=X&redir_esc=y#v=onepage&q=fundamental%20deviation%20selection%20fits%20IT&f=false

## Slide 42: Table for fundamental deviations for holes
Notes: https://books.google.com.sa/books?id=2ck0AwAAQBAJ&pg=SA6-PA13&lpg=SA6-PA13&dq=fundamental+deviation+selection+fits+IT&source=bl&ots=ZO-M0zNqbP&sig=ofRGWezbxKzJe9uW9zwxVZRZPdk&hl=en&sa=X&redir_esc=y#v=onepage&q=fundamental%20deviation%20selection%20fits%20IT&f=false

## Slide 43
1.4 Fundamental tolerance unit:
1.4.1Values of standard tolerances:
T = 10 0.2 (G – 1) (0.45 3√D + 0.001D)
G = Tolerance grade IT6 – IT 16
1.4.2 Fundamental deviations:
1.4.2.1 Shaft deviation:
For each letter symbol defining the position of the tolerance zone, the magnitude and sign of one of the two deviations which is known as the fundamental deviations (upper deviation) “es” or lower deviation “ei”
The other deviation is derived from the first one using the magnitude of the standard tolerance “IT”, by means of the following algebraic relationship:
The fundamental deviation given by the formulae in above tables of deviations is, in principle, that corresponding to that limit closest to the zero line, in other words, the upper deviation “es” for shafts (a) to (h), and the lower deviation “ei” for shafts (j) to (Zc).
ei = es - IT
es = ei + IT
CHAPTER ONE : Fits and Tolerances

## Slide 44
1.4.2.2 Hole deviation:
For each letter symbol, defining the position of the tolerance zone, the magnitude and sign of the fundamental deviation (lower deviation “EI” for holes (A) to (H) and upper deviation “ES” for holes (J) to (Zc),
The other deviation is derived from the first one, using the magnitude of the tolerance “IT” by means of the following relationships.
ES = EI + IT
OR
EI = ES - IT
CHAPTER ONE : Fits and Tolerances

## Slide 45: Example
Determine which type of fit is presented by H7/p6? For basic size of 30 mm determine the dimensions of the hole and the shaft for the given fit. (Fit: 30 H7/p6)
H7 : Tol Grade 7 mean 21μ variation
Capital H means basic hole system and upper deviation = zero
p6 : Tol Grade 6 means 13μ variation
(p means upper deviation is 22 μ)
Φ30.000
Φ30.021
Φ30.022
Φ30.035
INTERFERENCE FIT
Fit: 40 H8/e6

## Slide 46
CHAPTER ONE : Fits and Tolerances
Figure 1.7: Two comparable fits, with basic hole and basic shaft, in which a hole of a given grade is associated with a shaft with next finer grade (H7/P6 and P7/h6), have exactly the same clearance or interference.