## Slide 1: Lec1: Experiment
Designing the network, IP addressing and Subnets, designing using Variable Length Subnet Mask
Dr. Mohamed Abd-Eldayem
References:
  CCNA Curriculum
  CCNA Command Quick Reference by Scott Epson

## Slide 2: Network Devices Comparison
L3 Switch - Router | Bridge
Work on Layer 3 (Network Layer) of the OSI model | Work on Layer 2 (Data Link Layer) of the OSI model
Uses the IP address (Logical Address) for locating devices in the network. | Uses the MAC address (physical address) to locate devices in the network
Connects multiple network segments together | Connect two similar network segments together
Saves the bandwidth of the network because it establishes a direct link between the source and the destination address | Waste the bandwidth of the network because it broadcast messages

## Slide 3: IP address VS. MAC address
IP address | MAC address
Is a 32-bit (logical address) that is assigned to devices attached to the network by network devices such as switch. Used in layer 3 (Network Layer) of the OSI model | Is a (physical address) that is written on the network card of devices (permanent address). Used in layer 2 (Data Link Layer) of the OSI model

## Slide 4: 2.1 Ethernet Switching 2.1 Layer 2 bridging
00000CBBBBBB

## Slide 5: 2.1 Layer 2 bridging (A -> B)
The bridge has just been started so the bridge table is empty.
The bridge just waits for traffic on the segment. When traffic is detected, it is processed by the bridge.
Host A is pinging Host B. Data is transmitted on the entire collision domain (segment1), both the bridge and Host B process the packet.
Bridge Table | 
Port | MAC Address

## Slide 6: 2.1 Layer 2 bridging (A -> B)
The bridge adds the source address of the frame (Host A) to its bridge table. Since the frame was received on port 1, the frame must be associated with port 1 in the table.
The destination address of the frame is checked against the bridge table. Since the address is not in the table, the frame is forwarded to the other segment (Segment2).
Bridge Table | 
Port | MAC Address
Port 1 | 00000CAAAAAA

## Slide 7: 2.1 Layer 2 bridging (A -> B)
Host C & D discards the received frame as they were not the intended destination.
Host B processes the ping request and transmits a ping reply back to Host A. The data is transmitted over the whole collision domain. Both Host A and the bridge receive the frame and process it.
The bridge
  Adds the source address of the replay frame to its bridge table (Host B).
  Check the destination address of the frame against the bridge table. Since the address is found in the table at port 1 the frame is not forwarded.
Bridge Table | 
Port | MAC Address
Port 1 | 00000CAAAAAA
Port 1 | 00000CBBBBBB

## Slide 8: 2.1 Layer 2 bridging (A -> C)
Host A ping Host C.
  the frame is transmitted on the entire collision domain (segment1)
  Both the bridge and Host B process the frame.
  Host B discards the frame as it was not the intended destination.
The Bridge renew the source address of the frame (Host A) in the bridge table because it is already entered.
The destination address of the frame (Host C) is checked against the bridge. Since the address is not in the table, the frame is forwarded to the other segment (Segment2)

## Slide 9: 2.1 Layer 2 bridging (A -> C)
Host C processes the ping request and transmits a ping reply back to Host A. The data is transmitted over the whole collision domain (Segment 2).
Host D discards the frame, as it was not the intended destination.

## Slide 10: 2.1 Layer 2 bridging (A -> C)
The bridge adds the source address of the frame (Host C) to its bridge table. The frame must be associated with port 2 in the table.
The destination address of the frame (Host A) is checked against the bridge. The address is in the table but it is associated with port 1, so the frame is forwarded to the other segment (Segment1).
Bridge Table | 
Port | MAC Address
Port 1 | 00000CAAAAAA
Port 1 | 00000CBBBBBB
Port 2 | 00000CCCCCCC

## Slide 11: A bridge has only two ports and divides a collision domain into two parts, but it do not affect the logical or Layer 3 addressing. Thus, a bridge will divide a collision domain but has no effect on a logical or broadcast domain.

## Slide 12: 2.2 Switch operation
A switch is simply a bridge with many ports. When only one node (computer) is connected to a switch port, the collision domain on the shared media contains only two nodes.
Most switches are capable of supporting full duplex (means that data can be transmitted in both directions on the medium at the same time)

## Slide 13: Revision: Converting Decimal To Binary
Example convert the decimal number 198 to binary number?
Decimal Number | Divisor | Reminder
198 | 2 | 0
99 | 2 | 1
49 | 2 | 1
24 | 2 | 0
12 | 2 | 0
6 | 2 | 0
3 | 2 | 1
1 | 2 | 1
0 |  | 
The binary number is the reminder written from the bottom to the top
Decimal: 198
Binary: 11000110

## Slide 14: Revision: Converting Binary To Decimal
Converting the binary number 11000110 to decimal number
0 | 1 | 1 | 0 | 0 | 0 | 1 | 1
+ 0 x 20 | + 1 x 21 | + 1 x 22 | + 0 x 23 | + 0 x 24 | + 0 x 25 | + 1 x 26 | 1 x 27
0 | 2 + | 4 + | 0 + | 0 + | 0 + | 64 + | 128 +
 |  |  |  | = 198 | Number | Decimal | 

## Slide 15: IP Address
An IP address is four bytes (octets). Each contains eight bits (total of 32 bits in length).
Each octet is a number from 1 to 254.
IP addresses are usually given as dotted decimal notation.

## Slide 16
Class A, B, C, D, and E IP addresses
IP addresses are divided into five classes:
  Class A addresses are assigned to larger networks.
  Class B addresses are used for medium-sized networks.
  Class C for small networks.
  Class D used by multicast group.
  Class E reserved by research groups
Each class uses a different combination of octets to indicate the number of the network and the number of the host.
The first step in determining which part of the address identifies the network and which part identifies the host is identifying the class of an IP address.

## Slide 17: IP Classes
Class A
Class B
Class C

## Slide 18: 2.4 Reserved IP addresses:
Network address – Used to identify the network itself
  An IP address that has binary 0s in all host bit positions is reserved for the network address.
  Ex.: The 198.150.11.0 network.
    Data that is sent to any host on that network (ex: hosts number 198.150.11.1- 198.150.11.254) will be seen outside of the local area network as 198.159.11.0.
    The only time that the host numbers matter is when the data is on the local area network.
Broadcast address – Used for broadcasting packets to all the devices on a network
  The 198.150.11.255 broadcast address. Data that is sent to the broadcast address will be read by all hosts on that network (198.150.11.1- 198.150.11.254).

## Slide 19: Host & Network Portions for the different classes
Class | First octet | Example | Network Part | Host part | Number of Networks | Number of Hosts *
A | 1-126 | 12.240.60.89 127.8.90.2 | xxx.xxx.xxx.xxx | xxx.xxx.xxx.xxx | 126 | (23*23*23)-2 = 16777214
B | 128-191 | 130.240.60.89 191.8.90.2 | xxx.xxx.xxx.xxx | xxx.xxx.xxx.xxx | 16,384 | (23*23)-2 = 65,534
C | 192-223 | 192.240.60.89 223.8.90.2 | xxx.xxx.xxx.xxx | xxx.xxx.xxx.xxx | 2 million | (23)-2 = 254
The first address ( xxx.xxx.xxx.0) & the last address (xxx.xxx.xxx.111) are reserved for the network
( xxx.xxx.xxx.0) for the network & (xxx.xxx.xxx.111) for broadcasting

## Slide 20
Unicast | Broadcast | Multicast
Unicast packets are sent from single host to another single host. | Broadcast is when a single device is transmitting a message to all other devices in a given address range. | Multicast enables a single device to communicate with a specific set of hosts, not defined by any standard IP address and mask combination.
There is one device transmitting a message destined for one receiver. | This broadcast could reach all hosts on the subnet, all subnets, or all hosts on all subnets. Broadcast packets have the host (and/or subnet) portion of the address set to all ones. | Communication resembles a conference call. Anyone from anywhere can join the conference, and everyone at the conference hears what the speaker has to say. The speaker's message isn't broadcasted everywhere, but only to those in the conference call itself.

## Slide 21: Example1
Network Address: 72.0.0.0
Host1: 72.167.98.77
Host2: 72.167.98.70
Host3: 72.167.98.75
Host4: 72.167.98.71
What is the Network address?
72.0.0.0
To which class this network belongs?
Class A because network number = 72
72 ϵ {1-126}
What is the broadcast address?
72.255.255.255
What is the IP addresses of the hosts?
IP Address of host1: 72.167.98.77
IP Address of host2: 72.167.98.70
IP Address of host3: 72.167.98.75
IP Address of host4: 72.167.98.71
LAN

## Slide 22: What is subnetting?
Subnetting is the process of borrowing bits from the HOST bits, in order to divide the larger network into small subnets.
Subnetting does NOT give you more hosts, but actually costs you hosts (decrease number of hosts).
You lose two host IP Addresses for each subnet, and perhaps one for the subnet IP address and one for the subnet broadcast IP address.

## Slide 23: Why Do We Use Subnetting?
A company uses two or more types of LAN technology (for example, Ethernet, Token Ring) on their network or different physical media (such as Ethernet, FDDI, WAN, etc.)
Two network segments are restricted by distance limitations (for example, remote offices linked via point-to-point circuit).
Segments need to be localized for network management reasons (accounting segment, sales segment, etc.).
Hosts which dominate most of the LAN bandwidth need to be isolated.
Security.
The most common reason is to control network traffic.

## Slide 24: How it works?
The IP address is split into a network and host portion.
The network portion always remains fixed for a particular network, while the remaining bits which make up the host portion can be altered to give the range of addresses to assign to hosts.
To determine where the network portion ends and the host portion begins, a subnet mask is used.

## Slide 25: Subnet Mask
A subnet mask is used to separate a network number from the host number in an IP address.
255 represents a network and 0 represents a host.
Default subnet masks:
Class A - 255.0.0.0 - 11111111.00000000.00000000.00000000
Class B - 255.255.0.0 - 11111111.11111111.00000000.00000000
Class C - 255.255.255.0 - 11111111.11111111.11111111.00000000

## Slide 26: Steps to Solve Subnetting Questions
Look at the MSB (Most Significant Bit) of the IP, Identify the Class(A, B or C), then determine the number of bits assigned to the Network Portion
(8 for class A, 16 for Class B and 24 for Class C)
  Ex.: IP=182.250.200.3, Class = B, N =16 bits
Look at Subnet Mask (SM), the number of zeros identify the Host portion
  Ex. SM = 11111111.11111111.11111111.00000000, H=8 bits
Look at IP and SM together, The portion Between the Network and Host portions is the Sub Network portion.
  Ex. IP= 182 . 250 . 200 . 3
  10110110. 11111010.11001000.00000011
  SM = 11111111.11111111.11111111.00000000 = 255.255.255.0
N = 16
SN = 8
H= 8

## Slide 27
Identify the Subnet ID: By doing (IP address ) AND (Mask)
  Subnet ID = 10110110. 11111010.11001000.00000000
Identify Broadcast address: By changing all bits of host portion in Subnet ID to 1’s.
  Broadcast address = 10110110. 11111010.11001000.11111111
Identify the First IP address: Change the LSB of host portion in Subnet ID to 1.
  First IP address = 10110110. 11111010.11001000.00000001
Identify the Last IP address: Subtract 1 from host portion of Broadcast address.
  Last IP address = 10110110. 11111010.11001000.11111110
Steps to Solve Subnetting Questions

## Slide 28: Example (1)
Given the following IP address 38.9.211.19 with a subnet mask of 255.255.255.240 determine:
  Network Address
  Default subnet mask
  Broadcast address of the network
  Subnet ID
  Broadcast address of the subnet.
  First & last host address in the subnet.

## Slide 29: Example (1)
Network Address
    To determine the network address we have to determine the class of the IP address
    38.9.211.0  38 ϵ {1-126} Class A
    In class A network portion is the first octet & the remaining three octets for the host are zeros.
    Network Address: 38.0.0.0

## Slide 30: Example (1)
  Default subnet mask
  For Class A addresses, default subnet mask is: 255.0.0.0
  Broadcast address of the network
  Changing all the host bits to 1 give you the broad cast address:
  Broadcast Address = 38.255.255.255

## Slide 31: Example (1)
  Subnet ID:
    First: Determine the following bits in the following order:
      Network portion (N) (Fixed depends on the IP class)
      Subnet portion (S) (From the end of the network portion to the last bit in the mask with the value 1)
      Host portion (H) (The remaining bits after the subnet portion)
IP 00100110.00001001.11010011 . 00010011
Mask 11111111 . 11111111 . 11111111 .11110000
N = 8
H=4
S = 20

## Slide 32: Example (1)
    Second:
    Do the AND operation between the IP address & the mask
IP 00100110.00001001.11010011 . 00010011
Mask 11111111 . 11111111 . 11111111 .11110000
    ______________________________________________
  Subnet ID 00100110.00001001.11010011 . 00010000
  Subnet ID in decimal = 38.9.211.16
AND

## Slide 33: Example (1)
  Broadcast address of the subnet.
  To get the broad cast address replace the host bits in the subnet ID with 1s
  Subnet ID 00100110.00001001.11010011 . 00010000
Broadcast Address 00100110.00001001.11010011 . 00011111
Broadcast Address in decimal 38.9.211.31
Host bits

## Slide 34: Example (1)
  First & last host address in the subnet.
  To get the first address replace all the host bits with zeros except the last bit replace it with one as follows:
  Subnet ID 00100110.00001001.11010011 . 00010000
  First Host Address 00100110.00001001.11010011 . 00010001
  First Host Address in decimal 38.9.211.17
Host bits
Host bits

## Slide 35: Example (1)
  First & last host address in the subnet.
  To get the last address replace all the host bits with ones except the last bit replace it with zero as follows:
  Subnet ID 00100110.00001001.11010011 . 00010000
  Last Host Address 00100110.00001001.11010011 . 00011110
  Last Host Address in decimal 38.9.211.30
Host bits
Host bits

## Slide 36: Example (2): IP=182.250.200.028, SM= 255.255.255.248
  IP = 10110110. 11111010.11001000.00011100
  SM = 11111111.11111111.11111111.11111000
  Class of the IP is B
  Network Address= 10110110. 11111010.00000000.00000000
  Default Subnet Mask of the IP = 11111111.11111111.00000000.00000000
  Broadcast address of the network = 10110110. 11111010.11111111.11111111
  Subnet ID = 10110110. 11111010.11001000.00011000
  Broadcast address of the subnet = 10110110. 11111010.11001000.00011111
  First IP address = 10110110. 11111010.11001000. 00011001
  Last IP address = 10110110. 11111010.11001000. 00011110
N = 16
SN = 13
H= 3

## Slide 37: In Decimal Example (2): IP=182.250.200.28, SM= 255.255.255.248
  IP = 182.250.200.28
  SM = 255.255.255.248
  Class of the IP is B
  Network Address= 182.250.0.0
  Default Subnet Mask of the IP = 255.255.0.0
  Broadcast address of the network = 182.250.255.255
  Subnet ID = 182.250.200.024
  Broadcast address of the subnet = 182.250.200.31
  First IP address = 182.250.200.025
  Last IP address = 182.250.200.030

## Slide 38: Demonstrating the different type of IPs in Example (2)
Subnet ID: 182.250.200.024
Network Address: 182.250.0.0
First IP: 182.250.200.025
Last IP: 182.250.200.030

## Slide 39: Public and private IP addresses
Public IP addresses are unique and it must be obtained from an Internet service provider (ISP)
RFC 1918 sets aside three blocks of IP addresses for private, internal use. These three blocks consist of one Class A, a range of Class B addresses, and a range of Class C addresses. Addresses that fall within these ranges are not routed on the Internet backbone. Internet routers immediately discard private addresses.

## Slide 40: Public and private IP addresses
If addressing a nonpublic intranet, a test lab, or a home network, private addresses can be used instead of globally unique addresses.
Connecting a network using private addresses to the Internet requires translation of the private addresses to public addresses. This translation process is referred to as Network Address Translation (NAT).

## Slide 42
  For any IP address, if the subnet mask is the default IP address of that class then there is no subnetting

## Slide 43: Establishing the subnet mask address
Selecting the number of bits to use in the subnet process will depend on the maximum number of hosts required per subnet.
Most Significant Bit (MSB) Least Significant Bit (LSB)
The last two bits in the last octet, regardless of the IP address class, may never be assigned to the subnetwork.
The subnet mask gives the router the information required to determine in which network and subnet a particular host resides.

## Slide 44: Establishing the subnet mask address
If three bits were borrowed, the mask for a Class C address would be 255.255.255.224.
This mask may also be represented, in the slash format, as /27. The number following the slash is the total number of bits that were used for the network and subnetwork portion
To determine the number of bits to be used, the network designer needs to calculate how many hosts the largest subnetwork requires and the number of subnetworks needed.

## Slide 45
Subnetting chart

## Slide 46: Ex1.: A network requires 30 hosts and five subnetworks. IP = 192.168.10.0, Class C
Using the subnetting chart, by consulting the row titled ”Usable hosts”, the chart indicates that for 30 usable hosts three bits are required. This creates, six usable subnetworks.
Number of usable subnets= two to the power of the assigned subnet bits or borrowed bits, minus two (reserved addresses for subnetwork id and subnetwork broadcast)
  usable subnets =(2 borrowed bits) – 2 = (23) – 2 = 6
Number of usable hosts= two to the power of the bits remaining, minus two (reserved addresses for subnet id and subnet broadcast)
  usable hosts= (2 remaining host bits) – 2 = (25) – 2 = 30

## Slide 47: Ex1.: A network requires 30 hosts and five subnetworks. IP = 192.168.10.0, Class C

## Slide 48: Subnetting Class A and B networks
The available bits for assignment to the subnet field in a Class A address is 22 bits while a Class B address has 14 bits.
Assigning 12 bits of a Class B address to the subnet field creates a subnet mask of 255.255.255.240 or /28.
Assigning 20 bits of a Class A address to the subnet field creates a subnet mask of 255.255.255.240 or /28.
class of address needs to be subnetted:
  Total subnets = 2 the bits borrowed Total hosts= 2 the bits remaining Usable subnets = 2 the bits borrowed - 2 Usable hosts= 2 the bits remaining - 2