## Slide 1
CT 1306 Communication Networks Management Lab
Lec2
Based on Dr. Mahmood Abduldayem lectures

## Slide 2: Communication Networks Management
Communication Networks Management: Refers to the activities, methods, procedures, and tools related to operate, manage, maintain, and control resources for network systems. it includes the following responsibilities:
  Maintaining the stability of the network performance (and the services provided by the network) to work smoothly.
  Monitoring the network to discover problems as soon as possible, before users are affected.

## Slide 3: Communication Networks Management
  Tracking resources in the network and how they joined the network.
  Fixing and developing the network continuously to maintain its performance. For example:
    Exchanging old network devices.
    When new devices (such as Switch) is added to the network.

## Slide 4: Communication Networks Management
  Implementing corrective and preventive procedures to increase the network performance, such as:
    modifying the control parameters (Configuration) of network device.
  controlling resources in the network to support a particular service.
    Example: setting up the network so that users can have new service such as voice.

## Slide 5: Communication Networks Management
Functions that are implemented as part of the network management include:
  Monitoring, planning ,allocation, deployment, coordination of network resources
  Network planning,
  Directing the traffic of the data to balance the load of data in the network.
  Encryption key distribution.
  Setting management.
  Fault management
  Security management
  Performance management
  Bandwidth management

## Slide 7: Gathering data for Network Management
The data are collected to manage the network using different methods as follows:
  Software agents installed on infrastructure of the network
  Activity log files
  Spyware Sniffer
  Real monitoring by the user.

## Slide 8: "Simple Network Management Protocol"
SNMP is an acronym for "Simple Network Management Protocol"
SNMP is one of the seventh layer (Application Layer) protocols, the layer that is used by the network management system to monitor devices connected to the network.
SNMP is part of the Internet protocol package.