## Slide 1: CT1303 LAN
Rehab AlFallaj

## Slide 2: Standard Models:
OSI Model : Open system Interconnection.
  is a conceptual model that characterizes and standardizes the internal functions of a communication system by partitioning it into abstraction layers. The model is a product of the Open Systems Interconnection project at the International Organization for Standardization (ISO)

## Slide 3: Standard Models:
OSI Model : Open system Interconnection.
Layered Model: Why?
  Change.
  Design.
  Learning.
  Troubleshooting.
  Standards.

## Slide 4: ISO Model
Physical Layer:
  Electronic, Electrical, mechanical and procedural aspects of electrical signal of the data transmission.
  Physical interface between devices
  Handle transmission of bits over communication channel.
  Choice of wired or wireless medium.
  Data is converted into signals
  Include voltage level , connectors, media choice.
  Modulation techniques
  Its responsible the movement of individual bits from one node to another

## Slide 5: ISO Model

## Slide 6: ISO Model
Data Link Layer:
  Concerned with the linkages and mechanisms used to move data about the network, and deals with the ways in which data is reliably transmitted (integrity), Error checking.
  Transforms data into frame.
  Means of activating , maintaining and deactivating a reliable link.
  Error detection and control.
  Flow control.
  Higher layers may assume error free transmission.
  Its responsible the movement of frames from one node to another

## Slide 7: ISO Model

## Slide 8: ISO Model
Network Layer:
  Switching, Routing data across the network.
  Congestion control, Error handling
  Defines the processes used of logical addressing.
    IP addressing
  Transport of information
  Higher level do not need to know about underlying technology.
  responsible for creating , maintaining and ending network connection.
  Transfer a data packet from node within the network.
  Routing
  Its responsible the movement of individual packet from the source host to destination host.

## Slide 9: ISO Model

## Slide 10: ISO Model
Transport Layer:
  responsible for end-to-end error recovery and flow control. It ensures complete data transfer.
  disassembly and assembly of the data before and after transmission.
  Exchange of data between end system.(end to end flow control)
  Error free
  Quality of service.
  Layer 4 include transmission control protocol and user datagram protocol.
  Its responsible the delivery of message from one process to another.

## Slide 11: Iso model

## Slide 12: ISO Model
Session Layer:
  establishes, maintains, and manages the communication session (conversation, exchanges and dialogues) between computers, applications and each end.
  Control dialogue between applications
  Half duplex, full duplex.
  Synchronization points (back up point)
  Its responsible dialog control and synchronization

## Slide 13: Iso model
Presentation Layer:
  provides independence from differences in data representation (e.g., encryption) by translating from application to network format, and vice versa.
  transform data into the form that the application layer can accept
  Data formats and coding
  Data compression
  Encryption
  Its responsible translation , compression and encryption

## Slide 14: ISO model
Application Layer:
  Supports application and end-user processes. Communication partners are identified, quality of service is identified, user authentication and privacy are considered, and any constraints on data syntax are identified.
  Everything at this layer is application-specific. This layer provides application services for file transfers, e-mail, and other network software services. Telnet and FTP are applications that exist entirely in the application level. Tiered application architectures are part of this layer.
  Browsers, FTP clients, and mail clients are part of the application layer, Microsoft WORD,EXCEL are not.

## Slide 15: Iso model
  Layer where the application using the network resides
  Common network application include :remote login , file transfer, e-mail and web browsing
  Means for application to access OSI environment.
  Its responsible for providing the service for user.

## Slide 16: Iso model

## Slide 17: lan standard model
IEEE 802 standard model:
Four 4 main layers.
Physical Layer:
  Electronic, Electrical, mechanical and procedural aspects of electrical signal of the data transmission.
Data Link Layer:
  That consists of two sub-layers:
  Logical Link Control LLC.
  Media Access Control MAC.

## Slide 18: IEEE 802 model:
  Logical Link Control LLC protocol:
    Layer 2 uses Logical Link Control(LLC) to communicate with the upper-level layers.
    Establishment and control logical link between local devices.
    Synchronization تحديد سرعة التبادل بين الوحدات
    Error Control التحكم بالاخطاء
  Medium Access Control MAC:
    Layer 2 uses Media Access Control(MAC) to decide which computer will transmit.
    Protocols to data entering to network media
    MAC Addressing.
    Collision control.

## Slide 19: IEEE 802 model
Network Layer:
  Routing data across network and from a network to another different one.
Other layers:
  No rigid standard for the rest layers as it may vary from network to another one due to its functions and types.
  They could be OSI upper layers or any other standard model layers.

## Slide 20: OSI vs. IEEE 802 model

## Slide 21: LAN applications
Electronic Communication applications:
  Cheap
  Fixable
  Effectiveness
  Remote access to data
  Access to data from different places( network devices)

## Slide 22: LAN applications
Examples of Electronic Communication applications
  Email applications.
  Chatting applications.
  Audio and Video conferencing applications.
  Cyberspace conferencing.

## Slide 23: LAN applications
Distributed data bases:
  Data entered into a central datacenter or into a distributed databases then can be retrieved from varies local devices in the network.
    Universities database.
    Companies databases.

## Slide 24: Lan applications
Distributed information systems:
  systems that automate the operations of commercial enterprises such as banking and financial transaction processing systems, warehousing systems, and automated factories.
  Communicates to central computers (governments, universities) to retrieve or process information.

## Slide 25: Lan applications
Office automation and teamwork:
  Resource sharing: printers, storage.
  Reduce costs.
  Increase productivity
  Doing a collective work

## Slide 26: Lan application
Electronic transactions:
  Facilitate administrative work
  Reporting systems
  Document editing and viewing
  Document signing
  Document transfers
E-Business : for private business use
E-Government: for government use

## Slide 27: Lan application
Process capabilities improving Applications:
  More than one computer can work collaboratively to do complex and expensive tasks.

## Slide 28: Lan application
Reliability applications:
  Applications can be used to make usage of network devices even if some are offline or unavailable.