## Slide 1
CT 1306 Communication Networks Management Lab
Lec3

## Slide 2: Problem Solving Stages

## Slide 3: Communication Networks Management
Troubleshooting methods include:
  Process of Elimination
  Divide and Conquer
Software tools include:

## Slide 4: Problem Solving Stages
Use | Main Options
Verify basic connection | -n sets the number of packets (default 5)
Track packets by hops | -j specifies loose source route; -h max hops
Layer 7 connectivity | 
View protocol statistics | -s -p tcp shows TCP protocol statistics
Map IP to MAC address | -a show contents of cache; -s add static entry
View hosts IP settings | /all ; /renew requests a new DHCP lease
Tool
ping
tracert
telnet
netstat
arp
ipconfig

## Slide 5: 1. Ping
The PING utility tests connectivity between two hosts. PING uses a special protocol called the Internet Control Message Protocol (ICMP)to determine whether the remote machine (website, server, etc.) can receive the test packet and reply.
Also a great way to verify whether you have TCP/IP installed and your Network Card is working.
We'll start by Pinging the loopback address (127.0.0.1) to verify that TCP/IP is installed and configured correctly on the local computer.
Type: PING 127.0.0.1

## Slide 6: 1. Ping
This tells me that TCP/IP is working as well as my Network Card.
To test out connectivity to a website all you have to do is type: ping espn.com

## Slide 7: 1. Ping
The results should tell you if the connection was successful or if you had any lost packets.
Packet loss describes a condition in which data packets appear to be transmitted correctly at one end of a connection, but never arrive at the other. Why? Well, there are a few possibilities.
The network connection might be poor and packets get damaged in transit or the packet was dropped at a router because of internet congestion. Some Internet Web servers may be configured to disregard ping requests for security purposes.
Note the IP address of espn.com -- 199.181.132.250. You can also ping this address and get the same result.
However, Ping is not just used to test websites. It can also test connectivity to various servers: DNS, DHCP, your Print server, etc. As you get more into networking you'll realize just how handy the Ping utility can be.

## Slide 8: 2. Tracert
Tracert is very similar to Ping, except that Tracert identifies pathways taken along each hop, rather than the time it takes for each packet to return (ping).

## Slide 9: 2. Tracert
If I have trouble connecting to a remote host I will use Tracert to see where that connection fails. Any information sent from a source computer must travel through many computers / servers / routers (they're all the same thing, essentially) before it reaches a destination.
It may not be your computer but something that is down along the way. It can also tell you if communication is slow because a link has gone down between you and the destination.
If you know there are normally 4 routers but Tracert returns 8 responses, you know your packets are taking an indirect route due to a link being down.

## Slide 10: 3. ARP
The ARP utility helps diagnose problems associated with the Address Resolution Protocol (ARP).
TCP/IP hosts use ARP to determine the physical (MAC) address that corresponds with a specific IP address. Type arp with the – a option to display IP addresses that have been resolved to MAC addresses recently.

## Slide 11: 3. ARP

## Slide 12: 4. Netstat
Netstat (Network Statistics) displays network connections (both incoming and outgoing), routing tables, and a number of network interface statistics.
It is an important part of the Network + exam but it's a helpful tool in finding problems and determining the amount of traffic on the network as a performance measurement.

## Slide 13: 4. Netstat

## Slide 14: 4. Netstat
Netstat –s provides statistics about incoming and outgoing traffic

## Slide 15: 5. NSLookup
NSLookup provides a command-line utility for diagnosing DNS problems. In its most basic usage, NSLookup returns the IP address with the matching host name.

## Slide 16: 6. IPConfig
Not part of the TCP/IP utilities but it is useful to show current TCP/IP settings.
The IPConfig command line utility will show detailed information about the network you are connected to. It also helps with reconfiguration of your IP address through release and renew.
Let's say you want to know what you're IP address is -- ipconfig is what you type in the command prompt.

## Slide 17: 6. IPConfig