## Slide 1: SNMP
M Clements

## Slide 2: Simple Network Management Protocol
Manages elements in networks
  E.g. routers, switches, IP phones, printers etc.
Uses manager agent model
  client server model
Consists of
  Manager running network management system, agent, database of management information (Management Information Base MIB), managed devices (slaves), network protocol

## Slide 3: Uses of SNMP
Querying networked devices regularly to gain data to draw graphs
Warning administrator when managed device reached some predefined threshold
  E.g. sys admin could monitor the temperature of a server chassis
Provides data for future growth planning

## Slide 4: Management Information Base (MIB)
Used to pull information from network devices that enable SNMP.
Tree structure
  Variables represented as leaves on branches
  E.g. "free memory", "system name", "number of running processes", "default route"
  hierarchical namespace containing object identifiers (OID)
Used by manager and agent
Describes the structure of the management data of a device subsystem

## Slide 6: What is Object Identifier (OID)?
uniquely identify managed objects in a MIB hierarchy.

## Slide 7: Variable Descriptors
Variables described numerically
Selected from MIB tree
Uses numerical system
Abstract Syntax notation One (ASN.1)

## Slide 8
MIB group structure
ASN.1 standard describes data structures for representing, encoding, transmitting, and decoding data
Removes ambiguities by providing machine-independent method of addressing variables

## Slide 9: SNMP Operation
Manager can request information from managed device using GET, GETNEXT and GETBULK
Manager can update variables using SET
Agent can send data automatically using TRAP or INFORM to report alarms
Manager receives on UDP port 162
Agent receives on UDP port 161

## Slide 10: SNMP Communities
SNMP Communities: groups that devices and management stations running SNMP belong to.
Defines device groups where information is sent
Community name is used to identify the group
A SNMP device or agent may belong to more than one SNMP community and will not respond to requests from management stations that do not belong to one of its communities
SNMP default communities are:
  Write = private
  Read = public

## Slide 11: SNMP Community Strings
Like passwords for Community devices
Management device will need the strings to read and write to devices
Read-only community string often set to ‘public’
Read-write community string often set to ‘private’

## Slide 12: Enable SNMP on Cisco Routers
Example here uses default strings
Enter configuration mode (Community strings are highlighted by red)
Router(config)#snmp-server community public RO
Router(config)#snmp-server community private RW
RO specifies read only access
RW specifies read write access
Management stations need to supply the correct community strings to access the MIB data on the managed device

## Slide 13: SNMP Versions
Currently up to SNMPv3
Many network elements support only SNMPv1 and SNMPv2c. Support for SNMPv3 is minimal
SNMPv1 SNMPv1, implements community-based security
SNMPv2c SNMPv2 with community-based security
SNMPv2u SNMPv2 with user-based security
SNMPv2 SNMPv2 with party-based security
SNMPv3 SNMPv3, which implements user-based security

## Slide 14: Summary
SNMP manages networked devices
Uses GET, SET, GETNEXT, TRAP
Communities define groups for management
Community string like password
Public or private (default)
Uses UDP
Data held in MIB

## Slide 15: References
http://www.geekball.net/linksys/picture4.png
http://img.brothersoft.com/screenshots/softimage/h/hilisoft_snmp_mib_browser-63133-1.jpeg
http://publib.boulder.ibm.com/infocenter/tivihelp/v24r1/topic/com.ibm.netcool_ssm.doc/rg/images/rmon1Grp.gif