## Slide 1: Wide Area Networks and Internet CT1403
Lecture-6: Internet Network Layer
1

## Slide 2: Outline
CT1403
Datagram format, fragmentation and assembly
IP addressing: Classes, Subnets
CIDR: Classless Interdomain Routing
DHCP: Dynamic Host Configuration Protocol
<number>

## Slide 3
datagram format
      Fragmentation
      Reassembly
<number>

## Slide 4: The Internet network layer
forwarding
table
host, router network layer functions:
routing protocols
path selection
RIP, OSPF, BGP
IP protocol
addressing conventions
datagram format
packet handling conventions
ICMP protocol
error reporting
router “signaling”
transport layer: TCP, UDP
link layer
physical layer
network
layer
<number>

## Slide 5: IP datagram format
ver
length
32 bits
data
(variable length,
typically a TCP
or UDP segment)
16-bit identifier
header
checksum
time to
live
32 bit source IP address
head.
len
type of
service
flgs
fragment
offset
upper
layer
32 bit destination IP address
options (if any)
IP protocol version
number
header length
(bytes)
upper layer protocol
to deliver payload to
total datagram
length (bytes)
“type” of data
for
fragmentation/
reassembly
max number
remaining hops
(decremented at
each router)
e.g. timestamp,
record route
taken, specify
list of routers
to visit.
how much overhead?
20 bytes of TCP
20 bytes of IP
= 40 bytes + app layer overhead
<number>

## Slide 6: IP fragmentation, reassembly
network links have MTU (maximum transfer unit) - largest possible link-level frame
  different link types, different MTUs
large IP datagram divided (“fragmented”) within net
  one datagram becomes several datagrams
  “reassembled” only at final destination
  IP header bits used to identify, order related fragments
fragmentation:
in: one large datagram
out: 3 smaller datagrams
reassembly
…
…
<number>

## Slide 7: IP fragmentation, reassembly
Network Layer
4-36
ID
=x
offset
=0
fragflag
=0
length
=4000
ID
=x
offset
=0
fragflag
=1
length
=1500
ID
=x
offset
=185
fragflag
=1
length
=1500
ID
=x
offset
=370
fragflag
=0
length
=1040
one large datagram becomes
several smaller datagrams
example:
4000 byte datagram
MTU = 1500 bytes
1480 bytes in data field
offset =
1480/8
offset 0: meaning the data should be inserted at the beginning go byte 0
offset 185: meaning the data should be inserted at the beginning go byte 1480 (185*8=1480)
offset 370: meaning the data should be inserted at the beginning go byte 2960 (370*8=2960)
<number>

## Slide 8
IP Addressing
  Classes
  Subnets
<number>

## Slide 9: IP Addressing
Network Layer
IP address: 32-bit identifier for host, router interface
Interface: connection between host/router and physical link
  router’s typically have multiple interfaces (==>multiple IP addresses)
  host typically has one interface
  IP addresses associated with each interface
223.1.1.1
223.1.1.2
223.1.1.3
223.1.1.4
223.1.2.9
223.1.2.2
223.1.2.1
223.1.3.2
223.1.3.1
223.1.3.27
223.1.1.1 = 11011111 00000001 00000001 00000001
223
1
1
1
<number>

## Slide 10: Classes of IP Addresses
<number>

## Slide 11: Classes of IP Addresses
CT1403
44
<number>

## Slide 12: Classes of IP Addresses: How to count no. of Networks and Hosts within each Class
CT1403
عدد الشبكات (Class A) = 72 – 2 = 126 شبكة.
أقصى عدد الطرفيات في كل شبكة (Class A) = 242 – 2 = 16777214 طرفية.
عدد الشبكات (Class B) = 142 – 2 = 16382 شبكة.
أقصى عدد الطرفيات في كل شبكة (Class B) = 162 – 2 = 65534 طرفية.
عدد الشبكات (Class C) = 212 – 2 = 2097150 شبكة.
أقصى عدد الطرفيات في كل شبكة (Class C) = 82 – 2 = 254 طرفية.
reference: This slide is created by Dr. Mohammad Arafah
<number>

## Slide 13: Classes of IP Addresses
القيمتان صفر ( 00…0 ) و –1 ( 11… 1 ) لهما معنيان خاصان، فالقيمة صفر تعني هذه الشبكة، أما القيمة –1 فتعني بث الرسالة لجميع الطرفيات للشبكة المعنونة.
<number>

## Slide 14
Subnets
<number>

## Slide 15: Subnets
IP address:
  subnet part - high order bits
  host part - low order bits
what’s a subnet ?
  device interfaces with same subnet part of IP address
  can physically reach each other without intervening router
network consisting of 3 subnets
223.1.1.1
223.1.1.3
223.1.1.4
223.1.2.9
223.1.3.2
223.1.3.1
subnet
223.1.1.2
223.1.3.27
223.1.2.2
223.1.2.1
<number>

## Slide 16: Subnets
Network Layer
4-41
recipe
to determine the subnets, detach each interface from its host or router, creating islands of isolated networks
each isolated network is called a subnet
subnet mask: /24
223.1.1.0/24
223.1.2.0/24
223.1.3.0/24
223.1.1.1
223.1.1.3
223.1.1.4
223.1.2.9
223.1.3.2
223.1.3.1
subnet
223.1.1.2
223.1.3.27
223.1.2.2
223.1.2.1
<number>

## Slide 17: Subnets
Network Layer
4-42
how many?
Determined by subnet mask.
223.1.1.1
223.1.1.3
223.1.1.4
223.1.2.2
223.1.2.1
223.1.2.6
223.1.3.2
223.1.3.1
223.1.3.27
223.1.1.2
223.1.7.0
223.1.7.1
223.1.8.0
223.1.8.1
223.1.9.1
223.1.9.2
<number>

## Slide 18: Subnets
<number>
IP address is stored in S.Addr, D.Addr fields in IP header
Hierarchical, unlike Ethernet addresses
Consists of network and host portions
  network (prefix): same for all hosts in network
  contiguous block of IP address space
Dotted decimal notation: e.g. 128.208.2.151
<number>

## Slide 19: Subnets
Addresses are allocated in blocks called prefixes
Prefix is determined by the network portion
Has 2L addresses aligned on 2L boundary
Written:
address/length ===> e.g. 18.0.31.0/24
CT1403
<number>

## Slide 20: Subnets
CT1403
في المثال التالي، تجزئ الخانات 16 الخاصة برقم الطرفية في IP Address (Class B) إلى قسمين، القسم الأول مكون من 6 بتات للدلالة على الشبكة الجزئية والقسم الثاني مكون من 10 بتات للدلالة على الطرفية في تلك الشبكة الجزئية.
10
شبكة
طرفية
Class B
Class B
10
شبكة
طرفية
شبكة جزئية
6 bits
10 bits
<number>
reference: This slide is created by Dr. Mohammad Arafah

## Slide 21
CIDR
Classless Interdomain Routing
<number>

## Slide 22: IP addressing: CIDR
CIDR: Classless InterDomain Routing
  subnet portion of address of arbitrary length
  address format: a.b.c.d/x, where x is # bits in subnet portion of address
11001000 00010111 00010000 00000000
subnet
part
host
part
200.23.16.0/23
<number>

## Slide 23: Classless Interdomain Routing : CIDR
Generalizes the notation of subnet addressing
As within the subnet addressing, the 32-bit address is divided into two parts (net#, host # ) and has the dotted decimal form (a.b.c.d/x), where x indicates the number of bits in the first part of the address.
CIDR replaces Classful addressing, where the network portion of IP addresses were constrained to 8, 16, or 24
Classful addressing waists IP addresses
<number>

## Slide 24: Classless Interdomain Routing : CIDR
Most organizations needs more than class C but less than class B
CIDR allocates IP address blocks of variable size without regard to classes
  Example: site needs 2000 addresses
assign a block of 2048 addresses
With CIDR address lookup is more complicated
<number>

## Slide 25: CIDR Example
CT1403
مثال 6: قناع الشبكة الفرعية (Subnet Mask) هو (/30).
11111111 . 11111111 . 11111111 . 111111 00
قناع الشبكة الفرعية
ثابتة (رقم الشبكة)
متغيرة
(رقم الطرفية)
255.255.255.252 (/22)
255.255.255.252 | قناع الشبكة الفرعية (Dotted Decimal Notation)
22 - 2 = 2 طرفية | عدد الطرفيات التي تدعمها الشبكة
<number>
reference: This slide was created by Dr. Mohammad Arafah

## Slide 26
Obtaining IP Addresses
<number>

## Slide 27: IP addresses: how to get one?
Q: How does a host get IP address?
hard-coded by system administrator in a file
  Windows: control-panel->network->configuration->tcp/ip->properties
  UNIX: /etc/rc.config
More often using ===> DHCP: Dynamic Host Configuration Protocol: dynamically get address from as server
  “plug-and-play”
<number>

## Slide 28: DHCP: Dynamic Host Configuration Protocol
goal: allow host to dynamically obtain its IP address from network server when it joins network
  can renew its lease on address in use
  allows reuse of addresses (only hold address while connected/“on”)
  support for mobile users who want to join network (more shortly)
DHCP overview:
  host broadcasts “DHCP discover” msg [optional]
  DHCP server responds with “DHCP offer” msg [optional]
  host requests IP address: “DHCP request” msg
  DHCP server sends address: “DHCP ack” msg
<number>

## Slide 29: DHCP client-server scenario
223.1.1.0/24
223.1.2.0/24
223.1.3.0/24
223.1.1.1
223.1.1.3
223.1.1.4
223.1.2.9
223.1.3.2
223.1.3.1
223.1.1.2
223.1.3.27
223.1.2.2
223.1.2.1
DHCP
server
arriving DHCP
client needs
address in this
network
<number>

## Slide 30: DHCP client-server scenario
Network Layer
4-47
DHCP server: 223.1.2.5
arriving
client
DHCP discover
src : 0.0.0.0, 68
dest.: 255.255.255.255,67
yiaddr: 0.0.0.0
transaction ID: 654
DHCP offer
src: 223.1.2.5, 67
dest: 255.255.255.255, 68
yiaddrr: 223.1.2.4
transaction ID: 654
lifetime: 3600 secs
DHCP request
src: 0.0.0.0, 68
dest:: 255.255.255.255, 67
yiaddrr: 223.1.2.4
transaction ID: 655
lifetime: 3600 secs
DHCP ACK
src: 223.1.2.5, 67
dest: 255.255.255.255, 68
yiaddrr: 223.1.2.4
transaction ID: 655
lifetime: 3600 secs
<number>

## Slide 31: DHCP: more than IP addresses
Network Layer
4-48
DHCP can return more than just allocated IP address on subnet:
  address of first-hop router for client
  name and IP address of DNS sever
  network mask (indicating network versus host portion of address)
<number>

## Slide 32: DHCP: example
Network Layer
4-49
connecting laptop needs its IP address, addr of first-hop router, addr of DNS server: use DHCP
router with DHCP
server built into
router
DHCP request encapsulated in UDP, encapsulated in IP, encapsulated in 802.1 Ethernet
Ethernet frame broadcast (dest: FFFFFFFFFFFF) on LAN, received at router running DHCP server
Ethernet demuxed to IP demuxed, UDP demuxed to DHCP
168.1.1.1
DHCP
UDP
IP
Eth
Phy
DHCP
DHCP
DHCP
DHCP
DHCP
DHCP
UDP
IP
Eth
Phy
DHCP
DHCP
DHCP
DHCP
DHCP
<number>

## Slide 33: DHCP: example
Network Layer
4-50
DCP server formulates DHCP ACK containing client’s IP address, IP address of first-hop router for client, name & IP address of DNS server
encapsulation of DHCP server, frame forwarded to client, demuxing up to DHCP at client
router with DHCP
server built into
router
DHCP
DHCP
DHCP
DHCP
DHCP
UDP
IP
Eth
Phy
DHCP
DHCP
UDP
IP
Eth
Phy
DHCP
DHCP
DHCP
DHCP
client now knows its IP address, name and IP address of DSN server, IP address of its first-hop router
<number>

## Slide 34: DHCP: Wireshark output (home LAN)
Message type: Boot Reply (2)
Hardware type: Ethernet
Hardware address length: 6
Hops: 0
Transaction ID: 0x6b3a11b7
Seconds elapsed: 0
Bootp flags: 0x0000 (Unicast)
Client IP address: 192.168.1.101 (192.168.1.101)
Your (client) IP address: 0.0.0.0 (0.0.0.0)
Next server IP address: 192.168.1.1 (192.168.1.1)
Relay agent IP address: 0.0.0.0 (0.0.0.0)
Client MAC address: Wistron_23:68:8a (00:16:d3:23:68:8a)
Server host name not given
Boot file name not given
Magic cookie: (OK)
Option: (t=53,l=1) DHCP Message Type = DHCP ACK
Option: (t=54,l=4) Server Identifier = 192.168.1.1
Option: (t=1,l=4) Subnet Mask = 255.255.255.0
Option: (t=3,l=4) Router = 192.168.1.1
Option: (6) Domain Name Server
Length: 12; Value: 445747E2445749F244574092;
IP Address: 68.87.71.226;
IP Address: 68.87.73.242;
IP Address: 68.87.64.146
Option: (t=15,l=20) Domain Name = "hsd1.ma.comcast.net."
reply
Message type: Boot Request (1)
Hardware type: Ethernet
Hardware address length: 6
Hops: 0
Transaction ID: 0x6b3a11b7
Seconds elapsed: 0
Bootp flags: 0x0000 (Unicast)
Client IP address: 0.0.0.0 (0.0.0.0)
Your (client) IP address: 0.0.0.0 (0.0.0.0)
Next server IP address: 0.0.0.0 (0.0.0.0)
Relay agent IP address: 0.0.0.0 (0.0.0.0)
Client MAC address: Wistron_23:68:8a (00:16:d3:23:68:8a)
Server host name not given
Boot file name not given
Magic cookie: (OK)
Option: (t=53,l=1) DHCP Message Type = DHCP Request
Option: (61) Client identifier
Length: 7; Value: 010016D323688A;
Hardware type: Ethernet
Client MAC address: Wistron_23:68:8a (00:16:d3:23:68:8a)
Option: (t=50,l=4) Requested IP Address = 192.168.1.101
Option: (t=12,l=5) Host Name = "nomad"
Option: (55) Parameter Request List
Length: 11; Value: 010F03062C2E2F1F21F92B
1 = Subnet Mask; 15 = Domain Name
3 = Router; 6 = Domain Name Server
44 = NetBIOS over TCP/IP Name Server
……
request
<number>

## Slide 35: IP addresses: how to get one?
Q: how does network get subnet part of IP addr?
A: gets allocated portion of its provider ISP’s address space
ISP's block 11001000 00010111 00010000 00000000 200.23.16.0/20
Organization 0 11001000 00010111 00010000 00000000 200.23.16.0/23
Organization 1 11001000 00010111 00010010 00000000 200.23.18.0/23
Organization 2 11001000 00010111 00010100 00000000 200.23.20.0/23
... ….. …. ….
Organization 7 11001000 00010111 00011110 00000000 200.23.30.0/23
<number>

## Slide 36: IP addressing: the last word...
Q: how does an ISP get block of addresses?
A: ICANN: Internet Corporation for Assigned
Names and Numbers http://www.icann.org/
  allocates addresses
  manages DNS
  assigns domain names, resolves disputes
<number>

## Slide 37: Hierarchical addressing: route aggregation
“Send me anything
with addresses
beginning
200.23.16.0/20”
200.23.16.0/23
200.23.18.0/23
200.23.30.0/23
Fly-By-Night-ISP
Organization 0
Organization 7
Internet
Organization 1
ISPs-R-Us
“Send me anything
with addresses
beginning
199.31.0.0/16”
200.23.20.0/23
Organization 2
.
.
.
.
.
.
hierarchical addressing allows efficient advertisement of routing
information:
<number>

## Slide 38: Hierarchical addressing: more specific routes
ISPs-R-Us has a more specific route to Organization 1
“Send me anything
with addresses
beginning
200.23.16.0/20”
200.23.16.0/23
200.23.18.0/23
200.23.30.0/23
Fly-By-Night-ISP
Organization 0
Organization 7
Internet
Organization 1
ISPs-R-Us
“Send me anything
with addresses
beginning 199.31.0.0/16
or 200.23.18.0/23”
200.23.20.0/23
Organization 2
.
.
.
.
.
.
<number>