## Slide 1: CT1303 LAN
Rehab AlFallaj

## Slide 2: Lan devices
Network:
  Nodes:
    Service units: PC
    Interface processing Modules: it doesn’t generate data, but just it process it and do specific task to it: communication, connect, modulate, edit, justify signals etc …

## Slide 3: LAN devices: interface processing Modules
Network Interface Card (NIC):
  is to provide a physical link to a computer network: connects PCs, Workstations or any network device to the network.
  Flow control
  Control the interface between devices and transmission media

## Slide 4: LAN devices: interface processing Modules
Number of ports based on the type of media.

## Slide 5: LAN devices: interface processing Modules
Types of NIC based on the bus used:
  Industry Standard Architecture ISA bus:
    8 bits
  Extended Industry Standard Architecture EISA bus:
    16 bits
  Peripheral Component Interconnect PCI bus:
    32 bits
Logical Link Control
Medium Access Control

## Slide 6: LAN devices: interface processing Modules
Each NIC has unique serial number Physical Address. (48bit)

## Slide 7: LAN devices: interface processing Modules
Repeater:
  To repeat and extend the distance a signal can travel by regenerating the signal.
  Extends network area.
  Improves the signal.
  Works in physical layer.
  It does NOT see the packet data.

## Slide 8: LAN devices: interface processing Modules
HUB:
  A central device in a star topology that provides a common connection among the nodes.
  Broadcast the signal to all the ports\PCs connected to.
  Called: Multiport Repeater or Multi Access Unit.
  Works on physical layer.

## Slide 9: LAN devices: interface processing Modules
  Cheap.
  Economical way to build a cheap network.
  Builds a simple network.
  Makes network maintenance easy.
Active Hub:
  Regenerating and amplifying the signal before resending it to all the ports.
Passive Hub:
  Only resending the signal to the ports.

## Slide 10: LAN devices: interface processing Modules
Stand-alone Hub:
  single products with a number of ports, used to connect number of devices.
  least expensive type of hub.
  best suited for small, independent workgroups, departments, or offices.
  fewer than 12 users per LAN.
Stacked Hub:
  Several of hubs are "stacked" or connected together with short lengths of special cable.
  Ideal for who want to start with a minimal investment, but realize that the LAN will grow.

## Slide 11: LAN devices: interface processing Modules
Modular Hub:
  Like card cage with multiple card slots, each of which accepts a communications card, or module. Each module acts like a standalone hub
  Expandable by adding more cards.
  usually always have a management option.
  Modules supporting different types of network cabling, like coaxial
  For a medium to large sized company.

## Slide 12: LAN devices: interface processing Modules
  Easy maintenance for the network and cables.
  Ensure continuity of network operation.
Disadvantages:
  If hub disabled or crashed, all the network will be stopped.
  Long cables needed to link devices to hubs.

## Slide 13: LAN devices: interface processing Modules
Switch:
  Send the frame to the destination device only based on the physical address.
  Called: Intelligent Hub.
  Works in Data Link layer.
  Decrees the traffic on the network.
  Nodes connected to a switch can expect an immediate 40%-60% increase in performance

## Slide 14: LAN devices: interface processing Modules
Bridge:
  linking different LANs or LAN segments together.
  simpler and less expensive.
  Works in data link layer.
  Have a local Routing table.
  Makes a simple do/don't decision on which packets to send across two segments they connect.
  Filtering is done based on the destination address of the packet.
  If a packet's destination is a station on the same segment where it originated, it is not forwarded, otherwise, it forwards it to the proper segment.

## Slide 15: LAN devices: interface processing Modules
  Bridge can link two different networks or segments with different protocols.
  Switch can link devices in only one same network and same protocol.
  Extend network distance.
  Enable two different network to be linked.
  Link different cables and transmission media.
  Divide the network to segments or parts to decrees the traffic/collisions in each segment\part.

## Slide 16: LAN devices: interface processing Modules
Local bridge:
  Links two close networks.
Remote bridge:
  Link networks far to each other, or not close, using some linking device: Modem, phone cabling.

## Slide 17: LAN devices: interface processing Modules

## Slide 18: LAN devices: interface processing Modules
How bridge works:
  Routing protocol.
  destination address.
  Routing table.

## Slide 19: LAN devices: interface processing Modules
To disallow looping:
  Spanning Tree algorithm is used.
  Logical tree of bridges and devices.
  Regardless of the physical topology of the network ( star, ring) logical tree will force the logical tree algorithm to find the destination devices without looping.
  Bridges always sends data of its devices to update their routing table continuously.

## Slide 20: LAN devices: interface processing Modules
Router:
  Links Remote LANs cross Wide Area Network WAN or Internet.
  complex and more expensive than bridges.
  Works in Network layer.
  use information within each packet to route it from one LAN to another.
  Routers communicate with each other and share information that allows them to determine the best route through a complex network of many LANs.

## Slide 21: LAN devices: interface processing Modules
  Internetworking protocols are needed to allow Router to communicate with each other.
  Routing table based on Routing algorithms.
  Uses IP address
    Read destination address in packet header.
    Choose best routing path.
    Send to packets to destination or next router.
  Routing Algorithms are calculated by network engineers based on :
    Shortest path.
    Fastest path.
    Path with least traffic.

## Slide 22: LAN devices: interface processing Modules
  Routing tables can be Static or dynamic.
  Router uses Global Address to link devices to another device in WAN.
data link layer data: Frames
  physical address is used.
Network layer data: Packet
  Global address is used.

## Slide 23: LAN devices: interface processing Modules

## Slide 24: LAN devices: Service devices.
Devices that generate data.
Servers:
  Fast.
  Processing capabilities.
  Storage; files, Software, databases, network O.S
  Manages and control network.
  Interacts with other devices for data, services.
  Special operating systems that support network management: window NT, window 2000, window server 2008, windows server 2013, windows administrator.

## Slide 25: LAN devices: Service devices.
Printer servers.
  Manage printer attached to networks
File servers.
  Store and manage files and folder.
Application Server:
  Store and control applications used in networks.
Peripheral server:
  Manage any types of attached devices; disk storage.
Communication server:
  Manage any communication devices: modems, or connecting devices with outer devices using phone networking.

## Slide 26: LAN devices: Service devices.

## Slide 27: LAN devices: Service devices.
Client Station:
  PC, Terminal, workstation.
  Less capabilities than servers.
  Usually clients are much more than servers.
  Usually client for one user.
  Connect to server to do some tasks.
  Client can be any operating system.