## Slide 1: CT1303 LAN
Rehab AlFallaj

## Slide 2: Network standards
Standards determine:
  Techniques used in the networks.
  Its protocols.
  Network specifications and features

## Slide 3: LAN standards
Ethernet LAN standards:
  1982 by Xerox, Digital, Intel
  Use CSMA/CD protocol
  Transmission rate: 1-10 Mbps
  Standards include:
    Coaxial cable.
    Bus topology.
Number of projects and standards have been conducted by many associations of IEEE called project IEEE-802 for LAN standards.

## Slide 4: LAN standards: IEEE LAN 802

## Slide 5: LAN IEEE-802
LAN IEEE-802.1: Concerned with:
  Network Layer: internetworking among 802 LANs, MANs and WANs.
LAN IEEE-802.2: Concerned with:
  Logical Link Control LLC sub-layer
    DLL in IEEE standards : MAC+LLC

## Slide 6: LAN IEEE 802.2

## Slide 7: LAN IEEE 802
Based on Ethernet standards
IEEE 802.3: concerned with:
  CSMA/CD protocol. ~ similar to Ethernet
  Differ to Ethernet: not only Coaxial Cables used + not only Bus topology used: Ring …etc
  Transmission rate: more than 10Mbps, 100 Mbps Fast Ethernet and 1000 Mbps Giga Ethernet.
It has numbers of sub-standards related to Ethernet, Fast Ethernet LANs: type of transmission media, network length, transmission media, type of signal … etc

## Slide 8: LAN IEEE 802.3

## Slide 9: LAN IEEE 802.3
802.3 standards name contain 3 parts:
  1st part: Transmission rate:
    10 Mbps , 100 Mbps … etc
  2nd part: transmission type and signal:
    Base: base band: digital signal
    Broad: Broadband: analog
  3rd part: maximum network length or type of transmission media.
    5 (10 Base 5): 500m
    T (10 Base T): Twisted pair
    F (100 Base FX): Fiber Optics.

## Slide 10: LAN IEEE 802.3

## Slide 11: LAN IEEE 802
Giga Ethernet:
  Transmission rate: 1 Gbps: 1000Mbps
  name: 802.3Z
  Has several types based on the transmission media used:

## Slide 12: Ethernet LAN 802.3 technologies
Technologies used in he previous standards includes:
  Data Frames.
  MAC protocol type.
  type of transmission media.
  coding techniques.
  network topology.

## Slide 13: Data Frame for Ethernet and 802.3 networks
All 802.3 networks and Ethernet networks use MAC protocol of type CSMA/CD and similar type of data frame.
802.3 standards use frame length: 1518 byte ( preamble and CRC is not included)
Minimum frame length: 64 byte ( length enough to detect collisions if occurred)

## Slide 14: 802.3 data frame

## Slide 15: 802.3 data frame
Pre-amble حقل التزامن :
  7 byte.
  Used for synchronization.
Start Frame Delimiter (SFD)حقل البدء :
  1 byte.
Destination address عنوان المرسل إليه :
  6 byte ~ can be minimized to 2 byte.
  Physical address.
Source address عنوان المرسل :
  6 byte ~ can be minimized to 2 byte.
  Physical address.
Frame length fieldحقل طول الاطار :
  2 byte ~ 802.3 networks
  Type of protocol of the upper layer ~ Ethernet.

## Slide 16: 802.3 data frame
LLC data حقل بيانات الطبقة الاعلى:
  1500 byte – 64 byte length, includes:
Error Detection field (Cyclic Redundancy Check CRC): حقل اكتشاف الاخطاء
  4 byte.

## Slide 17: IEEE LAN standards
Ethernet LAN (by Xerox):
  Topology: Bus
  Transmission Media: Thick Coaxial Cable.
  Signal: Digital.
  Encoding Technique: Manchester.
  Devices used:
    Transceiver:
      To manage the access to the channel
      Has MAC protocols (CSMA/CD)
      External device ( out of the PC)
      Connect the coaxial cable.

## Slide 18: Ethernet LAN
    Transceiver Cable:
      DB-15 connector ( similar to AUI).
      Maximum length 50 m
      Consists of 5 pairs of UTP; 2 pairs for sending and receiving data, 2 pairs for controlling the data, 1 for voltage and electricity.
    Controller:
      To send controlling commands
      Has Logical Link Control LLC protocol mechanism.
      It is inside PC.

## Slide 19: Ethernet LAN

## Slide 20: 10 Base 5 standards
Maximum network length: 500 m
Transmission media: Thick Coaxial RG-8
Topology: bus
Signal: digital, Manchester encoding
Devices used:
  Medium Attached Unit MAU ~ Transceiver
  Attached Unit Interface AUI ~ Transceiver Cable
  Network Interface Card NIC:LLC protocols mechanisms , inside PCs

## Slide 21: 10 Base 5 standards

## Slide 22: 10 Base 2 standards
Transceiver or MAU is embedded into NIC to control and connecting to channel.
Transmission media: thin Coaxial RG-58
Network length: 185m , repeaters can be used to extend network length.
Topology: bus
Signal: digital, Manchester encoding.
Devices used: cables, BNC-T , BNC connectors, NICs

## Slide 23: 10 Broad 36 standards
Signal: analog NRZ encoding.
Topology: bus, tree
Network length: 1800 m, 3600m with repeaters.
100 devices can be connected in 1 cable
Pair of cables: sending, receiving cable, or 1 cable and dividing frequency bandwidth to sending and receiving parts.
TV. Cables can be used.
Network can be used for T.V broadcast + LAN
devices: used:
  Head End: in top of network to transmit signals from sending cable to receiving cable
  Modems: module signals .
  NIC: CSMA/CD

## Slide 24: 10 Broad 36 standards

## Slide 25: 10 Base T standards
2 pairs of UTP- CAT3
100 m without repeaters.
Hub used to connect devices.
Star topology
RG-45
Hub can have AUI,BNC ports for coaxial cables.
Signal: digital, Manchester encoding.
Maximum hubs can be used to connect 2 PCs are 4 hubs + 5 cables.

## Slide 26: 10 Base T standards
NIC is inside devices; RG-45 ports.
Twisted pair cables.
NIC is responsible for sensing + transmission + collision detection.

## Slide 27: 10 Base FP standards
Pair of Fiber Optics.
Star topology.
1 km for each part of network.
Analog signal.
Encoding the digital signal by Manchester to light signal turning on and off depends on the transmitted bit (0,1).
33 devices can be connected to each part of network.

## Slide 28: Fast Ethernet standards
100 Base T4
100 Base TX
100 Base FX

## Slide 29: Fast Ethernet: 100 Base T4
4 pairs of twisted pairs: 3 pairs for sending and receiving data, 1 pair for detecting collisions.
Transmission rate on each pair: 100/3=33.3 Mbps
Digital signal, NRZ ~ 8B6T
8 bit\6T (Ternary):
  Each 8 bits transformed to a symbol of 6 symbols (0,+,-)
Maximum cable length: 100m
Star topology
Maximum network length: 200m
Devices: same as 10 Base T : hubs, NICs

## Slide 30: Fast Ethernet: 100 base TX
Devices used: hubs, NIC
2 pairs of twisted pairs: 1 pair for sending, 1 for receiving data.
Maximum cable length: 100m
Maximum network length: 200m
Transmission media: UTP- Cat5 or STP
Digital signal, NTZ-I ~ 4B/5B ( to better detection errors, synchronization)

## Slide 31: Fast Ethernet : 100 Base FX
Ethernet + Fiber Optics
Light signal for digital data of type NRZ-I ~ 4B/5B
Pairs of Fiber Optics; 1 sending, 1 receiving
Maximum cable length: 100m.
Maximum network length: 400m

## Slide 32: Giga Ethernet standards
Transmission rate: 1Gbps~1000Mbps.
CSMA/CD as a MAC protocol.
Star, tree topology.
Hub, switch to connect devices and servers.
Data frame is similar to Ethernet data frame but:
  Minimum frame length: 4096 bit NOT 512 bit(64byte)
Digital signals; 8B/10B

## Slide 33: Giga Ethernet standards

## Slide 34: Giga Ethernet standards
1000 BASE SX:
  Pair of Multimode Fiber Optics.
  Maximum cable length: 275m ~ 62.5mm diameter, 500m ~ 50mm diameter.
  Light signal.
1000 BASE CX:
  STP.
  Maximum cable length : 25m.
1000 BASE T:
  4 pairs of UTP-Cat5, 100m

## Slide 35: Token passing standards
IEEE 802.5 standards has been developed to specify some standards for Ring Topology networks that used Token Passing Protocol as its main MAC protocol.
It can be used also in Star topology network that has MAU Medium Access Unit to connect devices, but logically works as Ring design by passing Token.
It differs that Ethernet with the data frame fields and its contents

## Slide 36: Token passing standards

## Slide 37: Token passing standards
Starting Delimiter SD:
  Jk0jk000( j,k) is used to define starting of frame.
Access Control AC:
  Manage accessing channel among devices and nodes.
Frame Control FC:
  To exchange commands to control channel access.
Destination, Sender Address.
  48 bit
  Physical address, by manifacturer.

## Slide 38: Token passing standards
Data field:
  Data, control commands.
Frame Check Sequence FCS:
  Using CRC as an error detection method.
End Delimiter ED:
  Bits to till receiver that no data are coming next.
Frame Status:
  If received or not.

## Slide 39: Token passing standards