## Slide 1: net301
LECTURE 10

## Slide 2: Network standards
Standards determine:
  Techniques used in the networks.
  Its protocols.
  Network specifications and features

## Slide 3: LAN standards
Ethernet LAN standards:
  1982 by Xerox, Digital, Intel
  Use CSMA/CD protocol
  Transmission rate: 1-10 Mbps
  Standards include:
    Coaxial cable.
    Bus topology.
Number of projects and standards have been conducted by many associations of IEEE called project IEEE-802 for LAN standards.

## Slide 4: LAN standards: IEEE LAN 802

## Slide 5: LAN IEEE-802
LAN IEEE-802.1: Concerned with:
  Network Layer: inter networking among 802 LANs, MANs and WANs.
LAN IEEE-802.2: Concerned with:
  Logical Link Control LLC sub-layer
    DLL in IEEE standards : MAC+LLC

## Slide 6: LAN IEEE 802.2

## Slide 7: LAN IEEE 802
Based on Ethernet standards
IEEE 802.3: concerned with:
  CSMA/CD protocol. ~ similar to Ethernet
  Differ to Ethernet: not only Coaxial Cables used + not only Bus topology used: Ring …etc
  Transmission rate: more than 10Mbps, 100 Mbps Fast Ethernet and 1000 Mbps Giga Ethernet.
It has numbers of sub-standards related to Ethernet, Fast Ethernet LANs: type of transmission media, network length, transmission media, type of signal … etc

## Slide 8: LAN IEEE 802.3

## Slide 9: LAN IEEE 802.3
802.3 standards name contain 3 parts:
  1st part: Transmission rate:
    10 Mbps , 100 Mbps … etc
  2nd part: transmission type and signal:
    Base: base band: digital signal
    Broad: Broadband: analog
  3rd part: maximum network length or type of transmission media.
    5 (10 Base 5): 500m
    T (10 Base T): Twisted pair
    F (100 Base FX): Fiber Optics.

## Slide 10: LAN IEEE 802.3

## Slide 11: LAN IEEE 802
Giga Ethernet:
  Transmission rate: 1 Gbps: 1000Mbps
  name: 802.3Z
  Has several types based on the transmission media used:

## Slide 12: Ethernet LAN 802.3 technologies
Technologies used in the previous standards includes:
  Data Frames.
  MAC protocol type.
  type of transmission media.
  coding techniques.
  network topology.

## Slide 13: Data Frame for Ethernet and 802.3 networks
All 802.3 networks and Ethernet networks use MAC protocol of type CSMA/CD and similar type of data frame.
802.3 standards use frame length: 1518 byte ( preamble and CRC is not included)
Minimum frame length: 64 byte ( length enough to detect collisions if occurred)

## Slide 14: 802.3 data frame

## Slide 15: 802.3 data frame
Pre-amble حقل التزامن :
  7 byte.
  Used for synchronization.
Start Frame Delimiter (SFD)حقل البدء :
  1 byte.
Destination address عنوان المرسل إليه :
  6 byte ~ can be minimized to 2 byte.
  Physical address.
Source address عنوان المرسل :
  6 byte ~ can be minimized to 2 byte.
  Physical address.
Frame length fieldحقل طول الاطار :
  2 byte ~ 802.3 networks
  Type of protocol of the upper layer ~ Ethernet.

## Slide 16: 802.3 data frame
LLC data حقل بيانات الطبقة الاعلى:
  1500 byte – 64 byte length, includes:
Error Detection field (Cyclic Redundancy Check CRC): حقل اكتشاف الاخطاء
  4 byte.