## Slide 1: net301
LECTURE 10

## Slide 2: Network Performance
measures of service quality of a telecommunications product as seen by the customer
Can I measure everything?
    Impact on devices (measurements and measuring)
    Balance between amount of information and time to get it

## Slide 3: Metrics
Network performance metrics
  Channel capacity, effective
  Channel utilization
  Delay
  Packet loss and errors

## Slide 4: Metrics
System performance metrics
    Availability
    Memory, CPU Utilization, load, I/O wait, etc.
Service performance metrics
    Wait time / Delay
    Availability
    How can I justify maintaining the service?
    Who is using it? How often?
    Economic value? Other value?

## Slide 5: Performance measures
Bandwidth
commonly measured in bits/second is the maximum rate that information can be transferred
Throughput
is the actual rate that information is transferred

## Slide 6: Performance measures
Latency
the delay between the sender and the receiver decoding it, this is mainly a function of the signals travel time, and processing time at any nodes the information traverses
Jitter
variation in the time of arrival at the receiver of the information

## Slide 7: Performance measures
Error rate
the number of corrupted bits expressed as a percentage or fraction of the total sent

## Slide 8: End-to-end Delay
The time required to transmit a packet along its entire path
  Created by an application, handed over to the OS, passed to a network card (NIC), encoded, transmitted over a physical medium (copper, fibre, air), received by an intermediate device (switch, router), analyzed, retransmitted over another medium, etc.
  The most common measurement uses ping for total round-trip-time (RTT).

## Slide 9: Types of Delay
Causes of end-to-end delay:
    Processor delays
    Buffer delays
    Transmission delays
    Propagation delays

## Slide 10: Processing Delay
Required time to analyze a packet header and decide where to send the packet (eg. a routing decision)
This can include error verification

## Slide 11: Queuing Delay
The time a packet is enqueued until it is transmitted
The number of packets waiting in the queue will depend on traffic intensity and of the type of traffic
Router queue algorithms try to adapt delays to specific preferences, or impose equal delay on all traffic.

## Slide 12: Transmission Delay
The time required to push all the bits in a packet on the transmission medium in use
For N=Number of bits, S=Size of packet, d=delay
d = S/N

## Slide 13: Propagation Delay
Once a bit is 'pushed' on to the transmission medium, the time required for the bit to propagate to the end of its physical trajectory
The velocity of propagation of the circuit depends mainly on the actual distance of the physical circuit
In the majority of cases this is close to the speed of light.
For d = distance, s = propagation velocity
PD = d/s

## Slide 14: Packet Loss
Occurs due to the fact that buffers are not infinite in size
When a packet arrives to a buffer that is full the packet is discarded.
Packet loss, if it must be corrected, is resolved at higher levels in the network stack (transport or application layers)