## Slide 1: net301
LECTURE 11

## Slide 2: IEEE LAN standards
Ethernet LAN (by Xerox):
  Topology: Bus
  Transmission Media: Thick Coaxial Cable.
  Signal: Digital.
  Encoding Technique: Manchester.
  Devices used:
    Transceiver:
      To manage the access to the channel
      Has MAC protocols (CSMA/CD)
      External device ( out of the PC)
      Connect the coaxial cable.

## Slide 3: Ethernet LAN
    Transceiver Cable:
      DB-15 connector .
      Maximum length 50 m
      Consists of 5 pairs of UTP; 2 pairs for sending and receiving data, 2 pairs for controlling the data, 1 for voltage and electricity.
    Controller:
      To send controlling commands
      Has Logical Link Control LLC protocol mechanism.
      It is inside PC.

## Slide 4: Ethernet LAN

## Slide 5: 10 Base 5 standards
Maximum network length: 500 m
Transmission media: Thick Coaxial RG-8
Topology: bus
Signal: digital, Manchester encoding
Devices used:
  Medium Attached Unit MAU ~ Transceiver
  Attached Unit Interface AUI ~ Transceiver Cable
  Network Interface Card NIC:LLC protocols mechanisms , inside PCs

## Slide 6: 10 Base 2 standards
Transceiver or MAU is embedded into NIC to control and connecting to channel.
Transmission media: thin Coaxial RG-58
Network length: 185m , repeaters can be used to extend network length.
Topology: bus
Signal: digital, Manchester encoding.
Devices used: cables, BNC-T , BNC connectors, NICs

## Slide 7: 10 Base 2 standards

## Slide 8: 10 Broad 36 standards
Signal: analog NRZ encoding.
Topology: bus, tree
Network length: 1800 m, 3600m with repeaters.
100 devices can be connected in 1 cable
Pair of cables: sending, receiving cable, or 1 cable and dividing frequency bandwidth to sending and receiving parts.
TV. Cables can be used.
Network can be used for T.V broadcast + LAN
devices: used:
  Head End: in top of network to transmit signals from sending cable to receiving cable
  Modems: module signals .
  NIC: CSMA/CD

## Slide 9: 10 Broad 36 standards

## Slide 10: 10 Base T standards
2 pairs of UTP- CAT3
100 m without repeaters.
Hub used to connect devices.
Star topology
RG-45
Hub can have AUI, BNC ports for coaxial cables.
Signal: digital, Manchester encoding.
Maximum hubs can be used to connect 2 PCs are 4 hubs + 5 cables.

## Slide 11: 10 Base T standards
NIC is inside devices; RG-45 ports.
Twisted pair cables.
NIC is responsible for sensing + transmission + collision detection.

## Slide 12: 10 Base FP standards
Pair of Fiber Optics.
Star topology.
1 km for each part of network.
Analog signal.
Encoding the digital signal by Manchester to light signal turning on and off depends on the transmitted bit (0,1).
33 devices can be connected to each part of network.

## Slide 13: Fast Ethernet standards
100 Base T4
100 Base TX
100 Base FX

## Slide 14: Fast Ethernet: 100 Base T4
4 pairs of twisted pairs: 3 pairs for sending and receiving data, 1 pair for detecting collisions.
Transmission rate on each pair: 100/3=33.3 Mbps
Digital signal, NRZ ~ 8B6T
8 bit\6T (Ternary):
  Each 8 bits transformed to a symbol of 6 symbols (0,+,-)
Maximum cable length: 100m
Star topology
Maximum network length: 200m
Devices: same as 10 Base T : hubs, NICs

## Slide 15: Fast Ethernet: 100 base TX
Devices used: hubs, NIC
2 pairs of twisted pairs: 1 pair for sending, 1 for receiving data.
Maximum cable length: 100m
Maximum network length: 200m
Transmission media: UTP- Cat5 or STP
Digital signal, NTZ-I ~ 4B/5B ( to better detection errors, synchronization)

## Slide 16: Fast Ethernet : 100 Base FX
Ethernet + Fiber Optics
Light signal for digital data of type NRZ-I ~ 4B/5B
Pairs of Fiber Optics; 1 sending, 1 receiving
Maximum cable length: 100m.
Maximum network length: 400m

## Slide 17: Giga Ethernet standards
Transmission rate: 1Gbps~1000Mbps.
CSMA/CD as a MAC protocol.
Star, tree topology.
Hub, switch to connect devices and servers.
Data frame is similar to Ethernet data frame but:
  Minimum frame length: 4096 bit NOT 512 bit(64byte)
Digital signals; 8B/10B

## Slide 18: Giga Ethernet standards

## Slide 19: Giga Ethernet standards
1000 BASE SX:
  Pair of Multimode Fiber Optics.
  Maximum cable length: 275m ~ 62.5mm diameter, 500m ~ 50mm diameter.
  Light signal.
1000 BASE CX:
  Maximum cable length : 25m.
1000 BASE T:
  4 pairs of UTP-Cat5, 100m

## Slide 20: Token passing standards
IEEE 802.5 standards has been developed to specify some standards for Ring Topology networks that used Token Passing Protocol as its main MAC protocol.
It can be used also in Star topology network that has MAU Medium Access Unit to connect devices, but logically works as Ring design by passing Token.
It differs that Ethernet with the data frame fields and its contents

## Slide 21: Token passing standards

## Slide 22: Token passing standards
Starting Delimiter SD:
  Jk0jk000( j,k) is used to define starting of frame.
Access Control AC:
  Manage accessing channel among devices and nodes.
Frame Control FC:
  To exchange commands to control channel access.
Destination, Sender Address.
  48 bit
  Physical address, by manifacturer.

## Slide 23: Token passing standards
Data field:
  Data, control commands.
Frame Check Sequence FCS:
  Using CRC as an error detection method.
End Delimiter ED:
  Bits to till receiver that no data are coming next.
Frame Status:
  If received or not.