## Slide 1: Net 301
LECTURE14

## Slide 2: How To Set Up A Secure Local Network
  Step 1: Identify Your Networking Needs
This is a very important step.the key considerations are:
  How many wired Ethernet ports, if any, will you need?
  Where will these Ethernet ports need to be located? (In other words, where will the PCs and other equipment that will be plugged into these Ethernet ports be located?)
  Where will the router and high-speed modems be located?
  Answering these questions will help you understand what types of equipment you need, as well as how much cable you’ll need.

## Slide 3: How To Set Up A Secure Local Network
Step 2: Determine Where To Put Your Equipment
Before you begin any installation, commit to the location for each piece of equipment in your network. This is critical if you’re going to run a cable beneath drywall or over a ceiling, because you won’t be able to change the cable lengths if something goes wrong.

## Slide 4: How To Set Up A Secure Local Network
Step 3: Gather Your Tools And Supplies
  Ethernet Cable..
  Cable Connectors..
  Crimper..
  Cable/DSL Modem.
  Wired/Wi-Fi Router
  Ethernet Hub

## Slide 5: How To Set Up A Secure Local Network
Step 4: Run The Cables
In this step, we’ll create the “cable runs” that will establish wired connections between the Ethernet ports on the ground floor and the router and cable modem upstairs.

## Slide 6: How To Set Up A Secure Local Network
Step 4: Run The Cables
Run cable from the router and cable/DSL modem location to the area where each Ethernet port will be located.
As you run the cable to these locations, make sure you temporarily affix the cable to the wall or floor so that you have a realistic idea of how much cable you’ll need. Also: Leave yourself five or 10 extra feet at the end of the cable, just in case.

## Slide 7: How To Set Up A Secure Local Network
Step 5: Crimp The Cables
Step 6: Connect All The Cables Together
Step 7: Test Your Network Connection
Step 8: Set Up Your Router

## Slide 8: Applications
Applications on a LAN can range from word processing to data base management systems.
The most universally used application is E-mail. An important security note is that on some systems it is also possible to restrict mail users from attaching files as a part of an antivirus program.

## Slide 9: Applications
Many application systems have their own set of security features, in addition to the protection provided by the network operating system.
Data base management systems, in particular, have comprehensive security controls built in to limit access to authorized users.

## Slide 10: Access Control Mechanisms
Network operating systems have access control mechanisms that are crucial for LAN security.
For example, access controls can limit:
  who can log on,
  what resources will be available,
  what each user can do with these resources,
  and when and from where access is available.
Management, LAN, security, and key user personnel should cooperate closely to implement access controls.

## Slide 11: THREATS TO LAN SECURITY
People Threats.. Costly
System administration error
Software/programming error (bugs)
Unauthorized use
Modification of data
Theft of computer assets
Hardware failure ( or any physical )

## Slide 12
http://www.acsa-admin.org/secshelf/book001/16.pdf