## Slide 1: Lecture 2: Internet Structure & Internetworking
By Dr. Najla Al-Nabhan edited by Maysoon Al Duwais
Introduction
1-<number>

## Slide 2: Outlines
Introduction
  Internet Infrastructure
  Packet-switching vs. circuit-switching
  delay, loss, throughput in networks
  protocol layers, service models
1-<number>
Notes: <number>

## Slide 3: What’s the Internet
1: Introduction
<number>
backbone
ISPs
regional
ISPs
local ISPs
enterprise
campus, ...
end systems
hosts, servers
pdas, mobiles

## Slide 4: Internet
<number>
<number>
  Internet: loosely hierarchical “network of networks”
Major Components: Hosts, Routers, Communication links
Protocols: for sending, receiving of msgs
  e.g., TCP, IP, HTTP, FTP, PPP
Internet standards
  RFC: Request for comments
  IETF: Internet Engineering Task Force
local ISP
company
network
regional ISP
router
workstation
server
mobile
Notes: <number>

## Slide 5: Internet: Three Components
<number>
<number>
End systems (hosts): millions of connected computing devices executing network applications
Routers: forwarding packets (chunks of data)
Communication links:
Connecting hosts and routers
  fiber, copper, radio, satellite
  transmission rate = bandwidth
local ISP
company
network
regional ISP
router
workstation
server
mobile
Notes: <number>

## Slide 6: Internet Service
<number>
<number>
Communication infrastructure enables distributed applications:
  Web, email, games, e-commerce, file sharing
Communication services provided to applications:
  Connectionless unreliable
  connection-oriented reliable
Notes: <number>

## Slide 7: Internet structure: network of networks
<number>
roughly hierarchical
“tier-1” ISPs
  National/international coverage
  Top of the Internet hierarchy
  Full peer-peer connections between tier-1 providers
  Has no upstream provider of its own
  (e.g., UUNet, BBN/Genuity, Sprint, AT&T),
Tier 1 ISP
Tier 1 ISP
Tier 1 ISP
Tier-1 providers interconnect (peer) privately
NAP
Tier-1 providers also interconnect at public network access points (NAPs)
Notes: <number>

## Slide 8: Internet structure: network of networks
<number>
<number>
“Tier-2” ISPs: smaller (often regional) ISPs
  Connect to one or more tier-1 ISPs, possibly other tier-2 ISPs
  Provide transit service to downstream customers
  … but, need at least one provider of their own
  Typically have national or regional scope
  E.g., Minnesota Regional Network
Tier 1 ISP
Tier 1 ISP
Tier 1 ISP
NAP
Tier-2 ISP
Tier-2 ISP
Tier-2 ISP
Tier-2 ISP
Tier-2 ISP
Tier-2 ISP pays tier-1 ISP for connectivity to rest of Internet
tier-2 ISP is customer of
tier-1 provider
Tier-2 ISPs also peer privately with each other, interconnect at NAP
Notes: <number>

## Slide 9: Internet structure: network of networks
<number>
<number>
“Tier-3” ISPs and local ISPs
  last hop (“access”) network (closest to end systems)
Tier 1 ISP
Tier 1 ISP
Tier 1 ISP
NAP
Tier-2 ISP
Tier-2 ISP
Tier-2 ISP
Tier-2 ISP
Tier-2 ISP
local
ISP
local
ISP
local
ISP
local
ISP
local
ISP
Tier 3
ISP
local
ISP
local
ISP
local
ISP
Local and tier- 3 ISPs are customers of
higher tier ISPs
connecting them to rest of Internet
Notes: <number>

## Slide 10: Internet structure: network of networks
<number>
<number>
a packet passes through many networks!
Tier 1 ISP
Tier 1 ISP
Tier 1 ISP
NAP
Tier-2 ISP
Tier-2 ISP
Tier-2 ISP
Tier-2 ISP
Tier-2 ISP
local
ISP
local
ISP
local
ISP
local
ISP
local
ISP
Tier 3
ISP
local
ISP
local
ISP
local
ISP
Notes: <number>

## Slide 11: A closer look at network structure:
Introduction
network edge:
  hosts: clients and servers
  servers often in data centers
access networks, physical media: wired, wireless communication links
network core:
  interconnected routers
  network of networks
mobile network
global ISP
regional ISP
home
network
institutional
network
1-<number>
Notes: <number>

## Slide 12
Introduction
Access net: home network
to/from headend or central office
cable or DSL modem
router, firewall, NAT
wired Ethernet (100 Mbps)
wireless access
point (54 Mbps)
wireless
devices
often combined
in single box
1-<number>
Notes: <number>

## Slide 13: Enterprise access networks (Ethernet)
Introduction
typically used in companies, universities, etc
  10 Mbps, 100Mbps, 1Gbps, 10Gbps transmission rates
  today, end systems typically connect into Ethernet switch
Ethernet
switch
institutional mail,
web servers
institutional router
institutional link to
ISP (Internet)
1-<number>

## Slide 14: Host: sends packets of data
host sending function:
takes application message
breaks into smaller chunks, known as packets, of length L bits
transmits packet into access network at transmission rate R
R: link transmission rate
host
1
2
two packets,
L bits each
packet
transmission
delay
time needed to
transmit L-bit
packet into link
L (bits)
R (bits/sec)
=
=
1-<number>

## Slide 15: Packet-switching
Introduction
mesh of interconnected routers
packet-switching: hosts break application-layer messages into packets
  forward packets from one router to the next, across links on path from source to destination
  each packet transmitted at full link capacity
1-<number>
Notes: <number>

## Slide 16: Packet-switching: store-and-forward
Introduction
takes L/R seconds to transmit (push out) L-bit packet into link at R bps
store and forward: entire packet must arrive at router before it can be transmitted on next link
more on delay shortly …
1-<number>
source
R bps
destination
1
2
3
L bits
per packet
R bps
end-end delay = 2L/R (assuming zero propagation delay)
Notes: <number>

## Slide 17: Packet Switching: queueing delay, loss
Introduction
A
B
C
R = 100 Mb/s
R = 1.5 Mb/s
D
E
queue of packets
waiting for output link
1-<number>
queuing and loss:
If arrival rate (in bits) to link exceeds transmission rate of link for a period of time:
  packets will queue, wait to be transmitted on link
  packets can be dropped (lost) if memory (buffer) fills up
Notes: <number>

## Slide 18: Two key network-core functions
Network Layer
4-<number>
forwarding: move packets from router’s input to appropriate router output
routing: determines source-destination route taken by packets
  routing algorithms
routing algorithm
local forwarding table
header value
output link
0100
0101
0111
1001
3
2
2
1
1
2
3
0111
dest address in arriving
packet’s header

## Slide 19: Alternative core: circuit switching
Introduction
end-end resources allocated to, reserved for “call” between source & dest:
In diagram, each link has four circuits.
  call gets 2nd circuit in top link and 1st circuit in right link.
dedicated resources: no sharing
  circuit-like (guaranteed) performance
circuit segment idle if not used by call (no sharing)
Commonly used in traditional telephone networks
1-<number>
Notes: <number>

## Slide 20: Circuit switching: FDM versus TDM
Introduction
FDM
frequency
time
TDM
frequency
time
4 users
Example:
1-<number>
Notes: <number>
Two simple multiple access control techniques.
Each mobile’s share of the bandwidth is divided into portions for the uplink and the downlink. Also, possibly, out of band signaling.
As we will see, used in AMPS, GSM, IS-54/136

## Slide 21: Packet switching versus circuit switching
Introduction
example:
1 Mb/s link
each user:
  100 kb/s when “active”
  active 10% of time
circuit-switching:
  10 users
packet switching:
  with 35 users, probability > 10 active at same time is less than .0004 *
packet switching allows more users to use network!
N
users
1 Mbps link
Q: how did we get value 0.0004?
Q: what happens if > 35 users ?
…..
1-<number>
* Check out the online interactive exercises for more examples
Notes: <number>

## Slide 22
Introduction
great for bursty data
  resource sharing
  simpler, no call setup
excessive congestion possible: packet delay and loss
  protocols needed for reliable data transfer, congestion control
Q: How to provide circuit-like behavior?
  bandwidth guarantees needed for audio/video apps
  still an unsolved problem (chapter 7)
packet switching
Q: human analogies of reserved resources (circuit switching) versus on-demand allocation (packet-switching)?
Packet switching versus circuit switching
1-<number>
Notes: <number>

## Slide 23: Advantages of Circuit Switching
<number>
Guaranteed bandwidth
  Predictable communication performance
  Not “best-effort” delivery with no real guarantees
Simple abstraction
  Reliable communication channel between hosts
  No worries about lost or out-of-order packets
Simple forwarding
  Forwarding based on time slot or frequency
  No need to inspect a packet header
Low per-packet overhead
  Forwarding based on time slot or frequency
  No IP (and TCP/UDP) header on each packet
Notes: <number>

## Slide 24: Disadvantages of Circuit Switching
<number>
Wasted bandwidth
  Bursty traffic leads to idle connection during silent period
Blocked connections
  Connection refused when resources are not sufficient
Connection set-up delay
  No communication until the connection is set up
  Unable to avoid extra latency for small data transfers
Network state
  Network nodes must store per-connection information
  Unable to avoid per-connection storage and state
Notes: <number>

## Slide 25: Packet Switching (e.g., Internet)
<number>
Data traffic divided into packets
  Each packet contains a header (with address)
Packets travel separately through network
  Packet forwarding based on the header
  Network nodes may store packets temporarily
Destination reconstructs the message
Notes: <number>

## Slide 26: How do loss and delay occur?
Introduction
packets queue in router buffers
packet arrival rate to link (temporarily) exceeds output link capacity
packets queue, wait for turn
A
B
packet being transmitted (delay)
packets queueing (delay)
free (available) buffers: arriving packets
dropped (loss) if no free buffers
1-<number>
Notes: <number>

## Slide 27: Four sources of packet delay
Introduction
dproc: nodal processing
check bit errors
determine output link
typically < msec
A
B
propagation
transmission
nodal
processing
queueing
dqueue: queueing delay
time waiting at output link for transmission
depends on congestion level of router
dnodal = dproc + dqueue + dtrans + dprop
1-<number>
Notes: <number>

## Slide 28
Introduction
dtrans: transmission delay:
L: packet length (bits)
R: link bandwidth (bps)
dtrans = L/R
dprop: propagation delay:
d: length of physical link
s: propagation speed in medium (~2x108 m/sec)
dprop = d/s
dtrans and dprop
very different
Four sources of packet delay
propagation
nodal
processing
queueing
dnodal = dproc + dqueue + dtrans + dprop
1-<number>
A
B
transmission
* Check out the Java applet for an interactive animation on trans vs. prop delay
Notes: <number>

## Slide 29: Packet loss
Introduction
queue (buffer) preceding link in buffer has finite capacity
packet arriving to full queue dropped (lost)
lost packet may be retransmitted by previous node, by source end system, or not at all
A
B
packet being transmitted
packet arriving to
full buffer is lost
buffer
(waiting area)
1-<number>
* Check out the Java applet for an interactive animation on queuing and loss
Notes: <number>

## Slide 30: Throughput
Introduction
throughput: rate (bits/time unit) at which bits transferred between sender/receiver
  instantaneous: rate at given point in time
  average: rate over longer period of time
server, with
file of F bits
to send to client
link capacity
Rs bits/sec
link capacity
Rc bits/sec
server sends bits
(fluid) into pipe
pipe that can carry
fluid at rate
Rs bits/sec)
pipe that can carry
fluid at rate
Rc bits/sec)
1-<number>

## Slide 31: Internet protocol stack
Introduction
application: supporting network applications
  FTP, SMTP, HTTP
transport: process-process data transfer
  TCP, UDP
network: routing of datagrams from source to destination
  IP, routing protocols
link: data transfer between neighboring network elements
  Ethernet, 802.111 (WiFi), PPP
physical: bits “on the wire”
application
transport
network
link
physical
1-<number>
Notes: <number>

## Slide 32: Encapsulation
Introduction
source
application
transport
network
link
physical
Ht
Hn
M
segment
Ht
datagram
destination
application
transport
network
link
physical
Ht
Hn
Hl
M
Ht
Hn
M
Ht
M
M
network
link
physical
link
physical
Ht
Hn
Hl
M
Ht
Hn
M
Ht
Hn
M
Ht
Hn
Hl
M
router
switch
message
M
Ht
M
Hn
frame
1-<number>
Notes: <number>

## Slide 33: Network layer
Network Layer
4-<number>
transport segment from sending to receiving host
on sending side encapsulates segments into datagrams
on receiving side, delivers segments to transport layer
network layer protocols in every host, router
router examines header fields in all IP datagrams passing through it
application
transport
network
data link
physical
application
transport
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical

## Slide 34: Two key network-layer functions
Network Layer
4-<number>
forwarding: move packets from router’s input to appropriate router output
routing: determine route taken by packets from source to dest.
  routing algorithms
analogy:
routing: process of planning trip from source to dest
forwarding: process of getting through single interchange

## Slide 35
Network Layer
1
2
3
0111
value in arriving
packet’s header
routing algorithm
local forwarding table
header value
output link
0100
0101
0111
1001
3
2
2
1
Interplay between routing and forwarding
routing algorithm determines
end-end-path through network
forwarding table determines
local forwarding at this router

## Slide 36: Connection setup
Network Layer
4-<number>
3rd important function in some network architectures:
  ATM, frame relay, X.25
before datagrams flow, two end hosts and intervening routers establish virtual connection
  routers get involved
network vs transport layer connection service:
  network: between two hosts (may also involve intervening routers in case of VCs)
  transport: between two processes