## Slide 1: CT 1502 Planning and Design of Communication Networks Circuit Switching Networks Lecture 2
Nada Al Dosary
Aldosary.na@gmail.com

## Slide 2: Outlines
Circuit Switching Principles and Benefits
Principles of Sharing
Circuit Switching Networks Architecture
Analysis of circuit switching network
Examples

## Slide 3: Circuit Switching Principles and Benefits
Principles of Sharing: designing technical architecture that provides communications over wired and wireless channels between variety distance points in order to “share” resources.
Network engineering aims to design and develop these “sharing” ways to achieve its objectives.

## Slide 4: Circuit Switching Principles and Benefits
Main purpose is Sharing the channel

## Slide 5: Circuit Switching Principles and Benefits
Principles of Sharing
  Fixed Sharing:
    Frequency Division Multiplexing(FDM)
    Time Division Multiplexing(TDM)
  Dynamic Division:
    more efficient, less expensive.

## Slide 6: Fixed sharing
time
time
frequency

## Slide 7: Principles of Fixed Division: Frequency
Frequency Bandwidth: the difference in hertz between the highest frequency the signal uses and the lowest frequency it uses.
Multiplexing: to refer to the combination of information streams from multiple sources for transmission over a shared medium.

## Slide 8: Principles of Fixed Division: Frequency
    Frequency Division Multiplexing(FDM): Divide the frequency spectrum into logical channels and assign each information flow one logical channel
N = F / f
N: number of sub-channel
F: frequency bandwidth
of shared medium(channel)
f: frequency of sub-bandwidth
Shared channel
Sub-channel
Sub-channel
Sub-channel

## Slide 9: Frequency Division Multiplexer(FDM)

## Slide 10: Frequency Division Multiplexer(FDM)
A circuit switch bundles (multiplexes) multiple voice calls on a high bandwidth link

## Slide 11: Example (Frequency Division Multiplexer)
Five channels, each with a 100-KHz bandwidth, are to be multiplexed together. What is the minimum bandwidth of the link if there is a need for a guard band of 10 KHz between the channels to prevent interference?
Answer :
For five channels, we need at least four guard bands. This means that the required bandwidth is at least
N=F/f => F= N . f
5 x 100 + 4 x 10 = 540 KHz,
as shown next slide

## Slide 12: Example (Frequency Division Multiplexer)

## Slide 13: Principles of Fixed Division: Time
    Time Division Multiplexing(TDM): is a digital process that allows several connections to share the high bandwidth of a link .Each connection occupies(يشغل) a portion of time in the link
      multiplexing in time simply means transmitting an item from one source, then transmitting an item from another source, and so on
      TDM is a digital multiplexing technique for combining several low-rate channels into one high-rate one.
Notes: T: في الوحدة الزمنية الواحدة، كم مقدار الداتا التي تحملها

## Slide 14: Principles of Fixed Division: Time
      N = T / s
      N: number of sub-channel
      T: time frame of shared
      medium(channel)
      S: time slots
Shared channel
Sub-channel
Sub-channel
Sub-channel

## Slide 15: Time Division Multiplexer(TDM)

## Slide 16: Time Division Multiplexer(TDM)
Time is divided into frames of fixed length
Each frame has a fixed number of constant-sized “slots”
Each circuit obtains one or more “slots” per frame

## Slide 17: Time Division Multiplexer(TDM)
Can all cars move
at the same time?

## Slide 18: Time Division Multiplexer(TDM)

## Slide 19: Time Division Multiplexer

## Slide 20: Time Division Multiplexer

## Slide 21: Time Division Multiplexer(TDM)
The data flow(تدفق البيانات) of each connection is divided into units(وحدات) , and the link combines one unit of each connection to make a frame.
The size of the unit can be 1 bit or several bits.
For n input connections , a frame is organized into a minimum of n time slots (num of connections = num of slots)
frame
unit
unit
unit
slot
slot
slot

## Slide 22: Time Division Multiplexer(TDM)
Note
In TDM , the data rate of the link that carries data from N connections must be N times the data rate of a connection to guarantee the flow of data.
Multiplexer
N
channels
Shared
channel
R1
R2
R3
.
.
.
Rn
R1=R2=R3=…….=Rn
R= R1+R2+R2+…..+Rn
R= n . R1

## Slide 23
Time Division Multiplexer

## Slide 24: Time Division Multiplexer

## Slide 25: Example (Time Division Multiplexer)
Four 1-Kbps connections are multiplexed together. A unit is 1 bit.
Find
  (1) the duration of 1 bit before multiplexing
  (2) the transmission rate of the link
  (3) the duration of a time slot
  (4) the duration of a frame

## Slide 26: Example (Time Division Multiplexer)
Answer:
We can answer the questions as follows:
1. The duration of 1 bit is 1/1 Kbps, or 0.001 s (1 ms).
2. The rate of the link is 4 Kbps.
3. The duration of each time slot 0.001/4 s or 25*10-5 s or 0.25 ms
4. The duration of a frame 1 ms.

## Slide 27: Dynamic Division
Dynamic division: allow the user to use channel to transmit data only when he need to.
In fixed division multiplexer Number of users “X” is equal to number of channels “N”
X=N
In Dynamic division
X>N

## Slide 28: Dynamic Division
User request a channel(call)
Circuit switch reserve a sub-channel for that user to use
After user done, the same channel can be reserved for other user
In case all channels busy, and some user request one, the circuit switch “reject”(رفض) the call, that refer as “congestion” (اختناق)

## Slide 29: Dynamic Division

## Slide 30: Dynamic Division
Number of congestions “rejects” should be limited for better performance and efficient usage.
For better usage of this method, the number of requests should be discrete and random in time “ منفصلة زمنياً تقطعاً عشوائياً” ex: Telephone users using Dail-up “المراقمة”
If a user needs a permanent connection “without disconnection” ; Leased line can be used.
  Expensive, No circuit switching, Readiness all time “ no rejects, or congestions”

## Slide 31: Fixed division
Dynamic Division

## Slide 32: Circuit Switching Networks Architecture
Fixed Telephone Networks
Mobile Telephone Networks

## Slide 33: Fixed Telephone Networks
Telephone networks take a hierarchy structure (شكلاً هرمياً), the base is users’ connections “Local Exchanges”(المقاسم المحلية) what form the local telephone network
The hierarchy summit “top” is the
“International Exchanges” (المقاسم الدولية)

## Slide 34: Fixed Telephone Networks
International Exchange
Gateway
Regional
Intermediate exchange
Intermediate exchange
Regional
Intermediate exchange
Intermediate exchange
Local exchange
Local exchange
Local exchange
Local exchange
Local exchange
Local exchange
Local exchange
Local exchange
subscribers

## Slide 35: Fixed Telephone Networks
Characteristics:
  Reliability
  Readiness
  Dial
  Connecting ( circuit switching)
  Continuation
  Ending

## Slide 36: Mobile Telephone Networks
Relies on circuit switching concept
Cellular phones using wireless communication channels
Connection circuit connect mobile users to the nearest cellular mobile network station
One call needs 2 communication channels, one for sending, the
other for receiving

## Slide 37: Mobile Telephone Networks
Mobile telephone networks can serve large number of subscribers at the same time as long as calls are “geographical isolated” (عزل جغرافي) to prevent signals “interference”(تداخل الاشارات)

## Slide 38: How Mobile Telephone Networks
re-usage of frequencies of wireless channels
  Reuse of limited wireless frequencies to serve the most users as possible
since mobile telephone relies on “circuit switching”, it’s requires:
  Dividing frequencies into “clusters”(مجموعات).
  For a frequency set used in one cell, can not be used in neighboring cells, but they can be used in distant cells
  “Geographical isolated” is mandatory for reusing frequencies to avoid interference.

## Slide 39: Frequency Reuse
assigning to each cell a group of channels used within a small geographic area.
Cells are assigned a group of channels that is completely different from neighboring cells.
The coverage area of cells is called the “footprint”.
This footprint is limited by a boundary so that the same group of channels can be used in different cells that are far enough away from each other so that their frequencies do not interfere.

## Slide 40: Circuit Switching Networks Performance
Three factors to define Network Performance:
  Use Demand
  Network Capacity
  Performance Measure

## Slide 41: Use Demands
How many requests?
  Requests are “random”(عشوائية)
  Sometimes high, sometimes low
  Calculate “traffic” (الحركة)
How long it takes to serve?
  Duration of service is “random”
  Long duration, short duration

## Slide 42: Use Demands
Incoming calls:
  Calculate R: how many calls in one unit of time
  R [calls / time unit]
Call duration:
  Calculate “call duration average” D
  D [time units / call]

## Slide 43: Use Demands
Time unit:
  The time unit used in circuit switching networks is:”Hour”
  Performance studies perform on “Busy Hour”
  Busy Hour : is the highest traffic hour in a day
  Service Providers offer discount and offers for subscrubers on remaining hours of the day to reduce the busy hour load.

## Slide 44: Use Demands
Traffic load:
  A = R [calls / hour] . D [hours / call]
  A: traffic load that measuring with “Erlang” as a unit.
  One Erlang is the usage of a channel within one hour

## Slide 45: Network Capacity
N: how many channels can be served
Multiplexer
N
channels
Shared
channels

## Slide 46: Performance Measure
How many rejected calls (Congestion) of total calls.
Rejected Traffic Load: J = B . A
Carried (Services) Traffic: K = (1-B) . A = A – J
Average Channel Occupancy(معدل شغل القناة): q = K / N
q: is service provider’s benefits

## Slide 47: Performance Measure
N= 10
Traffic load(A) and rejected traffic load (J) are proportional increase(يتزايد طردياً)
Carried traffic increase to the highest value that N can manage =(??)

## Slide 48: Performance Measure
Service providers tend to raise the traffic load in order to raise benefits (رفع الأرباح)
That leads to raising the “congestion” which also leads to lower the subscribers satisfaction (عدم رضى العميل) and make them looking for other service provider
Since the service provider is willing to satisfy customers, he should balance the traffic load and the benefits.

## Slide 49: Computing Performance Measure
Network Designer
Service Provider
Subscriber(user)
performance
Traffic
load
Network
Capacity
Load traffic and Network Capacity Balance

## Slide 50
The End