## Slide 1: NET301
Lecture 2

## Slide 2: Standard Models:
OSI Model : Open system Interconnection.
  is a conceptual model that characterizes and standardizes the internal functions of a communication system by partitioning it into abstraction layers. The model is a product of the Open Systems Interconnection project at the International Organization for Standardization (ISO)

## Slide 3: Standard Models:
Layered Model: The model groups similar communication functions into one of seven logical layers
  Change.
  Design.
  Learning.
  Troubleshooting.
  Standards.

## Slide 4: ISO Model
Physical Layer:
  Physical interface between devices
  Handle transmission of bits over communication channel.
  Choice of wired or wireless medium.
  Data is converted into signals
  Include voltage level , connectors, media choice.
  Modulation techniques
  Its responsible the movement of individual bits from one node to another

## Slide 6: ISO Model
Data Link Layer:
  Transforms data into frame.
  Means of activating , maintaining and deactivating a reliable link.
  Error detection and control.
  Flow control.
  Higher layers may assume error free transmission.
  Its responsible the movement of frames from one node to another

## Slide 8: ISO Model
Network Layer:
  Transport of information
  Higher level do not need to know about underlying technology.
  responsible for creating , maintaining and ending network connection.
  Transfer a data packet from node within the network.
  Routing
  Its responsible the movement of individual packet from the source host to destination host.

## Slide 10
Transport layer.
  Exchange of data between end system.(end to end flow control)
  Error free
  In sequence
  Quality of service.
  Layer 4 include transmission control protocol and user datagram protocol.
  Its responsible the delivery of message from one process to another.

## Slide 12: ISO Model
Session Layer:
  Control dialogue between applications
  Half duplex, full duplex.
  Synchronization points (back up point)
  Grouping
  Its responsible dialog control and synchronization

## Slide 13: ISO Model
Presentation Layer:
  Data formats and coding
  Data compression
  Encryption
  Its responsible translation , compression and encryption

## Slide 14: ISO model
Application Layer:
  Layer where the application using the network resides
  Common network application include :remote login , file transfer, e-mail and web browsing
  Means for application to access OSI environment .
  Its responsible for providing the service for user.

## Slide 16: lan standard model
IEEE 802 standard model:
Four 4 main layers.
Physical Layer:
  Electronic, Electrical, mechanical and procedural aspects of electrical signal of the data transmission.
Data Link Layer:
  That consists of two sub-layers:
  Logical Link Control LLC.
  Media Access Control MAC.

## Slide 17: IEEE 802 model:
  Logical Link Control LLC protocol:
    Layer 2 uses Logical Link Control(LLC) to communicate with the upper-level layers.
    Establishment and control logical link between local devices.
    Synchronization تحديد سرعة التبادل بين الوحدات
    Error Control
  Medium Access Control MAC:
    Layer 2 uses Media Access Control(MAC) to decide which computer will transmit.
    Protocols to data entering to network media
    MAC Addressing.
    Collision control.

## Slide 18: IEEE 802 model
Network Layer:
  Routing data across network and from a network to another different one.
Other layers:
  No rigid standard for the rest layers as it may vary from network to another one due to its functions and types.
  They could be OSI upper layers or any other standard model layers.

## Slide 19: OSI vs. IEEE 802 model

## Slide 20: LAN applications
Electronic Communication applications:
  Cheap
  Fixable
  Effectiveness
  Remote access to data
  Access to data from different places( network devices)

## Slide 21: LAN applications
Examples of Electronic Communication applications
  Email applications.
  Chatting applications.
  Audio and Video conferencing applications.
  Cyberspace conferencing.

## Slide 22: LAN applications
Distributed data bases:
  Data entered into a central datacenter or into a distributed databases then can be retrieved from varies local devices in the network.
    Universities database.
    Companies databases.

## Slide 23: Lan applications
Distributed information systems:
  systems that automate the operations of commercial enterprises such as banking and financial transaction processing systems, warehousing systems, and automated factories.
  Communicates to central computers (governments, universities) to retrieve or process information.

## Slide 24: Lan applications
Office automation and teamwork:
  Resource sharing: printers, storage.
  Reduce costs.
  Increase productivity
  Doing a collective work

## Slide 25: Lan application
Electronic transactions:
  Facilitate administrative work
  Reporting systems
  Document editing and viewing
  Document signing
  Document transfers
E-Business : for private business use
E-Government: for government use

## Slide 26: Lan application
Process capabilities improving Applications:
  More than one computer can work collaboratively to do complex and expensive tasks.

## Slide 27: Lan application
Reliability applications:
  Applications can be used to make usage of network devices even if some are offline or unavailable.