## Slide 1: Wide Area Networks and Internet CT1403
Lecture3: Internet Network Layer
1

## Slide 2: Outline
CT1403
Datagram format, fragmentation and assembly
IP addressing: Classes, Subnets
CIDR: Classless Interdomain Routing
DHCP: Dynamic Host Configuration Protocol
<number>

## Slide 3
datagram format
      Fragmentation
      Reassembly
<number>

## Slide 4: The Internet network layer
forwarding
table
host, router network layer functions:
routing protocols
path selection
RIP, OSPF, BGP
IP protocol
addressing conventions
datagram format
packet handling conventions
ICMP protocol
error reporting
router “signaling”
transport layer: TCP, UDP
link layer
physical layer
network
layer
<number>

## Slide 5: IP datagram format
ver
length
32 bits
data
(variable length,
typically a TCP
or UDP segment)
16-bit identifier
header
checksum
time to
live
32 bit source IP address
head.
len
type of
service
flgs
fragment
offset
upper
layer
32 bit destination IP address
options (if any)
IP protocol version
number
header length
(bytes)
upper layer protocol
to deliver payload to
total datagram
length (bytes)
“type” of data
for
fragmentation/
reassembly
max number
remaining hops
(decremented at
each router)
e.g. timestamp,
record route
taken, specify
list of routers
to visit.
how much overhead?
20 bytes of TCP
20 bytes of IP
= 40 bytes + app layer overhead
<number>

## Slide 6: IP fragmentation, reassembly
network links have MTU (maximum transfer unit) - largest possible link-level frame
  different link types, different MTUs
large IP datagram divided (“fragmented”) within net
  one datagram becomes several datagrams
  “reassembled” only at final destination
  IP header bits used to identify, order related fragments
fragmentation:
in: one large datagram
out: 3 smaller datagrams
reassembly
…
…
<number>

## Slide 7: IP fragmentation, reassembly
Network Layer
4-36
ID
=x
offset
=0
fragflag
=0
length
=4000
ID
=x
offset
=0
fragflag
=1
length
=1500
ID
=x
offset
=185
fragflag
=1
length
=1500
ID
=x
offset
=370
fragflag
=0
length
=1040
one large datagram becomes
several smaller datagrams
example:
4000 byte datagram
MTU = 1500 bytes
1480 bytes in data field
offset =
1480/8
offset 0: meaning the data should be inserted at the beginning go byte 0
offset 185: meaning the data should be inserted at the beginning go byte 1480 (185*8=1480)
offset 370: meaning the data should be inserted at the beginning go byte 2960 (370*8=2960)
<number>

## Slide 8
IP Addressing
  Classes
  Subnets
<number>

## Slide 9: IP Addressing
Network Layer
IP address: 32-bit identifier for host, router interface
Interface: connection between host/router and physical link
  router’s typically have multiple interfaces (==>multiple IP addresses)
  host typically has one interface
  IP addresses associated with each interface
223.1.1.1
223.1.1.2
223.1.1.3
223.1.1.4
223.1.2.9
223.1.2.2
223.1.2.1
223.1.3.2
223.1.3.1
223.1.3.27
223.1.1.1 = 11011111 00000001 00000001 00000001
223
1
1
1
<number>

## Slide 10: Classes of IP Addresses
<number>

## Slide 11: Classes of IP Addresses
CT1403
44
<number>

## Slide 12: Classes of IP Addresses
.
<number>

## Slide 13
Subnets
<number>

## Slide 14: What is subnetting?
Subnetting is the process of borrowing bits from the HOST bits, in order to divide the larger network into small subnets.
Subnetting does NOT give you more hosts, but actually costs you hosts (decrease number of hosts).
You lose two host IP Addresses for each subnet, and perhaps one for the subnet IP address and one for the subnet broadcast IP address.
<number>

## Slide 15: Why Do We Use Subnetting?
A company uses two or more types of LAN technology (for example, Ethernet, Token Ring) on their network or different physical media (such as Ethernet, FDDI, WAN, etc.)
Two network segments are restricted by distance limitations (for example, remote offices linked via point-to-point circuit).
Segments need to be localized for network management reasons (accounting segment, sales segment, etc.).
Hosts which dominate most of the LAN bandwidth need to be isolated.
Security.
The most common reason is to control network traffic.
<number>

## Slide 16: How it works?
The IP address is split into a network and host portion.
The network portion always remains fixed for a particular network, while the remaining bits which make up the host portion can be altered to give the range of addresses to assign to hosts.
To determine where the network portion ends and the host portion begins, a subnet mask is used.
<number>

## Slide 17: Subnet Mask
07/29/26
Fatimah Al-Akeel - Network 9
<number>
A subnet mask is used to separate a network number from the host number in an IP address.
255 represents a network and 0 represents a host.
Default subnet masks:
Class A - 255.0.0.0 - 11111111.00000000.00000000.00000000
Class B - 255.255.0.0 - 11111111.11111111.00000000.00000000
Class C - 255.255.255.0 - 11111111.11111111.11111111.00000000

## Slide 18: Steps to Solve Subnetting Questions
Look at the MSB (Most Significant Bit) of the IP, Identify the Class(A, B or C), then determine the number of bits assigned to the Network Portion
(8 for class A, 16 for Class B and 24 for Class C)
  Ex.: IP=182.250.200.3, Class = B, N =16 bits
Look at Subnet Mask (SM), the number of zeros identify the Host portion
  Ex. SM = 11111111.11111111.11111111.00000000, H=8 bits
Look at IP and SM together, The portion Between the Network and Host portions is the Sub Network portion.
  Ex. IP= 182 . 250 . 200 . 3
  10110110. 11111010.11001000.00000011
  SM = 11111111.11111111.11111111.00000000 = 255.255.255.0
<number>
N = 16
SN = 8
H= 8

## Slide 19
Identify the Subnet ID: By doing (IP address ) AND (Mask)
  Subnet ID = 10110110. 11111010.11001000.00000000
Identify Broadcast address: By changing all bits of host portion in Subnet ID to 1’s.
  Broadcast address = 10110110. 11111010.11001000.11111111
Identify the First IP address: Change the LSB of host portion in Subnet ID to 1.
  First IP address = 10110110. 11111010.11001000.00000001
Identify the Last IP address: Subtract 1 from host portion of Broadcast address.
  Last IP address = 10110110. 11111010.11001000.11111110
<number>

## Slide 20: Example (1)
Given the following IP address 38.9.211.19 with a subnet mask of 255.255.255.240 determine:
  Network Address
  Default subnet mask
  Broadcast address of the network
  Subnet ID
  Broadcast address of the subnet.
  First & last host address in the subnet.
<number>

## Slide 21: Example (1)
Network Address
    To determine the network address we have to determine the class of the IP address
    38.9.211.0  38 ϵ {1-126} Class A
    In class A network portion is the first octet & the remaining three octets for the host are zeros.
    Network Address: 38.0.0.0
<number>

## Slide 22: Example (1)
  Default subnet mask
  For Class A addresses, default subnet mask is: 255.0.0.0
  Broadcast address of the network
  Changing all the host bits to 1 give you the broad cast address:
  Broadcast Address = 38.255.255.255
<number>

## Slide 23: Example (1)
  Subnet ID:
    First: Determine the following bits in the following order:
      Network portion (N) (Fixed depends on the IP class)
      Subnet portion (S) (From the end of the network portion to the last bit in the mask with the value 1)
      Host portion (H) (The remaining bits after the subnet portion)
IP 00100110.00001001.11010011 . 00010011
Mask 11111111 . 11111111 . 11111111 .11110000
<number>
N = 8
H=4
S = 20

## Slide 24: Example (1)
    Second:
    Do the AND operation between the IP address & the mask
IP 00100110.00001001.11010011 . 00010011
Mask 11111111 . 11111111 . 11111111 .11110000
    ______________________________________________
  Subnet ID 00100110.00001001.11010011 . 00010000
  Subnet ID in decimal = 38.9.211.16
<number>
AND

## Slide 25: Example (1)
  Broadcast address of the subnet.
  To get the broad cast address replace the host bits in the subnet ID with 1s
  Subnet ID 00100110.00001001.11010011 . 00010000
Broadcast Address 00100110.00001001.11010011 . 00011111
Broadcast Address in decimal 38.9.211.31
<number>
Host bits

## Slide 26: Example (1)
  First & last host address in the subnet.
  To get the first address replace all the host bits with zeros except the last bit replace it with one as follows:
  Subnet ID 00100110.00001001.11010011 . 00010000
  First Host Address 00100110.00001001.11010011 . 00010001
  First Host Address in decimal 38.9.211.17
<number>
Host bits
Host bits

## Slide 27: Example (1)
  First & last host address in the subnet.
  To get the last address replace all the host bits with ones except the last bit replace it with zero as follows:
  Subnet ID 00100110.00001001.11010011 . 00010000
  Last Host Address 00100110.00001001.11010011 . 00011110
  Last Host Address in decimal 38.9.211.30
<number>
Host bits
Host bits

## Slide 28: Example (2): IP=182.250.200.028, SM= 255.255.255.248
  IP = 10110110. 11111010.11001000.00011100
  SM = 11111111.11111111.11111111.11111000
  Class of the IP is B
  Network Address= 10110110. 11111010.00000000.00000000
  Default Subnet Mask of the IP = 11111111.11111111.00000000.00000000
  Broadcast address of the network = 10110110. 11111010.11111111.11111111
  Subnet ID = 10110110. 11111010.11001000.00011000
  Broadcast address of the subnet = 10110110. 11111010.11001000.00011111
  First IP address = 10110110. 11111010.11001000. 00011001
  Last IP address = 10110110. 11111010.11001000. 00011110
<number>
N = 16
SN = 13
H= 3

## Slide 29: In Decimal Example (2): IP=182.250.200.28, SM= 255.255.255.248
  IP = 182.250.200.28
  SM = 255.255.255.248
  Class of the IP is B
  Network Address= 182.250.0.0
  Default Subnet Mask of the IP = 255.255.0.0
  Broadcast address of the network = 182.250.255.255
  Subnet ID = 182.250.200.024
  Broadcast address of the subnet = 182.250.200.31
  First IP address = 182.250.200.025
  Last IP address = 182.250.200.030
<number>

## Slide 30
CIDR
Classless Interdomain Routing
<number>

## Slide 31: IP addressing: CIDR
CIDR: Classless InterDomain Routing
  subnet portion of address of arbitrary length
  address format: a.b.c.d/x, where x is # bits in subnet portion of address
11001000 00010111 00010000 00000000
subnet
part
host
part
200.23.16.0/23
<number>

## Slide 32: Classless Interdomain Routing : CIDR
Generalizes the notation of subnet addressing
As within the subnet addressing, the 32-bit address is divided into two parts (net#, host # ) and has the dotted decimal form (a.b.c.d/x), where x indicates the number of bits in the first part of the address.
CIDR replaces Classful addressing, where the network portion of IP addresses were constrained to 8, 16, or 24
Classful addressing waists IP addresses
<number>

## Slide 33: Classless Interdomain Routing : CIDR
Most organizations needs more than class C but less than class B
CIDR allocates IP address blocks of variable size without regard to classes
  Example: site needs 2000 addresses
assign a block of 2048 addresses
With CIDR address lookup is more complicated
<number>

## Slide 34: CIDR Example
CT1403
مثال 6: قناع الشبكة الفرعية (Subnet Mask) هو (/30).
11111111 . 11111111 . 11111111 . 111111 00
قناع الشبكة الفرعية
ثابتة (رقم الشبكة)
متغيرة
(رقم الطرفية)
255.255.255.252 (/22)
255.255.255.252 | قناع الشبكة الفرعية (Dotted Decimal Notation)
22 - 2 = 2 طرفية | عدد الطرفيات التي تدعمها الشبكة
<number>
reference: This slide was created by Dr. Mohammad Arafah

## Slide 35
Obtaining IP Addresses
<number>

## Slide 36: IP addresses: how to get one?
Q: How does a host get IP address?
hard-coded by system administrator in a file
  Windows: control-panel->network->configuration->tcp/ip->properties
  UNIX: /etc/rc.config
More often using ===> DHCP: Dynamic Host Configuration Protocol: dynamically get address from as server
  “plug-and-play”
<number>

## Slide 37: DHCP: Dynamic Host Configuration Protocol
goal: allow host to dynamically obtain its IP address from network server when it joins network
  can renew its lease on address in use
  allows reuse of addresses (only hold address while connected/“on”)
  support for mobile users who want to join network (more shortly)
DHCP overview:
  host broadcasts “DHCP discover” msg [optional]
  DHCP server responds with “DHCP offer” msg [optional]
  host requests IP address: “DHCP request” msg
  DHCP server sends address: “DHCP ack” msg
<number>

## Slide 38: DHCP client-server scenario
223.1.1.0/24
223.1.2.0/24
223.1.3.0/24
223.1.1.1
223.1.1.3
223.1.1.4
223.1.2.9
223.1.3.2
223.1.3.1
223.1.1.2
223.1.3.27
223.1.2.2
223.1.2.1
DHCP
server
arriving DHCP
client needs
address in this
network
<number>

## Slide 39: DHCP client-server scenario
Network Layer
4-47
DHCP server: 223.1.2.5
arriving
client
DHCP discover
src : 0.0.0.0, 68
dest.: 255.255.255.255,67
yiaddr: 0.0.0.0
transaction ID: 654
DHCP offer
src: 223.1.2.5, 67
dest: 255.255.255.255, 68
yiaddrr: 223.1.2.4
transaction ID: 654
lifetime: 3600 secs
DHCP request
src: 0.0.0.0, 68
dest:: 255.255.255.255, 67
yiaddrr: 223.1.2.4
transaction ID: 655
lifetime: 3600 secs
DHCP ACK
src: 223.1.2.5, 67
dest: 255.255.255.255, 68
yiaddrr: 223.1.2.4
transaction ID: 655
lifetime: 3600 secs
<number>

## Slide 40: DHCP: more than IP addresses
Network Layer
4-48
DHCP can return more than just allocated IP address on subnet:
  address of first-hop router for client
  name and IP address of DNS sever
  network mask (indicating network versus host portion of address)
<number>

## Slide 41: DHCP: example
Network Layer
4-49
connecting laptop needs its IP address, addr of first-hop router, addr of DNS server: use DHCP
router with DHCP
server built into
router
DHCP request encapsulated in UDP, encapsulated in IP, encapsulated in 802.1 Ethernet
Ethernet frame broadcast (dest: FFFFFFFFFFFF) on LAN, received at router running DHCP server
Ethernet demuxed to IP demuxed, UDP demuxed to DHCP
168.1.1.1
DHCP
UDP
IP
Eth
Phy
DHCP
DHCP
DHCP
DHCP
DHCP
DHCP
UDP
IP
Eth
Phy
DHCP
DHCP
DHCP
DHCP
DHCP
<number>

## Slide 42: DHCP: example
Network Layer
4-50
DHCP server formulates DHCP ACK containing client’s IP address, IP address of first-hop router for client, name & IP address of DNS server
encapsulation of DHCP server, frame forwarded to client, demuxing up to DHCP at client
router with DHCP
server built into
router
DHCP
DHCP
DHCP
DHCP
DHCP
UDP
IP
Eth
Phy
DHCP
DHCP
UDP
IP
Eth
Phy
DHCP
DHCP
DHCP
DHCP
client now knows its IP address, name and IP address of DSN server, IP address of its first-hop router
<number>