## Slide 1: NET 301
LECTURE3

## Slide 2: LAN data transmission
Layer1 Physical Layer:
    Electronic, Electrical, mechanical and procedural aspects of electrical signal of the data transmission.
Data VS. Information
  Data: is raw, plain and unorganized facts that need to be processed. Data can be something simple and seemingly random and useless until it is organized.
  Information: When data is processed, organized, structured or presented in a given context so as to make it useful, it is called Information.

## Slide 3: signals
Signals:
  is a function that conveys information about the behaviour or attributes of some phenomenon.
  a detectable physical quantity or impulse (as a voltage, current, or magnetic field strength) by which messages or information can be transmitted .
  Electrical, electromagnetic or optical wave that represent an information

## Slide 4: data
Analogue data:
Any continuous data for which the time varying feature (variable) of the signal is a representation of some other time varying quantity.
  Sound waves
  Temperature
  Pressure

## Slide 6: data
Digital data:
can only take one finite number or value in one time.
  Students number
  Word “ book”

## Slide 8: signals
Signals also can be divided into :
Analogue signals:
  Continuous, changing with time. Can take a continuous electronic signal.

## Slide 9: Analogue signal
Microphone signal illustration:

## Slide 10: Analogue signal
The primary disadvantage of analog signal is that any system has noise
even if the resolution of an analog signal is higher than a comparable digital signal, after enough processing the analog signal to noise ratio will be lower.
Electrically, analog signal noise can be diminished by shielding, good connections, and several cable types such as coaxial or twisted pair.

## Slide 11: signal
Digital signal:
  Take discrete value in a time, discontinuing values over continuing time.

## Slide 12: signal
In computer architecture and other digital systems, a waveform that switches between two voltage levels representing the two states of a Boolean value (0 and 1).
The clock signal is a special digital signal that is used to synchronize digital circuits. Logic changes are triggered either by the rising edge or the falling edge.

## Slide 13: signal
The given diagram is an example of the practical pulse and therefore we have introduced two new terms that are:
  Rising edge: the transition from a low voltage (level 1 in the diagram) to a high voltage (level 2).
  Falling edge: the transition from a high voltage to a low one

## Slide 14: How to study signals?
Analogue and digital signals can be studied by studying:
Frequency and Time.
Frequency:
  Number of occurrences of a repeating event per unit time.
Signal Frequency:
  Number of signal cycles per second.

## Slide 15: signal
Signal1: needs 8\200=( 0.04) second for one cycle, 25 cycle per 1 second.
  Signal1 frequency: 25 (cycle\second) Hertz
Signal2 Frequency: 100 cycle\second

## Slide 16: Frequency bandwidth
Electrical waves could be a set of frequencies, more than one single frequency.
Signal Bandwidth:
  The difference between the highest frequency and the lowest frequency.
  It is typically measured in hertz, and may sometimes refer to passband bandwidth, sometimes to baseband bandwidth

## Slide 17: Frequency bandwidth

## Slide 18: Signals
signals can be represented:
  X(t) = A. sin (2 π.f. t + θ )
    Where:
    A: signal amplitude value in volts
    Sin: sin function.
    π : (Pi)3.14
    F: frequency ( cycles per second, Hz)
    T: time or period (seconds)
    Θ: (theta) Phase (radian)

## Slide 19: Signals
Amplitude (A)اتساع الاشارة :
  A measurement of the signal change over a single period.
  Can be positive or negative value.
  Measured in Volts.
Frequency (F) التردد :
  Number of cycle per one second
  Measured in Hertz Hz
Period (T):
  Time signal needs to perform one single cycle
  Measured in second

## Slide 20: Signals
Period and frequency are in a inverse relation.
  Frequency is inverse of period.
  period is inverse of Frequency.
  F= 1\T and T=1\F
Phase θ:
  The initial angle of a sinusoidal function (sin) at its origin.
  Another usage is the fraction of the wave cycle which has elapsed relative to the origin
  Measured in degree °
  Could be positive if signal leading ,or negative if signal lagging.

## Slide 21
Two signals with the same amplitude and phase, but different frequencies

## Slide 22
Two signals with the same phase and frequency, but different amplitudes

## Slide 23
Three sine waves with the same amplitude and frequency, but different phases

## Slide 24: Signals
Signal1 phase= 0 °
Phase could be measured in (radians).
One cycle= 2 π radian = 360 °

## Slide 25: Signals
Wave length:
  The distance between peaks (high points) is called wavelength
  Length of one complete cycle.

## Slide 26: Signals
V= f . λ
  V: wave propagation speed (meter/second)
  F: frequency (hertz)
  λ: (lambda)wavelength ( meter)
Wave speed differ from wave to wave, differ based on the Propagation medium.
  In space: electronic and electromagnetic wave propagation speed equals to light speed 300,000,000 m\s (3*10 8 m\s)
  Sound wave propagation speed 332m\s in zero degree temperature 0°

## Slide 27: signals
As F=1\T ,, then:
λ = V.T
  So λ unit is a distance based unit: