## Slide 1: Lecture 4 Network Layer(Part2): Routing Algorithms

## Slide 2: Routing
Routing - Process of finding a path from a source to every destination in the network.
  Goal - determine “good” path (sequence of routers) thru network from source to dest.
Algorithm - Routing protocols use algorithms for facilitating routing information and for best path determination.
4a-<number>
Notes: <number>

## Slide 3: Routing
4a-<number>
Graph abstraction for routing algorithms:
graph nodes are routers
graph edges are physical links
  link cost: delay, $ cost, or congestion level
A
E
D
C
B
F
2
2
1
3
1
1
2
5
3
5
“good” path:
  typically means minimum cost path
  other definitions possible

## Slide 4: Routing Algorithm: Static or Dynamic?
4a-<number>
Static:
routes manually defined
Remote networks are manually entered into the route table
change slowly over time or only one possible route
Appropriate in some circumstances, but obvious drawbacks (routes added/removed? sharing load?)
Not much more to say?
Dynamic:
Routes learned by communicating with other routers
routes change more quickly (Updated routing information)
  periodic update
  in response to link cost changes

## Slide 5: Global Dynamic Routing
4a-<number>
A
E
D
C
B
F
2
2
1
3
1
1
2
5
3
5
See the big picture; Find the best Route
What algorithm do you use?

## Slide 6: Routing Protocol Operating Fundamentals Dynamic Routing Protocol Operation
In general, the operations of a dynamic routing protocol can be described as follows:
Routers exchange routing information to learn about remote networks.
The router shares routing messages and routing information with other routers that are using the same routing protocol.
The router sends and receives routing messages on its interfaces.
When a router detects a topology change the routing protocol can advertise this change to other routers.
4a-<number>
Notes: <number>
<number>
7.1.3.1

## Slide 7: The Role of Dynamic Routing Protocols
Advantages of dynamic routing
  Automatically share information about remote networks
  Determine the best path to each network and add this information to their routing tables
  Compared to static routing, dynamic routing protocols require less administrative overhead
  Help the network administrator manage the time-consuming process of configuring and maintaining static routes
Disadvantages of dynamic routing
  Dedicate part of a routers resources for protocol operation, including CPU time and network link bandwidth
4a-<number>
Notes: <number>
<number>
7.1.1.3

## Slide 8
<number>
Autonomous system (AS)
Internet can be so large that one routing protocol cannot handle the updating of the routing tables of all routers.
For this reason, an internet is divided into autonomous systems.
Autonomous system (AS) is a group of networks and routers under the authority of a single administration.
Notes: <number>

## Slide 9
<number>
INTER-AND INTRA-DOMAIN ROUTING
Interior Gateway Protocols (IGP) (intra-domain routing)
Used for routing inside an AS
Examples: RIP, EIGRP, OSPF, and IS-IS
Each AS can choose an IGP to handle routing inside the AS
Exterior Gateway Protocols (EGP) (inter-domain routing)
Used for routing between Ass
Usually one EGP is chosen to handle routing between ASs.
Notes: <number>

## Slide 10
<number>
Notes: <number>

## Slide 11
4a-<number>
(Intra-domain)
(Inter-domain)

## Slide 12: Link-State Dynamic Routing
4a-<number>
Notes: <number>
<number>
7.4

## Slide 13: Link-State Routing Protocols
A router is configured with a link-state routing protocol can gather information from the network & create a complete routing table using Dijkstra’s algorithm
A link-state router uses the link-state information to a topology map and to select the best path to all destination networks in the topology.
4a-<number>
Notes: A link-state routing protocol is like having a complete map of the network topology. The sign posts along the way from source to destination are not necessary, because all link-state routers are using an identical map of the network. A link-state router uses the link-state information to create a topology map and to select the best path to all destination networks in the topology.
<number>

## Slide 14: Link State Process
<number>
Each router is responsible for contacting its own directly connected routers and networks
Each router creates packet called the link state packets (LSP) the states of the links by each node,
broadcasting of LSPs to every other routers, called flooding (efficiently)
Formation of a shortest path tree for each node (router)
Calculation of a routing table based on the shortest path tree

## Slide 15: Creation of LSP
<number>
LSP data: E.g. the node ID, the list of links, a sequence number, and age.
LSP Generation could be:
  When there is a change in the topology of the domain
  Or on a periodic basis
    There is no actual need for this type of LSP, normally 60 minutes or 2 hours

## Slide 16: Link State Algorithm: Some Notation
4a-<number>
Notation:
c(i,j): link cost from node i to j. cost infinite if not direct neighbors
D(v): current value of cost of path from source to dest. V
n(v): next hop from this source to v along the least cost path
N: set of nodes whose least cost path definitively known

## Slide 17: Dijkstra’s algorithm: example
4a-<number>
Step
0
1
2
3
4
5
start N
A
AD
ADE
ADEB
ADEBC
ADEBCF
D(B),n(B)
2,B
2,B
2,B
D(C),n(C)
5,C
4,D
3,D
3,D
D(D),n(D)
1,A
D(E),n(E)
infinity
2,D
D(F),n(F)
infinity
infinity
4,D
4,D
4,D
A
E
D
C
B
F
2
2
1
3
1
1
2
5
3
5

## Slide 18: Dijkstra’s Algorithm gives routing table
4a-<number>
A
A
B
C
D
E
F
n(A) = A
n(B) = B
n (C)= D
n(D) = D
n(E) = D
n(F) = D
Outgoing Link
destination

## Slide 19: Distance Vector Dynamic Routing
4a-<number>
Notes: <number>
<number>
7.2

## Slide 20: Distance Vector Routing Protocols
For R1, 172.16.3.0/24 is one hop away (distance) it can be reached through R2 (vector)
4a-<number>
Notes: <number>
<number>
7.1.4.3

## Slide 21: Distance Vector Routing Protocols
Distance vector means that routes are advertised by providing two characteristics:
Distance: Identifies how far it is to the destination network and is based on a metric such as the hop count, cost, bandwidth, delay, and more
Vector: Specifies the direction: the next-hop router or exit interface to reach the destination
4a-<number>

## Slide 22: Distance Vector Routing Protocols
A router using a distance vector routing protocol does not have the knowledge of the entire path to a destination network.
The only information a router knows about a remote network is the distance or metric to reach that network and which path or interface to use to get there.
Distance vector protocols use routers as sign posts along the path to the final destination.
Distance vector routing protocols do not have an actual map of the network topology.
4a-<number>

## Slide 23: Distance Vector routing protocols
Share updates between neighbors
Not aware of the network topology
RIPv1 send periodic updates to broadcast IP 255.255.255.255 even if topology has not changed
Updates consume bandwidth and network resources
RIPv2 and EIGRP use multicast addresses
EIGRP will only send an update when topology has changed
RIP uses the Bellman-Ford algorithm as its routing algorithm
IGRP and EIGRP use the Diffusing Update Algorithm (DUAL) routing algorithm developed by Cisco
4a-<number>
Notes: <number>
<number>
7.2.1.1

## Slide 24: Distance Vector Routing Algorithm
4a-<number>
Distance Table data structure
each node has its own row for each possible destination
column for each directly-attached neighbor to node
example: in node X, for dest. Y via neighbor Z:
D (Y,Z)
X
distance from X to
Y, via Z as next hop
c(X,Z) + min {D (Y,w)}
Z
w
=
=
D ()
Y
Z
Dx(Y,Z)
X
cost to destination via
destination
Column only for each neighbor
Rows for each possible dest !

## Slide 25: Example: Distance Table for E
4a-<number>
A
E
D
C
B
7
8
1
2
1
2
D ()
A
B
C
D
A
1
7
6
4
B
14
8
9
11
D
5
5
4
2
E
cost to destination via
destination
D (C,D)
E
c(E,D) + min {D (C,w)}
D
w
=
=
2+2 = 4
D (A,D)
E
c(E,D) + min {D (A,w)}
D
w
=
=
2+3 = 5
Loop back through E!
D (A,B)
E
c(E,B) + min {D (A,w)}
B
w
=
=
8+6 = 14
Loop back through E!
Column only for each neighbor
Rows for each possible dest !
D (row, col)
E

## Slide 26: Distance table gives routing table
4a-<number>
D ()
A
B
C
D
A
1
7
6
4
B
14
8
9
11
D
5
5
4
2
E
cost to destination via
destination
A
B
C
D
A,1
D,5
D,4
D,2
Outgoing link
to use, cost
destination
Distance table
Routing table
= least cost

## Slide 27: Distance Vector Routing: overview
4a-<number>
Iterative, asynchronous: each local iteration caused by:
local link cost change
message from neighbor: its least cost path change from neighbor
Distributed:
each node notifies neighbors only when its least cost path to any destination changes
  neighbors then notify their neighbors if necessary
wait for (change in local link cost of msg from neighbor)
recompute distance table
if least cost path to any dest has changed, notify neighbors
Each node:

## Slide 28: Comparison of LS and DV algorithms
4a-<number>
Message complexity
LS: nodes send info on directly connections to all other nodes
  More, smaller messages
DV: nodes send info on best paths to all destinations to neighbors
  Fewer, larger messages
Speed of Convergence
LS: O(n2) algorithm
DV: convergence time varies
  may be routing loops
  count-to-infinity problem
Robustness: what happens if router malfunctions?
LS:
  node can advertise incorrect link cost
  each node computes only its own table
DV:
  DV node can advertise incorrect path cost
  each node’s table used by others
    error propagate thru network

## Slide 29: DUAL
4a-<number>
Loop-free routing algorithm that performs a “diffused” computation of a routing table
Researched and developed at SRI International by Dr. J.J. Garcia-Luna-Aceves
No need for route hold down
http://www.cisco.com/univercd/cc/td/doc/cisintwk/ito_doc/en_igrp.htm
Enhanced IGRP integrates the capabilities of link-state protocols into distance vector protocols
DUAL enables EIGRP routers to determine whether a path advertised by a neighbor is looped or loop-free, and allows a router running EIGRP to find alternate paths without waiting on updates from other routers

## Slide 30: Routing
<number>
Recall: There are two parts to routing IP packets:
1. How to pass a packet from an input interface to the output interface of a router (packet forwarding) ?
2. How to find and setup a route ?
There are two approaches for calculating the routing tables:
  Static Routing
  Dynamic Routing: Routes are calculated by a routing protocol

## Slide 31
4a-<number>

## Slide 32: RIP -- What is it?
RIP is a routing protocol for exchanging routing table information between routers.
RIP is an IGP routing protocol used inside an AS.
It is a very simple protocol based on distance vector routing
4a-<number>

## Slide 33: RIP Characteristics
Distance vector routing protocol.
Uses hop count as a path selection metric.
RIP routes have an administrative distance of 120.
RIP has a maximum hop count of 15 hops , with “16” equal to “”.
Three types of timers.
4a-<number>

## Slide 34: Distance Vector Routing
In distance vector routing, each router shares its routing table with its immediate neighbors periodically and when there is a change.
The three features:
  Each router sends all or part of its routing table in routing updates
  Sharing only with neighbors
  Sharing at regular intervals and when there is a change
4a-<number>

## Slide 35: Routing Table
Every router keeps a routing table.
The routing table has one entry for each destination network of which the router is aware.
4a-<number>

## Slide 36: Routing Table
The entry consists of:
  the destination network address,
  the shortest distance to reach the destination in hop count,
  and the next route to which the packet should be delivered.
The table may contain other information.
4a-<number>

## Slide 37: Hop Count
The hop count is the number of networks that a packet encounters to reach its final destination.
After 15 hops, the packet is discarded
4a-<number>

## Slide 38: Initialization
When a router is added to a network, it initializes a routing table for itself, using its configuration file.
The table contains only the directly attached networks and hop counts, which are initialized to 1.
The next-hop field is empty.
<number>

## Slide 39: Sharing
The whole idea of distance vector routing is the sharing of information between neighbors
Although router A does not know about router C, router B does. So if router B shares its routing table with A, node A can also know how to reach node C
In distance vector routing, each node shares its routing table with its immediate neighbors periodically and when there is a change.
Note:
4a-<number>

## Slide 40: Updating
When a router receives a 2-column table from a neighbor, it needs to update its routing table. Updating takes 3 steps:
  The receiving router needs to add one hop count to each value in the hop count column
  The receiving router needs to add the name of the sending router to each row as the 3rd column if the receiving router uses information from any row. The sending router is the next node in the route
4a-<number>

## Slide 41: Updating
3- The receiving router needs to compare each row of its old table with the corresponding row of the modified version of the received table.
4a-<number>

## Slide 42: Updating Algorithm
4a-<number>

## Slide 43
4a-<number>

## Slide 44
<number>
Notes: <number>

## Slide 45: When to Share
The table is sent both periodically and when there is a change in the table
Periodic Update. A router sends its routing table, normally every 30 seconds, in a periodic update.
Triggered Update. A router sends its 2-column routing table to its neighbors any time there is a change in its routing table. The change can result from the following.
  A router receive a table from a neighbor resulting in changes in its own table after updating
  A router detects some failure in the neighboring links which results in a distance change to infinity
4a-<number>
Notes: Triggered Updates: If a metric changes on a link, a router immediately sends out an update without waiting for the end of the update period.
<number>

## Slide 46: Request and Response
Request. A request message is sent by a router that has just come up or by a router that has some time-out entries. A request can ask about specific entries or all entries
Response. A solicited response is sent only in answer to a request. It contains information about the destination specified in the corresponding request. An unsolicited response is sent periodically, every 30 s or when there is a change in the routing table
4a-<number>
Notes: Two types of messages:
  Request messages
    used to ask neighboring nodes for an update
  Response messages
    contains an update
<number>

## Slide 47: Timer in RIP
RIP uses 3 timers. The periodic timer controls the sending of messages, the expiration timer governs the validity of a route, and the garbage collection timer advertises the failure of a route
<number>

## Slide 48: Periodic Timer
The periodic timer controls the advertising of regular update messages
The working model uses a random number between 25 and 30 s
This is to prevent any possible synchronization and therefore overload on an network if routers update simultaneously
4a-<number>

## Slide 49: Expiration Timer
The expiration timer governs the validity of a route
When a router receives update information for a route, the expiration timer is set to 180 s for that particular route
Every time a new update for the route is received, the timer is reset
If the timer is expired, the hop count of the route is set to 16, which means the destination is unreachable
4a-<number>
Notes: Routes are timeout (set to 16) after 3 minutes if they are not updated
<number>

## Slide 50: Garbage Collection Timer
When the information about a route becomes invalid, the router does not immediately purge that route from its table
Instead, it continues to advertise the route with a metric value of 16
At the same time, the garbage collection timer is set to 120 s for that route
When the count reaches zero, the route is purged from the table
4a-<number>

## Slide 51: Example
A routing table has 20 entries. It does not receive information about five routes for 200 s. How many timers are running at this time?
Solution The 21 timers are listed below: Periodic timer: 1 Expiration timer: 20 − 5 = 15 Garbage collection timer: 5
4a-<number>

## Slide 52: RIP v1 Drawbacks
RIP version 1 does not recognize subnets.
This feature was added in RIP version 2.
Because RIP only uses hop count as a metric, packets may be forced to take a slower route with less hops over a faster route with more hops.
  Other routing protocols use a combination of different metrics to calculate a route.
4a-<number>

## Slide 53: RIPv2
<number>
RIPv2 is an extends RIPv1:
  Subnet masks are carried in the route information
  Authentication of routing messages
  Exploits IP multicasting
Extensions of RIPv2 are carried in unused fields of RIPv1 messages
Notes: Classless Addressing
Authentication
Multicasting
  RIPv1 uses broadcasting to send RIP messages to every neighbors. Routers as well as hosts receive the packets
  RIPv2 uses the all-router multicast address to send the RIP messages only to RIP routers in the network
<number>