## Slide 1: NET301
Lecture 4

## Slide 2: Data and information unit
Bit ( 0,1 )
  9 = 1001
  23 = 10111
  A = 10000001 ASCII -American Standard Code for Information Interchange
  أ = 11000110 ASMO
Byte = 8 bits
  Letter, number , special characters (! , ?)
Kilo byte = 1024 byte
  Kbyte
Mega Byte = 1024 Kbyte = 1024 ×1024 byte

## Slide 3: Data and information unit
Gigabyte = 1024 Mbyte
Terabyte = 1024 Gigabyte

## Slide 4: Bit rate
Bit rate:
  is the number of bits that are conveyed or processed, transmitted per unit of time.
  Bit\second , Kbyte\sec , gbyte\sec

## Slide 5: Bit rate

## Slide 6: DATA CODING
Data Coding:
  Converting information to digital signals.
  Using Coder مرمز \ Decoder محلل
Modulation:
  Converting information to analog signals.
  Using Modulator معدِل \ Demodulator عاكس التعديل.

## Slide 7: Encoding Techniques
Digital data to digital signal
Digital data to analog signal
Analog data to digital signal
Analog data to analog signal

## Slide 8: Digital data – analog signal
Using electronic circuit in (Modulation devices) to change wave in which it can be transmitted over transmission channel.
  Digital data digital data
  Digital data –> electromagnetic waves –> digital data
fiber optics
Telephone network

## Slide 9: Modulation
Modems:
  Devices can perform Modulation + Demodulation.
Carrier:
  is a high-frequency signal that acts as a basis for information signal. The receiving device is turned to the frequency of the carrier signal that it expects from the sender.
Encoding Techniques:
  Amplitude-Shift Keying (ASK).
  Frequency-Shift Keying (FSK).
  Phase-Shift Keying (PSK).
  Quadrature amplitude modulation (QAM)

## Slide 10: Modulation
ASK
FSK
PSK
QAM
Digital/analog Encoding

## Slide 11
Digital data to analog signal

## Slide 12: Definitions
Amplitude Change
Amplitude
Time
Amplitude
Time
Frequency Change
Amplitude
Time
Phase Change

## Slide 13: Modulation techniques

## Slide 14: Amplitude-shift keying
Change Strength of the signal amplitude to represent 1,0.
Ask is the most modulation method affected by noise.
Noise by heat, electromagnetic induction created by other sources.

## Slide 15: Frequency-shift keying
Change frequency of the signal to represent 0,1.
Not affected by noise.
Physical capabilities of carrier can limit the changes.

## Slide 16: Phase-shift keying
Changes the phase of the signal depend on the data to be transmitted.
bit 0 = 0 ° phase
Bit 1 = 180 ° phase

## Slide 17: Quadrature amplitude modulation
QAM:
  Changing signal phase + amplitude of the signal based on the data transmitted.

## Slide 18: Definitions
Relationship between different phases:
Phase = 0 degrees
Amplitude
Time
Time
Amplitude
Phase = 90 degrees
Time
Amplitude
Phase = 180 degrees
Phase = 270 degrees
Time
Amplitude

## Slide 19: Multilevel signaling
By frequency, amplitude and phase ; bit (0,1) can be represented.
Therefore: 1 signal for 1 bit.
Bit rate: number of bits per 1 second.
Baud rate (modulation rate): number of signals per 1 second.
Bit rate = baud rate.

## Slide 20: Multilevel signaling
To allow high speed data transmission, more than 1 signal can be used in modulation methods.
Ex: 4 signals in 4-PSK each one has a different phase ( 0 °,90 °,180 °,270 °).
0° = 00 (bit), 90°= 01 (bit) , 180°= 10 (bit), 270° = 11 (bit)
Each signal represent 2 bits
8-QAM : using 8 signals , each one can represents 3 bits… etc

## Slide 22: Multilevel signaling
8-QAM (2 amplitudes, 4 phases):
000
001
010
011
100
101
110
111

## Slide 23: Multilevel signaling
16-QAM ( 4 amplitudes, 8 phases):

## Slide 24: Multilevel signaling
8-PSK:
Phase | Tribit
0 | 000
45 | 001
90 | 010
135 | 011
180 | 100
225 | 101
270 | 110
315 | 111
8-PSK phase diagram
000
001
010
011
100
101
110
111

## Slide 25: Bit rate and frequency bandwidth
Bite rate has a direct relation with frequency bandwidth ( Nyguist Relation)
  The more data to be sent, the more frequency bandwidth needed to send this data.
Nyguest Relation:
  D = 2. W
    D: modulation rate (signal\sec) or (baud)
    W: frequency bandwidth (Hertz)R
R = D:
  R: bit rate (bit\sec)
R = 2.W

## Slide 26: Bit rate and frequency bandwidth
R = 2.W means: the more data transmission speed ( bit rate), the more frequency bandwidth needed in the transmission media used to send the data.

## Slide 27
Sinewave الاشارة الجيبية:
  Have two levels. One represent the positive part of the signal, one represent the negative part of the signal.
  positive part = bit (0) , negative part = bit ( 1)
  One cycle can send two 2 bits.
  More cycles in one 1 second W( bandwidth) ; bitrate R = double 2 cycles -> R = 2.W

## Slide 28: Bit rate and frequency bandwidth
Example:
What is the frequency bandwidth needed to send binary data with bitrate = 64kbyte\sec?
Solution:
R = 2 . W
W = R \ 2
R = 64 kbyte = 64000 byte
W = 64000 \ 2
W = 32000 Hz

## Slide 29: Bitrate and frequency bandwidth relationship for multilevel signals
To allow a high speed data transmission, multilevel signals are used.
8-PSK = 8 signals , each one represents 3 bits.
To calculate number of bit per signal:
  N = log 2 M
    N = number of bits per signal.
    M number of signals.
Log b x = y , b y = x

## Slide 30: Bitrate and frequency bandwidth relationship for multilevel signals
R = D. Log2. M
  R : bit rate (bit\sec)
  D: modulation rate-baud rate (signal\sec) ( baud)
As we already know: D = 2 .W
Therefore: R = D . Log2 M
  R = 2.W Log2.M
  W = R \ (2. log2 M )

## Slide 31: Example
Calculate frequency bandwidth needed to transmit data with 64 kbyte\sec, if number of signals is 16 . Calculate also baud rate.
1- bandwidth W:
  R = 2.W . Log2 M
  W = R \ 2. (Log2 M) = 64000 \ 2. log2 16 = 64000\8
  W = 8000 Hz
2- baud rate D: D = 2.W
  R = D . Log2 M
  D = R \ Log2 M
  D = 64000 \ Log2 16 = 64000\4 = 16000 baud

## Slide 32: example
OR :
  D = 2. W
  D = 2. 8000
  D = 16000 baud