## Slide 1: Lecture 5: Internetworking: A closer View
By Dr. Najla Al-Nabhan
Introduction
1-<number>

## Slide 2: Outlines
Introduction
  Review previous lecture:
  Internet?
    network edge
      end systems, access networks, links
    network core
      packet switching, circuit switching, network structure
  Packet-switching vs. circuit-switching
  delay, loss, throughput in networks
  protocol layers, service models
1-<number>
Notes: <number>

## Slide 3: What’s the Internet: “nuts and bolts” view
Introduction
millions of connected computing devices:
  hosts = end systems
  running network apps
communication links
  fiber, copper, radio, satellite
  transmission rate: bandwidth
Packet switches: forward packets (chunks of data)
  routers and switches
wired
links
wireless
links
router
mobile network
global ISP
regional ISP
home
network
institutional
network
smartphone
PC
server
wireless
laptop
1-<number>
Notes: <number>

## Slide 4
Introduction
a human protocol and a computer network protocol:
Q: other human protocols?
Hi
Hi
Got the
time?
2:00
TCP connection
response
Get http://www.awl.com/kurose-ross
<file>
time
TCP connection
request
What’s a protocol?
1-<number>
Notes: <number>

## Slide 5: A closer look at network structure:
Introduction
network edge:
  hosts: clients and servers
  servers often in data centers
access networks, physical media: wired, wireless communication links
network core:
  interconnected routers
  network of networks
mobile network
global ISP
regional ISP
home
network
institutional
network
1-<number>
Notes: <number>

## Slide 6
Introduction
Access net: home network
to/from headend or central office
cable or DSL modem
router, firewall, NAT
wired Ethernet (100 Mbps)
wireless access
point (54 Mbps)
wireless
devices
often combined
in single box
1-<number>
Notes: <number>

## Slide 7: Enterprise access networks (Ethernet)
Introduction
typically used in companies, universities, etc
  10 Mbps, 100Mbps, 1Gbps, 10Gbps transmission rates
  today, end systems typically connect into Ethernet switch
Ethernet
switch
institutional mail,
web servers
institutional router
institutional link to
ISP (Internet)
1-<number>

## Slide 8: Host: sends packets of data
host sending function:
takes application message
breaks into smaller chunks, known as packets, of length L bits
transmits packet into access network at transmission rate R
R: link transmission rate
host
1
2
two packets,
L bits each
packet
transmission
delay
time needed to
transmit L-bit
packet into link
L (bits)
R (bits/sec)
=
=
1-<number>

## Slide 9: Packet-switching
Introduction
mesh of interconnected routers
packet-switching: hosts break application-layer messages into packets
  forward packets from one router to the next, across links on path from source to destination
  each packet transmitted at full link capacity
1-<number>
Notes: <number>

## Slide 10: Packet-switching: store-and-forward
Introduction
takes L/R seconds to transmit (push out) L-bit packet into link at R bps
store and forward: entire packet must arrive at router before it can be transmitted on next link
more on delay shortly …
1-<number>
source
R bps
destination
1
2
3
L bits
per packet
R bps
end-end delay = 2L/R (assuming zero propagation delay)
Notes: <number>

## Slide 11: Packet Switching: queueing delay, loss
Introduction
A
B
C
R = 100 Mb/s
R = 1.5 Mb/s
D
E
queue of packets
waiting for output link
1-<number>
queuing and loss:
If arrival rate (in bits) to link exceeds transmission rate of link for a period of time:
  packets will queue, wait to be transmitted on link
  packets can be dropped (lost) if memory (buffer) fills up
Notes: <number>

## Slide 12: Two key network-core functions
Network Layer
4-<number>
forwarding: move packets from router’s input to appropriate router output
routing: determines source-destination route taken by packets
  routing algorithms
routing algorithm
local forwarding table
header value
output link
0100
0101
0111
1001
3
2
2
1
1
2
3
0111
dest address in arriving
packet’s header

## Slide 13: Alternative core: circuit switching
Introduction
end-end resources allocated to, reserved for “call” between source & dest:
In diagram, each link has four circuits.
  call gets 2nd circuit in top link and 1st circuit in right link.
dedicated resources: no sharing
  circuit-like (guaranteed) performance
circuit segment idle if not used by call (no sharing)
Commonly used in traditional telephone networks
1-<number>
Notes: <number>

## Slide 14: Circuit switching: FDM versus TDM
Introduction
FDM
frequency
time
TDM
frequency
time
4 users
Example:
1-<number>
Notes: <number>
Two simple multiple access control techniques.
Each mobile’s share of the bandwidth is divided into portions for the uplink and the downlink. Also, possibly, out of band signaling.
As we will see, used in AMPS, GSM, IS-54/136

## Slide 15: Packet switching versus circuit switching
Introduction
example:
1 Mb/s link
each user:
  100 kb/s when “active”
  active 10% of time
circuit-switching:
  10 users
packet switching:
  with 35 users, probability > 10 active at same time is less than .0004 *
packet switching allows more users to use network!
N
users
1 Mbps link
Q: how did we get value 0.0004?
Q: what happens if > 35 users ?
…..
1-<number>
* Check out the online interactive exercises for more examples
Notes: <number>

## Slide 16
Introduction
great for bursty data
  resource sharing
  simpler, no call setup
excessive congestion possible: packet delay and loss
  protocols needed for reliable data transfer, congestion control
Q: How to provide circuit-like behavior?
  bandwidth guarantees needed for audio/video apps
  still an unsolved problem (chapter 7)
packet switching
Q: human analogies of reserved resources (circuit switching) versus on-demand allocation (packet-switching)?
Packet switching versus circuit switching
1-<number>
Notes: <number>

## Slide 17: Internet structure: network of networks
Question: given millions of access ISPs, how to connect them together?
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
…
…
…
…
…
…
Notes: <number>

## Slide 18: Internet structure: network of networks
Option: connect each access ISP to every other access ISP?
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
…
…
…
…
…
…
…
…
…
…
…
connecting each access ISP to each other directly doesn’t scale: O(N2) connections.
Notes: <number>

## Slide 19: Internet structure: network of networks
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
…
…
…
…
…
…
Option: connect each access ISP to a global transit ISP? Customer and provider ISPs have economic agreement.
global ISP
Notes: <number>

## Slide 20: Internet structure: network of networks
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
…
…
…
…
…
…
… and regional networks may arise to connect access nets to ISPS
ISP B
ISP A
ISP C
IXP
IXP
regional net
Notes: <number>

## Slide 21: Internet structure: network of networks
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
…
…
…
…
…
…
… and content provider networks (e.g., Google, Microsoft, Akamai ) may run their own network, to bring services, content close to end users
ISP B
ISP A
ISP B
IXP
IXP
regional net
Content provider network
Notes: <number>

## Slide 22: Internet structure: network of networks
Introduction
at center: small # of well-connected large networks
  “tier-1” commercial ISPs (e.g., Level 3, Sprint, AT&T, NTT), national & international coverage
  content provider network (e.g, Google): private network that connects it data centers to Internet, often bypassing tier-1, regional ISPs
1-<number>
access
ISP
access
ISP
access
ISP
access
ISP
access
ISP
access
ISP
access
ISP
access
ISP
Regional ISP
Regional ISP
IXP
IXP
Tier 1 ISP
Tier 1 ISP
Google
IXP
Notes: <number>

## Slide 23: Tier-1 ISP: e.g., Sprint
Introduction
…
to/from customers
peering
to/from backbone
…
…
…
…
POP: point-of-presence
1-<number>
Notes: <number>

## Slide 24: How do loss and delay occur?
Introduction
packets queue in router buffers
packet arrival rate to link (temporarily) exceeds output link capacity
packets queue, wait for turn
A
B
packet being transmitted (delay)
packets queueing (delay)
free (available) buffers: arriving packets
dropped (loss) if no free buffers
1-<number>
Notes: <number>

## Slide 25: Four sources of packet delay
Introduction
dproc: nodal processing
check bit errors
determine output link
typically < msec
A
B
propagation
transmission
nodal
processing
queueing
dqueue: queueing delay
time waiting at output link for transmission
depends on congestion level of router
dnodal = dproc + dqueue + dtrans + dprop
1-<number>
Notes: <number>

## Slide 26
Introduction
dtrans: transmission delay:
L: packet length (bits)
R: link bandwidth (bps)
dtrans = L/R
dprop: propagation delay:
d: length of physical link
s: propagation speed in medium (~2x108 m/sec)
dprop = d/s
dtrans and dprop
very different
Four sources of packet delay
propagation
nodal
processing
queueing
dnodal = dproc + dqueue + dtrans + dprop
1-<number>
A
B
transmission
* Check out the Java applet for an interactive animation on trans vs. prop delay
Notes: <number>

## Slide 27: Packet loss
Introduction
queue (buffer) preceding link in buffer has finite capacity
packet arriving to full queue dropped (lost)
lost packet may be retransmitted by previous node, by source end system, or not at all
A
B
packet being transmitted
packet arriving to
full buffer is lost
buffer
(waiting area)
1-<number>
* Check out the Java applet for an interactive animation on queuing and loss
Notes: <number>

## Slide 28: Throughput
Introduction
throughput: rate (bits/time unit) at which bits transferred between sender/receiver
  instantaneous: rate at given point in time
  average: rate over longer period of time
server, with
file of F bits
to send to client
link capacity
Rs bits/sec
link capacity
Rc bits/sec
server sends bits
(fluid) into pipe
pipe that can carry
fluid at rate
Rs bits/sec)
pipe that can carry
fluid at rate
Rc bits/sec)
1-<number>

## Slide 29: Internet protocol stack
Introduction
application: supporting network applications
  FTP, SMTP, HTTP
transport: process-process data transfer
  TCP, UDP
network: routing of datagrams from source to destination
  IP, routing protocols
link: data transfer between neighboring network elements
  Ethernet, 802.111 (WiFi), PPP
physical: bits “on the wire”
application
transport
network
link
physical
1-<number>
Notes: <number>

## Slide 30: Encapsulation
Introduction
source
application
transport
network
link
physical
Ht
Hn
M
segment
Ht
datagram
destination
application
transport
network
link
physical
Ht
Hn
Hl
M
Ht
Hn
M
Ht
M
M
network
link
physical
link
physical
Ht
Hn
Hl
M
Ht
Hn
M
Ht
Hn
M
Ht
Hn
Hl
M
router
switch
message
M
Ht
M
Hn
frame
1-<number>
Notes: <number>

## Slide 31: Network layer
Network Layer
4-<number>
transport segment from sending to receiving host
on sending side encapsulates segments into datagrams
on receiving side, delivers segments to transport layer
network layer protocols in every host, router
router examines header fields in all IP datagrams passing through it
application
transport
network
data link
physical
application
transport
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical

## Slide 32: Two key network-layer functions
Network Layer
4-<number>
forwarding: move packets from router’s input to appropriate router output
routing: determine route taken by packets from source to dest.
  routing algorithms
analogy:
routing: process of planning trip from source to dest
forwarding: process of getting through single interchange

## Slide 33
Network Layer
1
2
3
0111
value in arriving
packet’s header
routing algorithm
local forwarding table
header value
output link
0100
0101
0111
1001
3
2
2
1
Interplay between routing and forwarding
routing algorithm determines
end-end-path through network
forwarding table determines
local forwarding at this router

## Slide 34: Connection setup
Network Layer
4-<number>
3rd important function in some network architectures:
  ATM, frame relay, X.25
before datagrams flow, two end hosts and intervening routers establish virtual connection
  routers get involved
network vs transport layer connection service:
  network: between two hosts (may also involve intervening routers in case of VCs)
  transport: between two processes

## Slide 35: Network service model
Network Layer
4-<number>
Q: What service model for “channel” transporting datagrams from sender to receiver?
example services for individual datagrams:
guaranteed delivery
guaranteed delivery with less than 40 msec delay
example services for a flow of datagrams:
in-order datagram delivery
guaranteed minimum bandwidth to flow
restrictions on changes in inter-packet spacing

## Slide 36: Network layer service models:
Network Layer
4-<number>
Network
Architecture
Internet
ATM
ATM
ATM
ATM
Service
Model
best effort
CBR
VBR
ABR
UBR
Bandwidth
none
constant
rate
guaranteed
rate
guaranteed
minimum
none
Loss
no
yes
yes
no
no
Order
no
yes
yes
yes
yes
Timing
no
yes
yes
no
no
Congestion
feedback
no (inferred
via loss)
no
congestion
no
congestion
yes
no
Guarantees ?

## Slide 37: Next Lecture
Introduction
2-<number>
Midterm 1