## Slide 1: Lecture6 PPP Protocol

## Slide 2: Outline
WAN Data Link Layer protocols
Point-to-point serial communications
Transmission Synchronization
HDLC

## Slide 3: WANs
As we have learned, all WAN connections consist of three basic elements:
  The physical transmission media
  Electrical signaling specifications for generating, transmitting, and receiving signals through various transmission media
  Data-link–layer protocols.

## Slide 4: WAN Data Link Layer Protocols
In addition to Physical layer devices, WANs require Data Link layer protocols to provide communication between two devices across the communication line.
Because there are many different ways to connect devices, there are many different data link protocols.
Data link protocols may provide any of the following services:
  Framing
  Session setup and termination
  Error detection
  Addressing on a multipoint medium
Notes: Framing Data is broken up into frames that are transmitted as independent units. If errors are detected in a frame, it is only necessary to retransmit that frame.
Session setup and termination For reliable services, session control messages are used by end systems to exchange status information about the session.

## Slide 5: WAN Data Link Protocols
The Data Link protocols may span only the local loop, span across regions, or even go intercontinental.
This is unlike the physical layer transmission technologies that are only concerned with moving electrical signals from customer location to the central office for processing.

## Slide 6: WAN Connection Types
WAN Data Link
Protocolos

## Slide 7: WAN Data Link Protocols
Each WAN connection type uses a Data Link layer protocol to encapsulate a packet while it is crossing the WAN link.
The choice of encapsulation protocols depends on the WAN technology and the equipment.
In the previous slide, a figure displays the more common WAN protocols and where they are used.
The following are short descriptions of each type of WAN protocol:

## Slide 8: WAN Data Link Protocols
HDLC: The default encapsulation type on point-to-point connections, dedicated links, and circuit-switched connections.
PPP: Provides router-to-router and host-to-network connections over synchronous and asynchronous circuits.
Serial Line Internet Protocol (SLIP): A standard protocol for point-to-point serial connections using TCP/IP. SLIP has been largely displaced by PPP.

## Slide 9: WAN Data Link Protocols
X.25: An ITU-T standard that defines how connections between a DTE and DCE are established and maintained in he packet-switched networks.
Frame Relay: An industry standard, switched, data link layer protocol that handles multiple virtual circuits. Frame Relay is a next-generation protocol after X.25. Frame Relay eliminates some of the time-consuming processes (such as error correction and flow control) employed in X.25.

## Slide 10: WAN Data Link Protocols
ATM: The international standard for cell relay in which devices send multiple service types, such as voice, video, or data, in fixed-length (53-byte) cells. Fixed-length cells allow processing to occur in hardware; thereby, reducing transit delays. ATM takes advantage of high-speed transmission media such as E3, SONET, and T3.

## Slide 11: Serial Point to Point Link
One sender, one receiver, one link, serial transmission.
Notes: Figure 3-3 shows a simple representation of a serial communication across a WAN.
Data is encapsulated by the communications protocol used by the sending router.
The encapsulated frame is sent on a physical medium to the WAN. There are various
ways to traverse the WAN, but the receiving router uses the same communications
protocol to de-encapsulate the frame when it arrives.
This is in contrast to parallel communications in which bits can be transmitted simultaneously
over multiple wires. As shown in Figure 3-2, a parallel connection theoretically
transfers data eight times faster than a serial connection. Based on this theory, a
parallel connection sends a byte (eight bits) in the time that a serial connection sends
a single bit. However, parallel communications do have issues with crosstalk across wires, especially as the wire length increases. Clock skew is also an issue with parallel
Because of their bidirectional
ability, serial communications are considerably less expensive to implement. Serial communications
use fewer wires, cheaper cables, and fewer connector pins.
communications. Clock skew occurs when data across the various wires does not
arrive at the same time, creating synchronization issues. Finally, most parallel communications
support only one-direction, outbound-only communication from the
hard drive.

## Slide 12: Serial Link
WAN technologies are based on serial transmission at the physical layer.
There are many different serial communication standards, each one using a different signaling method.
There are three important serial communication standards affecting LAN-to-WAN connections:
V.35, RS-232, and HSSI
The standard usually defines signal levels, maximum bandwidth, connector pin-out, and electrical characteristics of the serial lines.

## Slide 13: Transmission Synchronization
Asynchronous Transmission:
    Transmitting & Receiving devices maintain their own internal clocks. They do not synchronize their clocks before communicating.
data is transmitted in well-defined frames.
The frame includes both information (e.g., data) and overhead (e.g. control bits).
Each frame begins with a start bit & ends with a stop bit.

## Slide 14: Transmission Synchronization
Synchronous Transmission:
Transmitting device provides clocking.
May use separate channel that is dedicated to the clock
The clock signal acts a control line that tells the receiver when to read from the data line.
What this means is that the transmitter and receiver must synchronize their access to the data line in order to successfully transmit data.

## Slide 15: Transmission Synchronization
Synchronous transmission advantages:
  1. Lower overhead and thus, greater throughput
Synchronous transmission disadvantages:
  1. Slightly more complex
  2. Hardware is more expensive…

## Slide 16: Transmission Synchronization
Asynchronous transmission advantages:
  1. Simple, doesn’t require synchronization of both communication sides
  2. Cheap, timing is not as critical as for synchronous transmission, therefore hardware can be made cheaper
Asynchronous transmission disadvantages:
  1. Large relative overhead, a high proportion of the transmitted bits are uniquely for control purposes and thus carry no useful information

## Slide 17: HDLC

## Slide 18: HDLC
High-level Data Link Control (HDLC) is one of the oldest data link layer protocols for the WAN developed by the ISO.
HDLC is a bit-oriented protocol for communication over point-to-point and multipoint links.
Although HDLC can be used for point-to-multipoint connections, the most common usage of HDLC is for point-to-point serial communications.
It supports full-duplex communication.

## Slide 19: HDLC
The protocol uses the services of a physical layer, and provides either a best effort or reliable communications path between the transmitter and receiver (i.e. with acknowledged data transfer).
No authentication can be used with HDLC.
Many protocol suites use an HDLC (or HDLC-based) link layer, including X.25, the IP point-to-point protocol (PPP) and SNA.

## Slide 20: HDLC Encapsulation
HDLC defines a Layer 2 framing structure that allows for flow control and error control through the use of acknowledgments (just on multipoint).
Each frame has the same format, whether it is a data frame or a control frame.

## Slide 21: HDLC Encapsulation
Flag :
  The frame always starts and ends with an 8-bit Flag field.
  The bit pattern is 01111110.
  The Flag field initiates and terminates error checking.
Transparency
  The flag sequence must never occur within the content of a frame.
  A technique known as 0-bit insertion (bit stuffing) is used to prevent random data synthesizing a flag.
  This technique make HDLC transparent, since any stream of bits may be present between the open and closing flag of a frame.
  The receiving system strips out the inserted bits.
When frames are transmitted consecutively, the end flag of the first frame is used as the start flag of the next frame.
Notes: The flag sequence must never occur within the content of a frame otherwise it could be confused with an intentionally sent flag.
Because there is a likelihood that this pattern occurs in the actual data, the sending HDLC system always inserts a 0 bit after every five consecutive 1s in the data field, so in practice the flag sequence can only occur at the frame ends.

## Slide 22: Bit stuffing
Bit stuffing is the process of adding one extra 0 whenever five consecutive 1s follow a 0 in the data, so that the receiver does not mistake the pattern 0111110 for a flag.

## Slide 23: HDLC Encapsulation
Address:
  The address field identifies the secondary station that transmitted or is to receive the frame.
  This field is not needed for point-to-point links, but is always included for the sake of uniformity.
Control Field:
  It defines the three types of frames I,U and S Frame for HDLC.
Frame Check Sequence (FCS)
  Is usually a cyclic redundancy check (CRC) calculation remainder.
  The CRC calculation is redone in the receiver. If the result differs from the value in the original frame, an error is assumed.

## Slide 24: HDLC Encapsulation
Information (I) frame:
  I-frames carry upper layer information and some control information.
Supervisory (S) frame:
  S-frames provide control information.
Unnumbered (U) frame:
  U-frames support control purposes and are not sequenced.
Notes:   Unnumbered frames, used in link setup and disconnection, and hence do not contain ACK.
  Information frames, which carry actual information. Such frames can piggyback ACK in case of ABM
  Supervisory frames, which are used for error and flow control purposes and hence contain send and receive sequence numbers
Information (I) frame: I-frames carry upper layer information and some control information. This frame sends and receives sequence numbers, and the poll final (P/F) bit performs flow and error control. The send sequence number refers to the number of the frame to be sent next. The receive sequence number provides the number of the frame to be received next. Both sender and receiver maintain send and receive sequence numbers. A primary station uses the P/F bit to tell the secondary whether it requires an immediate response. A secondary station uses the P/F bit to tell the primary whether the current frame is the last in its current response.
Supervisory (S) frame: S-frames provide control information. An S-frame can request and suspend transmission, report on status, and acknowledge receipt of I-frames. S-frames do not have an information field.
Unnumbered (U) frame: U-frames support control purposes and are not sequenced. Depending on the function of the U-frame, its Control field is 1 or 2 bytes. Some U-frames have an Information field.

## Slide 25: HDLC Encapsulation
HDLC was not intended to encapsulate multiple Network layer protocols across the same link.
The HDLC header carries no identification of the type of protocol being carried inside the HDLC encapsulation.
Because of this, each vendor that uses HDLC has their own way of identifying the Network layer protocol, which means that each vendor’s HDLC is proprietary for their equipment

## Slide 26: CHDLC
Cisco has developed an extension to the HDLC protocol (Cisco HLDC (CHDLC) )to solve the inability to provide multiprotocol support,.
CHDLC frames contain a field for identifying the network protocol being encapsulated.

## Slide 27: PPP
Point-to-Point Protocol (PPP) is the name of a single protocol, whereas the “PPP” can be used to refer to the entire suite of protocols that are related to PPP.
The PPP protocol was developed by IETF as a means of transmitting data for more than one network protocol over the same point-to-point serial link in a standard, vendor-independent way.
It can carry IP, Novell IPX, AppleTalk, and DECnet traffic.

## Slide 28: PPP
PPP also offers many features that HDLC does not including the following:
  Authentication through the Password Authentication Protocol (PAP) and the Challenge-Handshake Authentication Protocol (CHAP)
  Compression capabilities with Stacker or Predictor
  PPP Multilink, the ability to bundle physical channels into a single logical channel.
  Support for Error detection and error recovery features
  Encapsulation for multiple routed protocols, including IP, Novell IPX, and AppleTalk

## Slide 29: PPP
PPP is a layered protocol, starting with a Link Control Protocol (LCP) for link establishment, configuration and testing. Once the LCP is initialized, one or many of several Network Control Protocols (NCPs) can be used to transport traffic for a particular protocol suite.
Notes: In terms of the architecture and frame formats, PPP can be seen as three different sub-protocols, for framing and lower level capabilities; it is basically HDLC. If you see the frame formats, it is very similar to HDLC. One sub-layer above is LCP, which provides all of the additional functionality in terms of authentication, multilink, and the general establishment configuration and testing of the data link connection. A third protocol is NCP; it is used for establishing and configuring different network layer protocols. It is basically the interface toward the upper layers.

## Slide 30: PPP and PHY Layer
PPP operates at the Data Link layer.
At the physical layer, PPP can be used across synchronous (e.g., ISDN, leased lines) and asynchronous (e.g., modem dialup) data links.

## Slide 31: HOW PPP Work
The mechanism that PPP uses to carry network traffic is to open a link with a short exchange of packets.
Once the link is open, network traffic is carried with very little overhead. Frames are sent as unnumbered information frames, meaning that no data link acknowledgement is required and no retransmissions are carried out.
So once the link is established, PPP acts as a straight data pipe for protocols.

## Slide 32: PPP Components

## Slide 33: PPP Components
  Three main components:
  HDLC:
    HDLC protocol for encapsulating datagrams over point-to-point links.
  LCP:
    To establish, configure, maintain and terminate the data link connection.
  NCPs:
    Family of NCPs for establishing and configuring different network layer protocols.
    Allows simultaneous use of multiple Network layer protocols
Notes: Translation: IP and IPX and others, simultaneously, over a single dialup or higher speed WAN link.

## Slide 34: Encapsulation
PPP defines a Protocol Type field.
The protocol type field identifies the type of packet inside the frame,. The following shows a PPP frame.

## Slide 35: PPP Data Frame
Flag: delimiter (framing)
Address: does nothing (only one option)
Control: does nothing; in the future possible multiple control fields
Protocol: upper layer protocol to which frame delivered (eg, PPP-LCP, IP, IPCP, etc)
Data: upper layer data being carried
FCS: cyclic redundancy check for error detection

## Slide 36: Byte Stuffing
One of PPP design requirements is data transparency.
Transparency means carrying any bit pattern in the data field
  data field must be allowed to include flag pattern <01111110>
  Q: is received <01111110> data or flag?
Sender: adds (“stuffs”) extra < 01111110> byte after each < 01111110> data byte
Receiver:
  two 01111110 bytes in a row: discard first byte, continue data reception
  single 01111110: flag byte

## Slide 37: Byte Stuffing
flag byte
pattern
in data
to send
flag byte pattern plus
stuffed byte in transmitted data

## Slide 38: LCP
Link establish: The process of bringing up the PPP link before any other protocols can begin transmission.
Link configuration: The process of negotiating and setting up the parameters of a link.
Link maintenance: The process of managing an opened link.
Link termination: The process of closing an existing link when it is no longer needed (or when the underlying physical layer connection closes).

## Slide 39: LCP
In link configuration, LCP frames are exchanged that enable the two physically-connected devices to negotiate the parameters (configuration options) under which the link will operate.
Device1 sends a configure request frame, containing configuration options.
Device2 responds with a frame confirming that the options are okay, suggesting different options or rejecting the options.
Configure-nak
Configure-reject
Notes: This exchange takes place in both directions and when a station has sent and received an acknowledge packet the link layer is declared open.
The other device (let's call it sayâ€¦ device B J) receives the Configure-Request and processes it. It then has three choices of how to respond:
If every option in it is acceptable in every way, device B sends back a Configure-Ack (â€œacknowledgeâ€). The negotiation is complete.
If all the options that device A sent are valid ones that device B recognizes and is capable of negotiating, but it doesn't accept the values device A sent, then device B returns a Configure-Nak (â€œnegative acknowledgeâ€) frame. This message includes a copy of each configuration option that B found unacceptable.
If any of the options that A sent were either unrecognized by B, or represent ways of using the link that B considers not only unacceptable but not even subject to negotiation, it returns a Configure-Reject containing each of the objectionable options.

## Slide 40: LCP Configuration Options
LCP offers PPP different options, including the following:
  Maximum-Receive-Unit (MRU): Lets a device specify the maximum size datagram it wants the link to be able to carry.
  Authentication-Protocol: the device can indicate the type of authentication protocol it wishes to use (if any).
  Compression: Allows the device to specify that it wants to use a compression. This is used to increase the throughput of PPP connections
  Quality-Protocol: If the device wants to enable quality monitoring on the link, what protocol to use
  Other options: Error detection, Magic Number, Multilink

## Slide 41: LCP
During link maintenance, LCP can use messages to provide feedback and test the link
Echo-Request, Echo-Reply, and Discard-Request - These frames can be used for testing the link.
Code-Reject and Protocol-Reject - These frame types provide feedback when one device receives an invalid frame due to either an unrecognized LCP code (LCP frame type) or a bad protocol identifier.

## Slide 42: LCP
The LCP closes the link by exchanging Terminate packets.
A termination request indicates that the device sending it needs to close the link.
When the link is closing, PPP informs the network layer protocols so that they may take appropriate action.
Notes: PPP can terminate the link at any time. This might happen because of the loss of the carrier, authentication failure, link quality failure, the expiration of an idle-period timer, or the administrative closing of the link.
The device initiating the shutdown (which may not be the one that initiated the link in the first place) sends a Terminate-Request message. The other device replies back with a Terminate-Ack.

## Slide 43: NCP
PPP use the NCP to permit multiple network layer protocols to operate on the same communications link.

## Slide 44: NCP
For every network layer protocol used, PPP uses a separate NCP. For example, IPv4 uses the IP Control Protocol (IPCP) and IPv6 uses IPv6 Control Protocol (IPv6CP).