## Slide 1: NET301
Lecture6

## Slide 2: Data impairments
Thermal Noise شوشرة حرارية
  is the electronic noise generated by the thermal agitation of the charge carriers (usually the electrons) inside an electrical conductor , which happens regardless of any applied voltage.
  Unwanted currents or voltages in an electronic component resulting from the agitation of electrons by heat

## Slide 3: Data impairments
Impulse Noise الشوشرة النبضية :
  usually caused by electromagnetic interference, scratches on the recording disks, and ill synchronization in digital recording and communication.
  consists of relatively short duration “on/off” noise pulses, caused by a variety of sources. Causes lost or damaged bits.

## Slide 4: Data impairments
Crosstalk التداخل المتعارض
  is any phenomenon by which a signal transmitted on one circuit or channel of a transmission system creates an undesired effect in another circuit or channel.

## Slide 5: Data impairments
Interference التداخل الكهربائي
  is anything which alters, modifies, or disrupts a signal as it travels along a channel between a source and a receiver.
  Ex: radio and mobile and T.V ..

## Slide 6: Data impairments
Attenuation الوهن - التدهور
  is the gradual loss in intensity of any kind of signals through a medium.
  It affects the propagation of waves and signals in electrical circuits, in optical fibers, and in air (radio waves).
  Attenuation depends on the signal frequency, distance of the transmission and the transmission medium.
  When signal travels through a medium, it loses some of its energy so that it can overcome resistance of the medium.

## Slide 7: Data impairments
Time Jitterالتزحزح الوقتي
  is the undesired deviation from true periodicity of an assumed periodic signal in electronics and telecommunications, often in relation to a reference clock source.
  is the deviation in or displacement of some aspect of the pulses in a high-frequency digital signal.

## Slide 8: Data impairments
Inersymbol Interference ISI تداخل الرموز
  Sometimes when the high frequency digital signal transmitted over a medium that has a limited frequency bandwidth, not all the frequency can transmit over this medium, which cause changes and damaged and interfere in the symbols of the digital signal.

## Slide 9: Data impairments units
Data impairments differ depends on the transmission medium, distance and frequency and other factors.
Amplifiers are used to amplified the signal.
Data impairments is measured with decibel (dB) .
Decibel: A measure of the relative strength of two signal points.
Decibel can be positive + if signal is amplified, or negative if signal is attenuated.

## Slide 10: decibel
dB = 10 Log10 ( P2/P1)
  P2: the power of a signal at the end point (Watt)
  P1: the power of a signal at the start point (Watt).
Example1:
Imagine a signal travels through a transmission medium and its power is reduced to half. Calculate the decibel.
  Reduced to half means P2 = ½ P1
  dB = 10 Log10 (P2/P1) =
  10 Log 10 (0.5 p1/p1)
  dB = 10 Log 10 (0.5) =
  10 (-0.3) = - 3 dB

## Slide 11: Channel capacity & thermal Noise
Shannon capacity: the theoretical highest data rate for the channel.
Thermal noise affects signals and may cause damages or changes in the signals.
Shannon capacity:
C = W Log2 ( 1+ S/N)
  C: channel capacity, maximum bit rate (bit/sec)
  W: frequency bandwidth (Hz)
  S: Signal power (Watt)
  N: Noise power (watt)

## Slide 12: Channel capacity & thermal Noise
Example:
What is the channel capacity for a phone line if the line frequency bandwidth is 3000 Hz. Given that signal to noise ratio is 3162
Solution:
C = W * Log2 ( 1 + S/N)
C = 3000 * Log2 ( 1+ 3162)
C = 3000 * Log2 (3163)
C = 3000 * 11.62
C = 34860 bps (bit/sec)